## Slide 1: Chapter 3 DIVERTOR AND SOL PHYSICS, PLASMA-WALL INTERACTIONS
DTT-RP 4TH in-person meeting
Frascati, 6-8 May 2024
P. Innocente, E. Tsitrone, M. Wischmeier
DTT Consortium (DTT S.C.a r.l. Via E. Fermi 45 I-00044 Frascati (Roma) Italy)

## Slide 2: Rationale of Ch.3
Plasma wall interaction as important as plasma exhaust  chapter title has been changed
Considering the limit on pages the chapter was focused on what it is useful to do on PEX&PWI  No modeling results included
High relevance of SN as for comparison and extension of present knowledge with focus on ELM free scenarios
Alternative divertor configuration (ADC) focused on XD and SN-NT as from present EF priorities
High relevance of ramp-up/ramp-down (with the limiter phase) for W devices
Detailed description of all PWI expects to controls and to study
Importance of wall cleaning/conditioning

## Slide 3: INDEX
2.1 Introduction
3.2 DTT plasma facing components and diagnostics relevant for divertor and SOL physics
3.3 Divertor and edge physics studies
  3.3.1 Divertor scenario development
  3.3.2 Alternative divertor configurations
3.4 Far SOL physics and first wall loads
  3.4.1 Optimizing plasma ramp-up and ramp-down
  3.4.2 Assessing far SOL transport and first wall fluxes
  3.4.3 Impact of off-normal events on the first wall

## Slide 4: INDEX
  3.4 Plasma Wall Interactions in a full tungsten environment
    3.5.1 Wall conditioning
    3.5.2 W erosion and material migration
    3.5.3 Fuel retention and recovery; dust production
    3.5.4 W morphology changes under plasma loading
    3.5.5 Wall monitoring system
    3.5.6 Future PFC and edge diagnostics enhancements: using DTT divertor test modules
  3.4 Plasma Wall Interactions in a full tungsten environment
  3.6 Headlines of the research programme for Divertor, SOL and PWI
  3.7 References
  Total pages : 16

## Slide 5: Changes
No changes on respect December 2023

## Slide 6: Headlines
Headlines number | Headlines contents | Priority (+, ++, +++) | ITER | DEMO
Construction Phase 2022-2029 |  |  |  | 
C.3.1 | Definition of first wall shape and parameters | +++ |  | 
C.3.2 | Definition of markers types and position in FW | ++ |  | 
C.3.3 | Definition of optimal diagnostics requirements for PEX/PWI analysis | ++ | * | *
Phase 1 2029-2034 |  |  |  | 
1.3.1 | Developments of plasma start-up and ramp-up scenarios with boronization | +++ | * | 
1.3.2 | Developments of plasma start-up and ramp-up scenarios without boronization | + | * | *
1.3.3 | Development of strike point sweeping method | +++ | * | *
1.3.4 | Development of SN detached configuration in L-mode | + | * | 
1.3.5 | Development of SN detached configuration in H-mode | +++ | * | *
1.3.6 | Development of XD divertor configuration | +++ |  | *
1.3.7 | Development of NT divertor configuration | +++ |  | *
1.3.8 | Optimization of boronization | ++ | * | 
1.3.9 | Quantification of D retention in clean W | +++ | * | *
1.3.10 | Quantification of the impact of boronization on D retention | ++ | * | 

## Slide 7: Headlines
Headlines number | Headlines contents | Priority (+, ++, +++) | ITER | DEMO
Phase 2 2034-2038 |  |  |  | 
2.3.1 | Evaluation of lq at high toroidal field and comparison with scalings | +++ | * | *
2.3.2 | Evaluation of transport parameters in limiter phase and in the far-SOL | +++ | * | *
2.3.3 | Optimization of detachment by seeding | +++ | * | *
2.3.4 | Development of methods to control detachment | +++ | * | *
2.3.5 | Development of ELM control methods by gas-puffing, pellet RMP | ++ | + | 
2.3.6 | Development and control of XPR low-ELMs scenarios | ++ | + | *
2.3.7 | Optimization of XD configuration with seeding | +++ |  | *
2.3.8 | Test new FW and divertor materials | ++ |  | *
Phase 3 2038-… |  |  |  | 
3.3.1 | Optimization of detachment in SN with different seeding | +++ | * | *
3.3.2 | Optimization of XD configuration | +++ |  | *
3.3.3 | Optimization of NT configuration | +++ |  | *
3.3.4 | Comparison of SN to XD and NT configurations | ++ |  | *
3.3.5 | Estimation of wall erosion and W migration and validation of codes | +++ | * | *
3.3.6 | Evaluation of D retention after erosion/redeposition and W surface modification | +++ | * | *
3.3.7 | Development of methods for D removal | ++ | * | *

## Slide 8: Possible extensions of the chapter
We can include modeling results on PEX and PWI but where to focus?
Possible PEX studies
  Comparison between SN and ADC
  Study of XPR scenario
  SN-PT in H-mode in different plasma scenario (Bt, Ip, Psol)
  L-mode studies
  Limiter/ramp-up/ramp-down, L-H transition
  3D studies (gas-puffing location, interaction with ICRH antenna, RMP)
  Start from day0 as suggested by DTT management?
Possible PWI studies
  Tungsten erosion/deposition/migration
  GDC modeling
  Modeling on dust
  Integration with diagnostics

## Slide 9: General points for discussion
Snowflake configuration: is it an interesting configuration to study? Maybe we could find problems with present divertor/FW/diagnostics.
Phase 1, heating phase C (16 MW ECRH, 4 MW ICRH, 6T, 4 MA): in this phase H-mode is difficult to achieve. How useful is this phase? Should we try to study the phase to asses the minimum nsep to reduce L-H threshold?
Phase 2, heating phase D (16 MW ECRH, 4 MW ICRH, 5-10 MW NBI, 6T, 5.5 MA): Should we try to study the phase to asses the minimum nsep to reduce L-H threshold?
Phase 3, heating phase E (32 MW ECRH, 8 MW ICRH, 10 MW NBI, 6T, 5.5 MA). Since now only n/nG=0.5 what about to analyse higher/lower density operation scenario?
Phase 3, heating phase E (32 MW ECRH, 8 MW ICRH, 10 MW NBI, 3T, 2.5 MA). What about low toroidal field/current at high heating?
Is there any possibility to consider experiments with tritium?