## Slide 1: DTT diagnostic design status
1st ENEA-KFE remote meeting, 28 November 2024
DTT Consortium, Rome, Italy1, ENEA- «Plasma studies and DTT machine» Division, NUC-PLAS2
DTT-THM-DIA Team1
Presented by Marco Ciotti2

## Slide 2: DTT diagnostic strategy
Equipment for Machine/Divertor Protection and Plasma Control have the priority in the diagnostic procurement plan
Final selection and development of the other diagnostics (physics studies) will follow closely the Research Plan (PHASE 1 and PHASE 2 equipment)
AIM  diagnostics to cover the DTT scientific mission
About #80 diagnostic techniques are planned in full power operation
About #160 systems were allocated
30% (about 25 systems) phase1 equipment to guarantee machine protection and plasma control
DTT
DTT
End 2030
Marco Ciotti- KFE-ENEA Meeting- 28-11-2024

## Slide 3: DTT diagnostic environment
Diagnostic integration activities and interface issues are demanding 
integration effort must include both PHASE 1 and PHASE 2 diagnostic packages (according to the scientific programs)
DTT is:
  a compact, superconducting machine;
  with a substantial amount of external heating power (up to 45MW);
  equipped with actively cooled components;
  intensive remote handling is required.
  Design of IN-Vessel diagnostic lay-out and cables routing
  are particularly challenging 
  Compatibility with very narrow space (compact) between First Wall or Divertor Cassette and Vacuum Vessel
  Withstand: Thermal load during plasma operations and high temperatures during baking operations, low cryogenic temperatures (superconducting)
  High level of neutron flux and fluence,
  EC stray radiation
Marco Ciotti- KFE-ENEA Meeting- 28-11-2024

## Slide 4: DTT diagnostic equipment strategy
DTT – THM – DIA - WBS IV |  | Project Leader | 2023 DTT Shareholder Services & WPDIV-IDTT | 
DTI | Tomography and SXR imaging | G.M.Apruzzese | ENEA, INFN, RFX, CNR, UNIMIB, UNITOV | 
DSP | Active and Passive Spectroscopy | F.Bombarda | ENEA, RFX, CNR, POLITO, UNIMIB | 
DIP | Interferometry and Polarimetry | D.Fiorucci | ENEA, RFX, UNITOV | 
DTS | Thomson Scattering systems | L.Giudicotti | RFX, ENEA | 
DMA | Magnetic Sensors | G.Artaserse M.Baruzzo | ENEA, CETMA, CREATE, RFX, UNICA | IPP-Prague-Czech Republic (IPP-CR)
DWI | Embedded, Infra-Red and Visible cameras and other PWI Diagnostics | M.Iafrati | ENEA, RFX, CNR | CEA-France (CEA)
DEE | Electron Cyclotron Emission Diagnostics | C.Sozzi a.i. | CNR, RFX | 
DRE | Reflectometric Measurements | G.De Masi | RFX, INFN | IST-Lisbon-Portugal
DGN | Neutrons and Gammas diagnostics | D.Marocco | ENEA, CNR, UNIMIB | 
DRA | Run Aways Diagnostics | B.Esposito | ENEA, UNITOV, CREATE | VR-KTH Stockholm-Sweden (VR)
DPF | Fast Particles Diagnostics | M.Nocente | UNIMIB, CNR | Universitad de Sevilla-Spain (CIEMAT)

## Slide 5: Equatorial Ports Heating+RH
1
3
5
8
9
10
17
2
18
16
14
Ion Cyclotron
Electron Cyclotron
Neutral Beam Inj.
Remote Handling Sectors
13
7
4
12
11
15
Marco Ciotti- KFE-ENEA Meeting- 28-11-2024

## Slide 6: DTT diagnostic equipment: eq. ports
3
8
9
17
10
5
1
15
Charge Exchange (CXRS) | Sector 10
Interferometer Tangential | 
Reflectometry Plasma Position | 
Diagnostic Neutral Beam Inj. | 
Reflectometry Density Profile Reconstruction | 
Ion Cyclotron Heating
Electron Cyclotron Heating
Neutral Beam Injection
Remote Handling Sectors
Sector 8 | Thomson Scattering LIDAR
 | SXR imaging
 | SXR Crystal Spectrometer
Bolometer Tomography | Sector 15
SXR Tomography | 
Interferometer Tangential | 
IR/VIS Cameras | 
Sector 9 | Interferometer Tangential
 | IR/VIS Cameras
 | REIS Spectrometer
 | NGA & OGA
 | Cherenkov Probe
 | Charge Exchange (CXRS)
 | Electron Cyclotron Emission Turbulence Coherent
Sector 5 | Electron Cyclotron Emission Imaging
 | Phase Contrast Imaging
 | Visible Fast Camera
 | ECE Eterodyne Radiometer
Sect. 3 | Interferometer Vertical
 | IR/VIS Cameras
 | Visible: Zeff-Bremmsthralung profile / Spectrrometer Survey&Divertor
Sector 1
Radial Neutron Gamma Camera
VUV Spectrometer | Sector 17
XUV Spectrometer | 
Time-Of-Flight Neutron Spectrometer | 
Thomson Scattering Divertor and Pedestal | 
Phase Contrast Imaging | 
VUV Spectrometer Edge | 
Phase 1 Diagnostics

## Slide 7
1
13
2
3
4
5
8
7
9
10
11
12
14
15
16
17
18
Sect. 3 | P1
 | P3
P4
Sector 10
P1 | Sect. 11
P4 | Sect. 13
P3 | Sect. 15
DTT: EC Stray Sniffer Probe PHASE 1
P1
P3
Sector 9
Sect. 6 | P1
 | P4
6
Sector 1
P4
Sect. 4 | P4
P1 | Sect. 14
Sector 18
P1
P1 | Sect. 16
P4 | 
Withstand Stray EC Radiation is a critical aspect of the Diagnostic Design
Sniffer Probe allocation  monitor and interlocking functionality
Marco Ciotti- KFE-ENEA Meeting- 28-11-2024

## Slide 8
1
13
2
3
4
5
8
7
9
10
11
12
14
15
16
17
18
Sector 1 | 
Bolometer Cameras (Tor. Asymm.) | P1
Radial Neutron Gamma Camera | P3
Laser Induced Breakdown Spectroscopy | 
Sect. 3 | P2, P3, P4 | Interferometer Vertical
 | P3 | Visible Multi Spectral Imaging System
Sect. 4 | P2 | IR Camera
 | P4 | Thermal He Beam
Sector 7 | P1 | Laser Induced Breakdown Spectroscopy (Divertor)
 | P2 | VUV Spectrometer Imaging Divertor
Charge Exchange (CXRS) | P1 | Sector 10
Bolometer Cameras (Tor. Asymm.) | P1 | 
Reflectometry Plasma Position PPR | P1, P3 | 
Reflectometry Turbulence TR | P2, P4 | 
Diagnostic Neutral Beam MSE Optics | P2 | 
Diagnostic Neutral Beam Inj. | P3 | 
Reflectometry Dens. Prof. Reconstr. DPR | P3 | 
Electron Cyclotron Emission Radiometer in Line | P2 | 11
Fast Ion Loss Detector FILD | P4 | 
IR Camera | P2 | 13
Collective Thomson Scattering. | P4 | 16
XUV Spectrometer Divertor | P2 | Sector 17
IR Camera | P2 | 
Time-Of-Flight Neutron Spectrometer | P3 | 
Thomson Scattering Divertor and Pedestal | P2, P3 | 
Phase Contrast Imaging | P3 | 
VUV Spectrometer Edge | P4 | 
Sector 5 | P1 | Bolometer Cameras (Tor. Asymm.)
 | P3 | Electron Cyclotron Emission Oblique
 | P3 | Phase Contrast Imaging
 | P3 | Event Detec. Visible Fast Camera
 | P4 | Sample Introduction System
Collective Thomson Scattering | P2 | 15
Sector 2 | P2 | Electron Cyclotron Emission Radiometer in Line
 | P2 | Laser Blow Off
 | P4 | Langmuir Probes Reciprocating
Gas Puffing Imaging | P4 | 14
Imaging Neutral Particle Analyzer | P4 | Sector 9
Fast-Ion Deuterium alpha (FIDA) | P2 | 
IR Camera | P2 | 
Cherenkov Probe | P3 | 
Charge Exchange (CXRS) | P3 | 
Electron Cyclotron Emission Turbulence Coherent | P3 | 
DTT PHASE 2 Diagnostic Equipment Allocation
IR Camera | P1 | 12
Charge Exchange (CXRS) | P2
Beam Emission Spectroscopy | P2
Interferometer Divertor | P4
Sector 8 | 
Marco Ciotti- KFE-ENEA Meeting- 28-11-2024

## Slide 9: First Wall Inner and Outer: instrumentation and cables routing
Part. Rogowski & Current Shunt (Active) – FW locking brackets
Langmuir Probes & Thermocouples - (HFS FW Limiter Module)
Microbalance Redeposition Probe (Active) – HFS FW Standard Module
Long Term Samples (LTS) (Passive) - Limiter Module
Marco Ciotti- KFE-ENEA Meeting- 28-11-2024

## Slide 10: Vacuum Vessel sensors: internal and external
Diamagnetic Loops | Optic Fiber Current | Rogoski Coils | BiaXial Pick up Coils | Monaxial Pick up Coils | FluX Loops | Saddle Loops | Hall Probes
Magnetic Sensor – VV INternal
Number of magnetic sensors  352
Numbers of cables  695
Marco Ciotti- KFE-ENEA Meeting- 28-11-2024
Magnetic Sensor – VV EXternal
Number of magnetic sensors  444
Numbers of cables  681
 |  |  |  | High Frequency Pick up Coils
BiaXial Pick up Coils | FluX Loops | Monaxial Pick up Coils | Diamagnetic Loops | 
Notes: FIBERGLASS INSULATED CABLE

## Slide 11: Vacuum Vessel sensors: internal and external 2
Internal & External Pick-Up Coils
External Saddle Loops
Internal & External Flux Loops
Critical aspects:
  tight space available
  in-vessel obstacles (other subsystems services)
Critical  In-Vessel signal cable choice:
Neutron irradiation and heating can generate spurious output (additional tiny voltage) corrupting the final signal
Suitable EC stray protection
Marco Ciotti- KFE-ENEA Meeting- 28-11-2024

## Slide 12: Magnetic Sensors
Sensor types chosen to cover DTT Operation and Experimental program needs |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Loops |  |  |  |  | Pick-up Coils |  |  |  |  |  |  | Current Rogowski Coils |  |  | Special Sensors |  |  |  | 
Flux |  | Saddle | Diamagnetic |  | Tangential Bi-Axial |  | Toroidal mono-Axial |  |  | HF Bi-Axial | Bi-Axial | Plasma | Halo |  | Hall | Hybrid | Fiber Opt. FOCS | Shunt | 
Shape Equilibrium loop voltage Eddy current |  | Error field Equilibrium Plasma shape current & centroid position | Plasma magnetic energy |  | Plasma current & centroid position & shape and equilibrium Vertical speed |  | Plasma magnetic energy |  |  | Vertical speed Plasma shape & equilibrium MHD fluctuation | Plasma shape & equilibrium | Plasma current Eddy currents | Halo & eddy currents |  | Bi-axial magnetic field |  | Plasma current | Halo currents, ELMS | 
VV-INT | VV-EXT | VV-EXT | VV-INT | VV-EXT | VV-INT | VV-EXT | VV-EXT | VV-INT | DIV | VV-INT | DIV | VV-EXT | FW | DIV | VV-EXT | VV-INT | VV-EXT | DIV | FW
9 | 11 | 156 | 3 | 3 | 204 | 240 | 12 | 12 | 8 | 124 | 52 | 3 | 60 | 32 | 16 | TBD | 3 | 16 | TBD
964 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
  Positioning of INternal and EXternal Vacuum Vessel magnetic sensors have been optimized over the main DTT scenarios XD, SN-NT, SN  reconstruction capabilities of plasma current, plasma centroid, plasma shape
  Shape reconstruction, in presence of measurement errors  estimated errors cm especially for the advanced divertor configurations
  Number and position of proposed divertor cassette sensors optimized to improve reconstruction capabilities of equilibrium reconstruction codes, x-point and strike point positions

## Slide 13: High Field Side First Wall: standard module customized to host diagnostics components
10
3
Marco Ciotti- KFE-ENEA Meeting- 28-11-2024

## Slide 14
Zeff LOS profile Dumps (minimize reflection)
HFS-FW Standard Module Customization preliminary design  under assessment
Critical  compatibility with First Wall HFS Cooling System requirements
Critical  withstand plasma thermal load, neutron effects, EC stray radiation
Single Wave Guide pair  3 LOS & pairs of antennas
Local modifications to create windows for the PPR LOS
Vertical Interferometer/Polarimeter Corner Cube back reflectors
Thermal bridge replacing a cooling tube of the standard module
Plasma Position Reflectometer (PPR)
Sector 10
Vertical Interferometer/Polarimeter and Zeff profile
Sector 3

## Slide 15: Divertor Test module diagnostic instrumentation
Partial Rogowski coils around divertor cassette structure (poloidal current measurement)
Measurements  in contact points between cassette and divertor rail
Magnetic sensors
Embedded: Langmuir Probes and Thermocouples
FOS: Fiber Optics Sensors Array
Bi-axial Pick-Up Coil
Mono-axial Pick-Up Coil
Hybrid Hall probe
Sensor's topology optimized for reconstruction of the X-point and strike points positions
Optical Fibers installation scheme under assessment  in a groove along the side
surface of the mono-block (below the top surface exposed to the plasma)
Marco Ciotti- KFE-ENEA Meeting- 28-11-2024
Highlighted regions potentially useful for the embedded sensors integration  specific integration schemes under assessment

## Slide 16: Divertor Test module diagnostic instrumentation and cables routing
 | Sector number | Magnetic sensors |  |  |  |  |  |  |  |  |  | Embedded |  |  |  | Fiber Optics Sensors (FOS) | 
Sensors/Array per sector | 1 | Bi-axial Pick up Coil | 13 | Mono-Axial pickup Coil | 2 | Hall Probe Hybrid | 1 | Halo current (Rogowski) | 8 | Current Shunt | 4 | Langmuir Probes | 600 | Thermocouples (Science) | 150 | FOS Array | 5
 | 5 |  | 13 |  | 2 |  | 1 |  | 8 |  | 4 |  | 150 |  | 150 |  | 5
 | 10 |  | 13 |  | 2 |  | 1 |  | 8 |  | 4 |  | 150 |  | 150 |  | 5
 | 15 |  | 13 |  | 2 |  | 1 |  | 8 |  | 4 |  | 150 |  | 150 |  | 0
Cables | Type | MIC |  |  |  |  |  |  |  |  |  | MIC/fiber glass insulated conductors |  |  |  | Optic fiber | 
 | Diameter | Φ 4mm |  |  |  |  |  |  |  |  |  | Φ 4/1,5mm |  |  |  | Φ 8mm | 
 | Cable per sensor | Bi-axial Pick up Coil  2x, Others  1x |  |  |  |  |  |  |  |  |  | 1x |  |  |  | 1x | 
 | Total Number | 41 => sector 1, 5, 10 and 15 |  |  |  |  |  |  |  |  |  | 750 => Sector 1 300 => Sector 5, 10 and 15 |  |  |  | 5 => sector 1, 5, 10 | 
Confirmed | 
To be confirmed | 

## Slide 17: Divertor Visible Imaging
The design aims to maximum coverage of the divertor region
Two telescopes to optimize Divertor view:
  UPPER  an almost perpendicular (darker blue)
  LOWER more tangential (lighter blue)
Overview of the Divertor Visible Imaging (Zeff poloidal LoS profile in green color)
Marco Ciotti- KFE-ENEA Meeting- 28-11-2024
Collected light can be shared among different spectrometers and interferential filter devices:
UPPER VIEW: The “vertical integrated image” is directed to a high resolution (HR) CT spectrometer, while the “horizontal integrated image” is further split between HR and several low resolution (LR) spectrometers
LOWER VIEW: The image collected with the more tangential observation of the DIVERTOR and it is split between a Multispectral Imaging system (VFID) MANTIS-type (plasma detachment through tomographic reconstruction with high spatial resolution (<5mm)) and a HR CT Spectrometer.

## Slide 18: VIS/IR tangential views  Tangential Viewing System (TVS)
Dichroic
Folding Mirrors
IR channel
Cryostat Flange
Optical Head
3m
VIS channel
(to be completed)
TVS Optical Design
IR cameras | 
Wide Angle | 50-100 Hz
VIS cameras | 
Wide Angle | 50-500 Hz
Fast | 10-50 Khz
TVS spatial coverage
Outer First Wall
Divertor
Inner First Wall
Inner First Wall
79m² of the chamber seen  73.7% of the chamber inner area
Overlapping surfaces 22.1m² (i.e. covered by 2 cameras)
3 endoscope allocated; 120° toroidally spaced
Equatorial left and right view
TVS  poor/limited coverage of the divertor area
Envisaged a periscope IR camera allocated on port5
Notes: New detector dimensions considered: 1280x1024, 15µm pixel

## Slide 19
PHASE 1 Diagnostic (and part of PHASE 2 Diagnostic impacting on assembly)
 Conceptual Design completed in March 2024
PHASE 2 diagnostic preliminary conceptual design in progress with particular attention to integration and interface issues
Status of the design activities
On May the 7th the DTT Diagnostics Design Review Committee (DTT-DIA-DRC) has been nominated
The DTT Research Plan (DTT-RP) has been completed and released on June 2024 (available online on the DTT Project website https://www.dtt-project.it/index.php/about/dtt-research-plan.html)
Marco Ciotti- KFE-ENEA Meeting- 28-11-2024
The scope of the DTT-DIA-DRC is to provide advices, regarding DTT diagnostic area (DTT-DIA), to the DTT management on the following aspects:
Consistency, completeness, and maturity of the design;
Incongruity of the costs, both hardware and human, exposed by the project leaders and adequacy of construction schedule;
Possible simplifications and/or reduction of scope to reduce costs;
Priority with respect to PHASE 1 and PHASE 2 of DTT operational program.
The panel report has been released on July 2024 where the envisaged DTT diagnostic equipment has been overall confirmed and the strategy of PHASE 1 and PHASE2 DTT diagnostic equipment has been refined following the DTT Research Plan

## Slide 20: Concluding Remarks
Diagnostics planning and realization in a Tokamak is a complex issue, in DTT even more;
DTT consortium partners have a long tradition in diagnostic development;
Activities are ongoing in agreement with the research plan and DTT scientific targets;
Phase 1 diagnostics are progressing according to the project schedule;
Collaborations with Enea or DTT consortium are wellcome
Marco Ciotti- KFE-ENEA Meeting- 28-11-2024

## Slide 21
DTT Diagnostic Equipment Design progress status
KFE-ENEA meeting