## Slide 1
Laser Interaction with Foam Targets for the Generation of Laser-Driven Sources of Particles and Radiation for Nuclear Physics with Lasers
8th International Conference on Frontiers in Diagnostics Technologies (ICFDT8) Frascati, Italy | October 2026
Sebastian Busch (Goethe University Frankfurt / GSI Darmstadt)
Prof. Dr. Olga Rosmej, Parysatis Tavana and collaborations
Foam Structure
CHO-Foam

## Slide 2
PHELIX Laser System Parameters and DLA Setup for Laser-Plasma Coupling
Foam ionization by suitable ns-pulse
 depending on foam density and length
Laser Parameters (2022) | 
Focus size | ~ (13 x 21) µm
Intensity ns-pulse | ~ 1013 W/cm2
Delay | ~ 5 ns
Intensity ps-pulse | ~ 1019 W/cm2
Wavelength | 1052 nm
Energy (FWHM) | 14–19 J
Longer acceleration path in foam-plasma
 Higher electron energies and conversion efficiencies
1/16
19.10.2026 Sebastian Busch
Electron spectra along the laser axis
Foam Structure
Direct Laser Acceleration (DLA)

## Slide 3
Irradiation of target with PHELIX-Laser
 MeV bremsstrahlung Photons via Direct Laser Acceleration (DLA):
High energy bremsstrahlung generation via deceleration of e- in a high-Z converter
Emitted radiation directed onto different materials  nuclear reactions, esp. (γ, xn)-reactions
Photonuclear cross sections (GDR) peak above ~7.5 MeV
Principle: Analyze produced isotopes with High-Purity Germanium (HPGe) detectors
Giant Dipole Resonance (GDR): Collective oscillation of protons against neutrons within a nucleus leading to particle emission
2/16
19.10.2026 Sebastian Busch
Theoretical Background
Generation of High Energetic Photon Using Foam Targets
Notes: PHELIX = Petawatt High Energy Laser for Heavy Ion Experiments

## Slide 4
Theoretical Background Principle of Nuclear Diagnostics in GDR Bremsstrahlung
3/16
19.10.2026 Sebastian Busch
Select suitable materials with:
  High cross section in the energy range of interest
  Produced Isotopes must be detectable  suitable half-life & γ-energy
Used materials: Au, Ta, In, Cu, Nb, Cr
Laser intensity : =
Average binding energy per nucleon: or
 7 orders of magnitude higher
It is still not possible to induce nuclear reactions directly through high intensity infrared laser light
 We use a promising indirect approach with low density foam targets
Notes: , I = 1/2c*epsilon_0*E^2
𝐸=~(10^7 V)/(10^(−12) cm)=10^19 V/cm, I = 1/2c*epsilon_0*E^2

## Slide 5
Select suitable materials with:
  High cross section in the energy range of interest
  Produced Isotopes must be detectable  suitable half-life & γ-energy
Used materials: Au, Ta, In, Cu, Nb, Cr
Post-shot procedure:
Record spectra using Ge-Detectors
Number of photon-induced reactions:
Determine isotope yields for bremsstrahlung spectrum reconstruction
: Number of irradiated nuclei
: Threshold energy of the reaction
: Reaction cross section
: Energy distribution of incoming particles
Theoretical Background Principle of Nuclear Diagnostics
4/16
19.10.2026 Sebastian Busch

## Slide 6
Experiments at PHELIX (GSI, Darmstadt)
  Application of directed DLA electron beams for the production of Bremsstrahlung > 10 MeV
  Characterization of Bremsstrahlung spectra using photonuclear reactions
Targets:
Foams of various thicknesses & densities  300, 500, and 1000 µm & 2, 4, and 8 mg/cm3
Au- (10 µm), Cu- (1 µm), Al-foils (50 µm)
Foam + gold converter, tungsten, indium
Foam + Converter
Foam Structure
CHO-Foam (8 mg/cm3)
Laser Parameters PHELIX (2022) | 
Focal spot size | Best focus: (13 x 15) µm2
Wavelength | 1052 nm
Intensity ns-pulse | ~ 1013–1014 W/cm2
Energy ns-pulse | 0.3–3 % of main-pulse
Delay | ~ 5 ns
Intensity ps-pulse | ~ 1019 W/cm2
Pulse duration | ~ 650 fs
Energy ps-pulse | ~ 70 J
Foam ionization by a tailored ns-pulse
5/16
19.10.2026 Sebastian Busch

## Slide 7
TLD Spectrometer
Focus-Diagnostic
0.99T-MS +170°
100 mm
100 mm
ps- & ns-pulse
0.99T-MS 0°, -5°
0.99T-MS -80°
Nuclear probes
7.5 mm
7.5 mm
15 mm
15 mm
Nuclear Probes on Thin Copper Plates (4 cm to TCC)
P-21-00005 – Experimental Setup
Target Set-Up
1 mm In probe
2 mm W, 1 mm Au converter
1 mm Foam, in copper washer
Foam target, CHO, 8 mg/cc
0.2 mm Al-tape
Al holder
Detectors used: - High-purity germanium detectors (HPGe) - Model: GEM-S5020P4-B
Background reduction through: - Nitrogen cooling - Lead shielding
19.10.2026 Sebastian Busch
6/16

## Slide 8
Nuclear Diagnostics
Autoradiography Using Thin Copper Foils
10.8 MeV
9.74 min
-energy: 1.172 MeV (0.34%)
Imaging of decay via image plate scanning provides spatial activity maps.
Enables correction of sample position and calculation of BS divergence
19.10.2026 Sebastian Busch
7/16
Autoradiography of copper foils irradiated by bremsstrahlung photons visualises the spatial distribution of radiation source (E > 10 MeV)
Notes: (10-min exposure)

## Slide 9
Nuclear Diagnostics
Autoradiography Using Thin Copper Foils
Autoradiography of copper foils irradiated by bremsstrahlung photons visualises the spatial distribution of radiation source (E > 10 MeV)
IP Scan for Autoradiography
= 20°
FWHM area
Probe position
Foam 1 mm, 4 mg/cm3, 2 mm W + ns-pulse
Divergences for Various Foam Target Setups
Horizontal Position [mm]
Vertical Position [mm]
19.10.2026 Sebastian Busch
7/16

## Slide 10
Nuclear Diagnostics
Bremsstrahlung Reconstruction for Shot on Foam Target
Probe Spectrum for Foam-Target measured in HPGe-Detector
Reconstructed BS-Spectrum
19.10.2026 Sebastian Busch
8/16

## Slide 11
Sh 30: 1 mm Foam 4 mg/cc + 3 mm converter and ns-pulse Sh 41: 2 mm W and ns-pulse
 Record conversion efficiency for Laser (FWHM) to BS (> 7 MeV) of up to 1.8%!
Nuclear Diagnostics
Comparison of Results for Foam Target with Converter and only Converter
19.10.2026 Sebastian Busch
9/16

## Slide 12
Results for Nuclear Diagnostics and Thermoluminescent Dosimeter (TLD) Spectrometer in Good Agreement
8-Channel in Vacuum TLD Spectrometer at PHELIX
Results for Shot 30: 1 mm Foam 4 mg/cc + 3 mm Converter and ns-Pulse
Signal on Imaging Plates
TLD Spectrometer Results
TLD vs. ND Bremsstrahlung Comparison
TLD simulations by:
Alessandro Tentori, GSI
19.10.2026 Sebastian Busch
10/16

## Slide 13
Laser peak intensity >1019 W/cm2
  Transfer of previous approaches to Advanced Radiographic Capability (ARC) conditions
 For the development of ultra-bright MeV photon sources for ICF experiments at ARC/NIF
https://lasers.llnl.gov/news/nif-focus-inside-arc-laser
PHELIX Best Focus
Experiments at PHELIX: P-23-00193 (2024)
19.10.2026 Sebastian Busch
11/16
Mission of ARC: MeV Bremsstrahlung source to radiograph the moment of DT-implosion
ARC Beamlet Pair

## Slide 14
 Only 5–10 % energy with 1018 W/cm2 peak intensity
  Transfer of previous approaches to Advanced Radiographic Capability (ARC) conditions
   Near relativistic intensity (<1018 W/cm2) ,  Stretched PHELIX pulse & increased focal spot
 For the development of ultra-bright MeV photon sources for ICF experiments at ARC/NIF
https://lasers.llnl.gov/news/nif-focus-inside-arc-laser
Experiments at PHELIX: P-23-00193 (2024)
19.10.2026 Sebastian Busch
11/16
ARC Focus
ARC Beamlet Pair

## Slide 15
Teff = 5–9 MeV
foam+foil
Teff = 0.1 MeV (foil)
  Transfer of previous approaches to ARC conditions
  Investigation of neutron generation & measurement
Oct./Nov. 2024
Laser parameters:
Nd:glass l = 1.053 mm, s-polarized
Main pulse:
E = ~30 J
t = ~ 0.65 ps up to 2.5 ps
ns-pulse:
E = 1–9 J
t = 3 ns, delay = 2–7 ns
ns-pulse energy & delay tailored to foam target
P-23-00193: Laser and Target Parameters
19.10.2026 Sebastian Busch
12/16
PHELIX I ~ 1018 W/cm2
Very large focal spot (>40 µm) at near-relativistic intensity
Electron Spectra (1018 W/cm2)

## Slide 16
Target: CHO-foam (2 mg/cc) + 1 mm Pb
0.65 ps
1.3 ps
2.5 ps pulse duration
Shot | Target | Pulse duration / ps | Divergence / sr | NPh (> 7 MeV) | Eavg / MeV
46 | Foam (2 mg/cc, 800 µm) + 1 mm Pb | 0.65 | 0.21 | 2.2E+10 | 11.2
47 |  | 1.3 | 0.22 | 7.1E+09 | 10.9
48 |  | 0.65 | 0.19 | 2.0E+10 | 11.1
51 |  | 2.5 | 0.21 | 1.2E+10 | 9.3
Bremsstrahlung spectra with photon energies up to 25–30 MeV and an average energy of 9–11 MeV at near-relativistic intensity and below.
Same target (foam + Pb), different pulse durations (0.65–2.5 ps) and laser intensities (2· 1017 – 1018 W/cm2)
Experiments at PHELIX (P-23-00193) Generation of MeV-BS with Sub-Relativistic Laser Intensities (ARC-Like)
19.10.2026 Sebastian Busch
13/16
Similar MeV photon conversion efficiency at sub-relativistic intensities

## Slide 17
Shot | Target (all with ns-pulse) | Laser parameters
36 | Foam (8 mg/cc, 300 µm) + 1 mm Ta | 0.65 ps / 1018 Wcm-2
38 | 1 mm Ta | 
42 | Foam (2 mg/cc, 800 µm) + 110 µm Pb | 
44 | Foam (2 mg/cc, 800 µm) + 10 µm Au | 
46 | Foam (2 mg/cc, 800 µm) + 1 mm Pb | 
47 |  | 1.3 ps / 5 ⋅ 1017 Wcm-2
48 |  | 0.65 ps
51 |  | 2.5 ps / 2.5 ⋅1017 Wcm-2
52 | Foam (2 mg/cc, 800 µm) + 2 mm Pb + 1 mm Au | 0.65 ps
TLD-Results in Forward Direction (+3.5°)
P-23-00193 - Results TLD-Analysis: Similar Doses Across Different Pulse Durations and Target Setups
19.10.2026 Sebastian Busch
14/16
Converter + ns-pulse
Foam + converter + ns-pulse
1018 W/cm2, 0.65 ps / > 2 ⋅ 1017 W/cm2, 2.5 ps
1018 W/cm2
TLD-BS-Results in Forward Direction (+3.5°)
Varying pulse durations (0.65–2.5 ps) and laser intensities (2· 1017 – 1018 W/cm2) were used

## Slide 18
Stronlgy Enhanced Photon Fluence Using Foams compared to Compound Parabolic Concentrator (CPC)
19.10.2026 Sebastian Busch
15/16
Example of CPC source
Au activations at 1 m per 1 g
DLA S02
Target: CHO 2 mg/cc, 1 mm + 2 mm Au
ARC: 1.8 ps, 0.27 kJ
Target: CPC + 2 mm Au
ARC: 4 beams, each
10 ps; 4x 600 J= 2.4 kJ
ARC axis,
20 cm from TCC
S. Kerr, D. Rusby, NIF
Same activation of 196Au with 10×lower laser energy → 10×higher photon fluence
CPC: FWHM 87°
BS in GDR (> 8 MeV)
DLA: FWHM 40°
BS in GDR (> 8 MeV)
0.75 T spectrometer
Array of Au-discs for
activation by gamma-rays
Focusing in CPC-Cone

## Slide 19
Nuclear diagnostics is an essential tool for characterizing (> 7 MeV) bremsstrahlung spectra
Up to 2% conversion efficiency from laser to bremsstrahlung (> 7 MeV) – new record!
Superiority of foam & converter confirmed compared to converter-only setups with pre-plasma:
- Yields and energies strongly exceed ponderomotive scaling even at subrelativistic intensities (< 1018 W/cm2)
Shot to shot stability using various kind of foam, converter and laser parameter combinations
Experiment at ARC/NIF 02/26 for the first time with foam targets demonstrated 10x higher photon fluence per Joule on target laser energy in GDR than commonly used target approach
Outlook
Further experiments at ARC/NIF and PETAL/LMJ (2028)
Summary and Outlook
19.10.2026 Sebastian Busch
16/16

## Slide 20: Thank you for your attention and to all participants and collaborators!
ROSMEJ, Olga (GSI)
MARTYNENKO, Artem (GSI)
KOZLOVA, Ekaterina (GSI)
KÜHL, Thomas (GSI) SPIELMANN, Uwe (GSI)
TENTORI, Alessandro (GSI)
SCHULTHEIS, Simon (TU Darmstadt)
ZARROUK, Karim (TU Darmstadt)
BOLLER, Pascal (TU Darmstadt)
ROSMEJ, Olga (Goethe Uni Frankfurt, HFHF)
BUSCH, Sebastian (Goethe Uni Frankfurt, HFHF)
GYRDYMOV, Mikhail (Goethe Uni Frankfurt)
BELOIU, Philipp (Goethe Uni Frankfurt)
JACOBY, Joachim (Goethe Uni Frankfurt)
TAVANA, Parysatis (Goethe Uni Frankfurt/ Uni Jena)
BLEOTU, Petrisor-Gabriel (ELI-NP)
MAGUREANU, Alexandru (ELI-NP)
NAZAROV, Wigen (UOD)
ALONZO, Massimo (ENEA Frascati)
SCISCIO, Massimiliano (ENEA Frascati)
CIPRIANI, Mattia (ENEA Frascati)
CONSOLI, Fabrizio (ENEA Frascati)
VERONA, Claudio (University of Rome)
CHENG, RUI (Institute Of Modern Physics, China)
YANG, Jie (Institute of Modern Physics)
CIKHARDT, Jakub (Czech Technical University)
SCHNEIDER, Dieter (LLNL)
ANDREEV, Nikolai (JIHT)
Notes: Olga zu GSI?

## Slide 21: Backup

## Slide 22
Cross Sections for (γ,xn)-Reactions
Reactions in Indium
Reactions in Copper Plates
Imaging Plate (IP) Scan with Probe
Neutrons
MeV-BS
Autoradiography
Theoretical Background Cross Sections of Nuclear Reactions
19.10.2026 Sebastian Busch

## Slide 23
Detectors used: High-purity germanium detectors (HPGe) Model: GEM-S5020P4-B
Background reduction through: - Nitrogen cooling - Lead shielding
P-23-00193 – Experimental Setup
Experimental Setup and Placement of ND
Target
Bonner Sphere
+170°
0.99T-MS
3.5°
TLD-Spectrometer
+20°
-10°
0.99T-MS
20°
TLD-Spectrometer
Nuclear Diagnostic
0°, ~17 mm
Laser
Gamma & Neutron Measurements
Gamma Measurements
Foam Target + Converter Box
Foam Target + Diagnostic Stack
19.10.2026 Sebastian Busch

## Slide 24
P-23-00193 - Results Autoradiography: Divergence
Sh 36
Shot | Target (Foams preionized) | Pulse duration / fs | / °
36 | Foam (8 mg/cc, 300 µm) + 1 mm Ta | 650 | 20.7
40 | Foam (8 mg/cc, 300 µm) + 1 mm Ta + 1 mm Au |  | 16.6
46 | Foam (2 mg/cc, 800 µm) + 1 mm Pb |  | 14.5
47 |  | 1300 | 14.8
48 |  | 650 | 14.0
51 |  | 2500 | 14.4
52 | Foam (2 mg/cc, 800 µm) + 2 mm Pb + 1 mm Au | 650 | 23.0
64 | Foam (5 mg/cc, 500µm) + 1 mm Cu + 3 mm Ta |  | 24.8
Shot | Target (Foams preionized) | Pulse duration / fs | 
36 | Foam (8 mg/cc, 300 µm) + 1 mm Ta | 650 | 20.7
40 | Foam (8 mg/cc, 300 µm) + 1 mm Ta + 1 mm Au |  | 16.6
46 | Foam (2 mg/cc, 800 µm) + 1 mm Pb |  | 14.5
47 |  | 1300 | 14.8
48 |  | 650 | 14.0
51 |  | 2500 | 14.4
52 | Foam (2 mg/cc, 800 µm) + 2 mm Pb + 1 mm Au | 650 | 23.0
64 | Foam (5 mg/cc, 500µm) + 1 mm Cu + 3 mm Ta |  | 24.8
Half angle
Shot
Divergence
19.10.2026 Sebastian Busch

## Slide 25
Shot | Target (all with ns-pulse) | Pulse Duration / fs
36 | Foam (8 mg/cc, 300 µm) + 1 mm Ta | 650
42 | Foam (2 mg/cc, 800 µm) + 110 µm Pb | 
44 | Foam (2 mg/cc, 800 µm) + 10 µm Au | 
46 | Foam (2 mg, 800 µm) + 1 mm Pb | 
47 |  | 1300
48 |  | 650
51 |  | 2500
52 | Foam (2 mg, 800 µm) + 2 mm Pb + 1 mm Au | 650
6-channel in Vacuum TLD Spectrometer
TLD-Results in Forward Direction (+3.5°)
P-23-00193 - Results TLD-Analysis
19.10.2026 Sebastian Busch

## Slide 26
CHO-Foam
Target Holder
γ-Probe Stack
In Al, on Cu-plate
60 mm
60 mm
Cu-Plate for Autoradiograpy
Nuclear Probes (Gamma Measurement)
15 mm
Cr
Cu
Nb
In
Ta
Au
15 mm
Gamma & Neutron Measurements
Foam Target + Converter Box
Gamma Measurements
Foam Target + Diagnostic Stack
P-23-00193 – Experimental Setup Nuclear Diagnostics
19.10.2026 Sebastian Busch

## Slide 27
Gamma Measurements
Foam Target + Diagnostic Stack
Foam Target + Converter Box
Gamma & Neutron Measurements
15 mm
Cr
Cu
Nb
In
Ta
Au
15 mm
Nuclear Probes for Neutron Measurement)
Neutron Box Setup (Expl.)
8x In (25x25x1 mm3)
1x Au (15x15x1 mm3)
25 mm
25 mm
γ-Probe Stack
Laser dir.
Nuclear Probes (Gamma Measurement)
P-23-00193 – Experimental Setup Nuclear Diagnostics
19.10.2026 Sebastian Busch

## Slide 28
Cross Sections: (γ, xn)-Reactions
Ge-Detector Spectrum (Up to 550 keV)
Energy [keV]
  Characterization of bremsstrahlung spectra using photonuclear reactions
Target | Pulse Duration / fs
CHO (8 mg/cc, 300 µm) + 1 mm Ta | 650
Energy [MeV]
Cross Section [mb]
19.10.2026 Sebastian Busch

## Slide 29
P-23-00193 - Results Bremsstrahlung Reconstruction using Nuclear Diagnostics
Ge-Detector Spectrum (Up to 550 keV)
Reconstructed Bremsstrahlung Spectrum
Shot 36 – Gamma Probes
Energy [keV]
19.10.2026 Sebastian Busch

## Slide 30
Bremsstrahlung divergence:
Neutron box setup | 
Shot | Sequence
64 | Small Cu – large Ta – small Ta – gamma probes – 1st–20th small Cu – large Cu
19.10.2026 Sebastian Busch
P-23-00193 - Results Cu-Analysis for Neutron Box in Shot 64
15 mm
Cr
Cu
Nb
In
Ta
Au
15 mm

## Slide 31
Neutron Box Setup | 
Shot | Order
64 | Small Cu – big Ta – sm. Ta – Gamma probes – 1.-20. sm. Cu – big Cu
Materials inside converter box (from laser direction, values in mm):
- Cu (15x15x1) - Ta (33x35x2) - Ta (15x15x1) - Au (15x15x1), Ta (15x15x1), 2xIn (15x15x0.25 jeweils), Nb (15x15x0.5), Cu (15x15x1), Cr (15x15x1) - 20xCu (15x15x1 each) - Cu (30x30x2)
Gamma probes
Converter
Autoradiography
Autoradiography
Converter Box Setup
Target
10 mm
3 mm
In + Au
Converter + Probes
Shot 64
P-23-00193 – Experimental Setup Neutron Conver Box
19.10.2026 Sebastian Busch

## Slide 32
P-23-00193 - Results Cu-Analysis for Neutron Box in Shot 64
Neutron box setup | 
Shot | Sequence
64 | Small Cu – large Ta – small Ta – gamma probes – 1st–20th small Cu – large Cu
19.10.2026 Sebastian Busch

## Slide 33
Neutron Source | Neutrons
0. Cu (1 mm) | 4.6E+05
Ta-Converter (2 mm) | 3.6E+07
Cu-Stack (20 mm) | 3.1E+07
Au-Probe (1 mm) | 2.0E+07
Ta-Probe (1 mm) | 1.2E+07
Sum | >8.9E+07
Number
P-23-00193 - Results Cu-Analysis for Neutron Box in Shot 64
19.10.2026 Sebastian Busch
Neutron box setup | 
Shot | Sequence
64 | Small Cu – large Ta – small Ta – gamma probes – 1st–20th small Cu – large Cu
Notes: Rechts ggf etwas schöner

## Slide 34
Shot | 36 | 38 | 42 | 44 | 46 | 47 | 48 | 51 | 52
(TLD) / ° | 26.0 | 56.3 | 10.9 | 13.2 | 13.4 | 17.2 | 15.3 | 19.0 | 23.9
(Cu-Scans) / ° | 20.7 | X | X | X | 14.5 | 14.8 | 14.0 | 14.4 | 23.0
Shot | 36 | 38 | 42 | 44 | 46 | 47 | 48 | 51 | 52
 | 26.0 | 56.3 | 10.9 | 13.2 | 13.4 | 17.2 | 15.3 | 19.0 | 23.9
 | 20.7 | X | X | X | 14.5 | 14.8 | 14.0 | 14.4 | 23.0
Shot | Target (all with ns-pulse) | Pulse Duration / fs
36 | Foam (8 mg/cc, 300 µm) + 1 mm Ta | 650
38 | 1 mm Ta | 
42 | Foam (2 mg/cc, 800 µm) + 110 µm Pb | 
44 | Foam (2 mg/cc, 800 µm) + 10 µm Au | 
46 | Foam (2 mg/cc, 800 µm) + 1 mm Pb | 
47 |  | 1300
48 |  | 650
51 |  | 2500
52 | Foam (2 mg/cc, 800 µm) + 2 mm Pb + 1 mm Au | 650
TLD-Results in Forward Direction (+3.5°)
TLD-Results in 20° Direction
P-23-00193 - Results TLD-Analysis
19.10.2026 Sebastian Busch

## Slide 35
Experiment | Shot | Number of Activated Nuclei (196Au) | Activations At 1m Per 1g |  |  | 
 |  |  | Total | Per J (Total) | Per J (>1018 W/cm2) | Per J (>1017 W/cm2)
ARC-like (2024) | 46 | 1.37E+06 | 2.01E+03 | 6.71E+01 | 2.89E+03 | 1.53E+02
 | 47 | 1.37E+06 | 2.02E+03 | 6.72E+01 | - | 1.39E+02
 | 48 | 3.06E+06 | 4.50E+03 | 1.50E+02 | 6.47E+03 | 3.41E+02
 | 51 | 1.90E+06 | 2.80E+03 | 9.32E+01 | - | 6.12E+02
NIF/ARC 2026 (avg.1-14 probes) | 1 | 2.64E+06 | 2.97E+04 | 1.07E+02 | 2.47E+03 | 2.06E+02
 | 2 | 3.16E+06 | 3.50E+04 | 1.27E+02 | 1.40E+03 | 2.52E+02
Shot | Pulse duration / fs | Laser Energy Above: |  | 
 |  | 1018 W/cm2 | 1017 W/cm2 | Total
46, 48 | 650 | 0.70 J | 13.19 J | ~30 J
47 | 1300 | 0 | 14.51 J | 
51 | 2500 | 0 | 4.57 J | 
Same order of magnitude for number of activated 196Au nuclei per laser energy for PHELIX- & ARC/NIF-experiment.
PHELIX:
NIF/ARC:

## Slide 36
Mix- & 22Na-source:
Reference Date: 01.06.2006
Nuclide | Half-life | Activity / kBq
241Am | 432.6 (6) a | 0.9501
109Cd | 461.9 (4) d | 4.54
139Ce | 137.641 (20) d | 0.4866
57Co | 271.81 (4) d | 0.3953
60Co | 5.2711 (8) a | 0.7703
137Cs | 30.05 (8) a | 0.63
133Ba | 10.539 (6) a | 0.4322
85Sr | 64.850 (7) d | 0.7524
88Y | 106.63 (5) d | 1.688
51Cr | 27.704 (4) d | 10.66
Reference Date: 13.06.2023
Nuclide | Half-life | Activity / kBq
22Na | 949.69 d | 3.7⋅104
Detector Preparation: Calibration
/ kBq
Reference Date: 01.06.2006
Nuclide | Half-Life | Activity / kBq
241Am | 432.6 (6) a | 0.9501
109Cd | 461.9 (4) d | 4.54
139Ce | 137.641 (20) d | 0.4866
57Co | 271.81 (4) d | 0.3953
60Co | 5.2711 (8) a | 0.7703
137Cs | 30.05 (8) a | 0.63
133Ba | 10.539 (6) a | 0.4322
85Sr | 64.850 (7) d | 0.7524
88Y | 106.63 (5) d | 1.688
51Cr | 27.704 (4) d | 10.66
Reference Date: 13.06.2023
Nuclide | Half-Life | Activity / kBq
22Na | 949.69 d | 3.7⋅104
Energy Calibration Calibration Sources Detector Efficiency
19.10.2026 Sebastian Busch

## Slide 37
Up to 600 keV
Above 600 keV
HPGe-detector background had to be considered:
Long measurements without sample were performed
Substract background for true number of counts
Avoid/Substract overlapping lines
Detector Preparation: Background
Background measurement
19.10.2026 Sebastian Busch