## Slide 1
From Discharge Physics to Reactive Chemistry: an Integrated Diagnostic Path to Plasma Agriculture
ISTP CNR – Bari, Italy
DOMENICO ACETO
M. Ambrico, G. Dilecce, P. F. Ambrico
ICFDT – Frontiers in Diagnostic Technologies
19/10/2026 - Frascati
A multi-diagnostic framework for atmospheric-pressure DBD reactors

## Slide 2: Plasma-Activated Water
MOTIVATION
Aceto D. et al., Front. Phys. 12, 2024 | https://doi.org/10.3389/fphy.2024.1399910
Plasma Activated Water: indirect treatment
RONS produced in the plasma to substrates.
Fertigation
Decontamination
Rotondo, P.R., Aceto, D. et al., Sci Rep 15, 5536 (2025) | https://doi.org/10.1038/s41598-025-88369-7
NO3-
NO2-
H2O2

## Slide 3: Plasma-Activated Fog
MOTIVATION
PAW shortcomings in decontamination
Chemical stability during storage
Washing wet-sensitive produce may damage them
Treating large volumes of water makes the process difficult to scale up
→
Plasma-Activated Fog (PAF)
Same RONS chemistry carried on an aerosol → very large gas–liquid interface
Delivered immediately without wetting and with no thermal or mechanical stress → suits delicate produce
scales more naturally toward industrial post-harvest
Objective
Thorough physico-chemical characterisation of the process for its full optimisation.

## Slide 4: PAF reactor design
EXPERIMENTAL
Reactor
Coaxial DBD + medical glass nebulizer, double-distilled water
Power supply
AC, 19.5 kV peak voltage
Burst mode
15 cycles @ 25 kHz · 500 Hz repetition · 30% duty cycle
Feed gas
10 sLm ambient air → fog saturates the treatment chamber
Design choice: the discharge zone sits upstream of the nebulization chamber → stable discharge, humidity-robust electrical characteristics, low experiment-to-experiment variance.
Aceto, D. et al. Chem. Biol. Technol. Agric. 12, 151 (2025) | https://doi.org/10.1186/s40538-025-00865-0

## Slide 5: Aerosol characteristics
DIAGNOSTICS · PHYSICAL CHARACTERIZATION
< 5 µm
aerosol droplet diameter
After gas expansion and nebulization the fog reaches the substrate at ~17 °C → products are not thermally stressed.

## Slide 6: Electrical characteristics of the discharge
DIAGNOSTICS · PHYSICAL CHARACTERIZATION
38 mJ
dissipated per voltage burst
Almost ideal shape of the Lissajous figure indicates a regular, reproducible discharge
Notes: Energy balance: 38 mJ per burst at 500 Hz = 19 W; into 10 slm of air this is an adiabatic rise of 88 K, i.e. 388 K, matching the 380 K SPS rotational temperature - almost all the dissipated power ends up as gas enthalpy. (Assumes 500 Hz burst repetition - confirm.)

## Slide 7: Optical Emission Spectroscopy
DIAGNOSTICS · PHYSICAL CHARACTERIZATION
E/N from line ratios
FNS 391.4 / SPS 337.1 nm intensity ratio: an E/N proxy in air.
Gas temperature
SPS(0,0) rotational structure: streamer gas temperature ≈ 107 °C.
Notes: In air the N2+ FNS(0,0) 391.4 nm over N2 SPS(0,0) 337.1 nm ratio is the standard E/N proxy: the two upper states have very different thresholds (18.7 vs 11.0 eV), so their ratio is steeply field-dependent. The conversion to E/N needs a collisional-radiative model (quenching, cascade) - that is exactly why we add EFISH two slides later. The SPS(0,0) rotational envelope gives ~380 K, consistent with the energy balance on the electrical slide.

## Slide 8: Emission spectra across feed-gas mixtures
FNS/SPS falls
0.23 → 0.19 → 0.13 with argon; Ar* → N₂(C) transfer also lowers it.
N₂ vibration drops
SPS (1,4)/(0,3): 1.01 → 0.95 → 0.84, a proxy of weaker N₂(v).
Same gas temperature
N₂(0,0) rotational envelope identical in the three air–argon mixtures.
Closed reactor, burst-averaged spectra, each panel scaled to the named band.
DIAGNOSTICS · PHYSICAL CHARACTERIZATION
Notes: Closed reactor, burst-averaged. Two cautions for this audience. (1) The FNS/SPS drop with argon is NOT automatically a lower E/N: Ar metastables transfer energy to N2(C) and boost SPS, which lowers the ratio at constant field. OES alone cannot separate the two - this is the question EFISH answers. (2) The SPS Delta-v ratio tracks the C-state vibrational distribution, a proxy of ground-state N2(v), relevant because O + N2(v) -> NO + N is the low-temperature Zel'dovich channel. Rotational temperature is unchanged, so the trends are not thermal.

## Slide 9: RONS transport in the afterglow
Transport + conversion
NO rises along the afterglow. x₀ lies in the recirculation just after the discharge. Downstream stations span 2-3 ms after the discharge zone.
ICCD LIF in the open tube, along the axis downstream of the discharge; inset: CFD gas-density map.
DIAGNOSTICS · LIF
Notes: These are ICCD-LIF values in the OPEN tube, on the axis downstream of the discharge zone (x0 ~1 cm after the sheath). The flow model (next slide, backup) puts x0 exactly at the reattachment of the recirculation bubble behind the sheath, so only the two downstream points can be read as an afterglow time: 130 -> 200 ppm over 2-3 ms. CAUTION: these are two orders of magnitude above the PMT-LIF values at the nozzle exit (slide after next). Be ready to explain the different configuration and probe point, or do not quote both absolute scales.

## Slide 10: NO and OH fluorescence in the effluent
NO even in argon
NO γ v′=0 clean in air, 80/20 and dry argon: ambient air is entrained.
OH marks the plasma
Strong in the discharge; marginal downstream, except in dry argon.
Yield, not density
Quenching by N₂, O₂ and H₂O is far stronger than by argon.
Background-subtracted LIF downstream of the open reactor
DIAGNOSTICS · LIF
Notes: Downstream of the nozzle. NO gamma v'=0 progression is clean in air, 80/20 and even dry argon: ambient air is entrained and the plasma still makes NO. OH is strong in the discharge (see backup OH-LIF slide) and marginal downstream, which is the "short-lived marker of the active region" point of the abstract. Caveat: LIF = density x fluorescence yield; quenching by N2/O2/H2O is much stronger than by Ar, so argon signals are favoured.

## Slide 11: Absolute NO at the nozzle exit
LIF at 226.16 nm, closed configuration, discharge-off background subtracted.
DIAGNOSTICS · LIF
Laser path
Sampling zone
Collection with optical fiber to monochromator
Notes: PMT LIF at 226.16 nm, closed reactor, at the nozzle exit. Calibration with the certified 116 ppm NO/N2 mixture in all four carriers: one slope (4.6e-10 V s/ppm) - the transition is saturated, so quenching differences cancel. The delay scan is flat because the gas needs ~10 ms from the discharge to the nozzle, five burst periods at 500 Hz (confirm the burst rate). Argon gives 0.28 ppm vs 0.06-0.08 ppm with air in the feed. These values are far below the open-tube ICCD scale: different configuration and probe point; jet dilution at the probe is below 1.4x, so it does not explain the gap.

## Slide 12: Long-lived RONS in the effluent
Ambient vs humid feed: adding water vapour to the plasma feed enhances HNO₃ and other oxygenated nitrogen species relevant to PAF chemistry.
FT-IR of effluent gases: N₂O, NO₂, HNO₃, N₂O₅, O₃, CO₂
DIAGNOSTICS · FTIR

## Slide 13: Condensed PAF composition
Time-dependent chemistry
NO₃⁻ becomes the dominant species: ~40 → 445 mg L⁻¹ (1 → 10 min).
H₂O₂ rises to 3.5 mg L⁻¹ by 10 min; NO₂⁻ reaches 1.5 mg L⁻¹ then plateaus.
pH drops from 6 to 2.5, acidification tracks nitric-acid uptake.
Condensation promotes gas-to-liquid uptake, favouring nitrate accumulation.
H₂O₂, NO₂⁻, NO₃⁻ and acidic pH drive antimicrobial oxidative stress.
DIAGNOSTICS · LIQUID PHASE

## Slide 14: Raman Spectroscopy
DIAGNOSTICS · LIQUID PHASE
The nitrate ν₁ symmetric-stretch band (1045 cm⁻¹) gives a label-free measure of [NO₃⁻]

## Slide 15: From reactive chemistry to decontamination – in vitro
TREATMENT PERFORMANCE
Conidial germination inhibition
Listeria monocytogenes (five-strain mix): all conditions (p < 0.05)
Post-harvest fungi
Complete spore inhibition after 3–5 min for most species; M. fructicola most sensitive, A. alternata / A. carbonarius most resistant.
≤ 30 s
for marked in-vitro CFU drop
Chieffi, D., Aceto, D. et al., Food Research International 236, 119114 (2026) | https://doi.org/10.1016/j.foodres.2026.119114

## Slide 16: From reactive chemistry to decontamination – in vivo
TREATMENT PERFORMANCE
Strawberries & table grapes — untreated vs. 10 min PAF
Pesticide residues: untreated vs. PAF
45–80 %
fewer rotted table grapes (cultivar-dependent)
52–74 %
fewer rotted strawberries
up to 70 %
reduction of chemical pesticides

## Slide 17: An integrated diagnostic path for plasma agriculture
One diagnostic path follows RONS from the discharge field to the treated liquid.
Discharge physics. 38 mJ/burst heats the gas to ≈380 K, OES identifies reactive species and gives E/N trends.
Gas phase. Calibrated LIF gives absolute NO, OH marks the active zone, FT-IR tracks NOₓ, HNO₃ and O₃.
Liquid phase. Raman, validated by colorimetry, quantifies NO₃⁻, NO₂⁻ and H₂O₂ as the PAF acidifies.
Linking operating conditions to RONS dose underpins scale-up and predictive treatments.
Next steps
E/N in all gas mixtures
N₂(v) kinetics and Zel’dovich NO
Dose-response optimisation
Pre-industrial post-harvest trials
CONCLUSIONS & PERSPECTIVES
Notes: Close on the ladder: field (OES, EFISH) -> gas-phase species (LIF, FT-IR) -> liquid (Raman). The decontamination results are the application payoff, not the claim of this talk.

## Slide 18
THANK YOU FOR YOUR ATTENTION!

## Slide 19: EFISH: an independent route to E/N
Field-induced SHG
I(2ω) ∝ (Nχ⁽³⁾E)² I(ω)²: the signal reads E directly.
No kinetic model
E(t) at laser-pulse resolution, free of collisional-radiative rates.
The argon test
Is the FNS/SPS drop in argon a lower E/N, or Ar* energy transfer?
Principle of EFISH and its role as a model-free check of the OES-derived E/N; measurements on this reactor are in progress.
DIAGNOSTICS · PHYSICAL CHARACTERIZATION
Notes: The applied field breaks the inversion symmetry of the gas; a focused ns laser at omega then generates a coherent signal at 2 omega whose intensity scales as (N chi3 E)^2 I^2. Calibrated against a known Laplacian field (discharge off), it gives the absolute field with the laser-pulse time resolution and no assumption on excitation or quenching rates. Here it is set up to answer the question left open by OES in argon mixtures. [If you have field data by the talk, replace the schematic with the E(t) trace.]

## Slide 21: Condensed PAF composition
DIAGNOSTICS · LIQUID PHASE

## Slide 22: From reactive chemistry to decontamination – in vivo
TREATMENT PERFORMANCE
Strawberries
Grapes

## Slide 23: Does the optical port change what you measure?
Discharge identical
Packet period 38.26 ± 0.02 µs, burst 19–786 µs, in both geometries.
Air spectra identical
N₂⁺/N₂ and the vibrational ratios agree to within 2 %.
Argon spectra are not
N₂ (0,3)/Ar I 419.8 falls 6× once nozzle and window are fitted.
Seventeen spectral windows measured in both configurations; every ratio taken inside a single acquisition.
BACKUP

## Slide 24: Emission inside a single voltage burst
Gate-delay scan
One 5 µs gate per trace, stepped through the 800 µs burst.
Emission comes in packets
21 packets, one per 38.26 µs cycle, each about 20 µs wide.
Ratios stay constant
N₂⁺/N₂ and OH/N₂ do not evolve within a packet, below 1.4 σ.
Air, 382–414 nm, 181 gates of 5 µs, 200 accumulations.
BACKUP

## Slide 25: OH laser-induced fluorescence in the discharge
Excitation at 281.8 nm
A–X (1,0) pumped; fluorescence collected 25–35 nm away.
Proof that it is LIF
(0,0)/(1,1) inverts: 1.5–1.6 in emission, 0.6–1.0 under the laser.
Vibrational transfer
v′=1 → v′=0 competes with quenching at atmospheric pressure.
Humid argon, 2000 accumulations, 5 µs gate; single-gate data, so no lifetime information.
BACKUP

## Slide 26: Calibrated NO at the nozzle exit
One calibration
Certified NO/N₂ in four carriers: k = 4.64 × 10⁻¹⁰ V s ppm⁻¹.
Argon: 4× more NO
0.28 ppm with argon against 0.055–0.076 ppm with air in the feed.
Lower bounds
All four plasma signals fall below the 0.3 ppm linear range.
PMT LIF at 226.16 nm, closed reactor, nozzle exit; discharge-off background subtracted. Error bars: counting statistics and slope.
DIAGNOSTICS · LIF
Notes: Calibration: the certified 116 ppm NO/N2 standard is metered into the feed (10 slm; 7 slm for pure argon) and the PMT LIF signal is integrated 18-75 ns after the 226.16 nm pulse. One slope fits all four carriers within 7 %, because the transition is saturated. With the discharge on (discharge-off run subtracted) the nozzle exit carries 0.076 ppm (air), 0.055 (80/20), 0.067 (50/50) and 0.284 ppm (argon). All four lie below 0.3 ppm, where the calibration is sub-linear because of NO flow delivery, so read them as lower bounds. The argon/air factor of ~4 is the robust result. Expect the question about the much larger open-tube ICCD values: different configuration and probe point; jet dilution at the probe is below 1.4x.

## Slide 27: How the NO scale was set
Same slope in every carrier
4.4–5.1 ×10⁻¹⁰ V s ppm⁻¹ from pure air to pure argon.
Saturated transition
Signal does not follow laser energy, so quenching differences cancel.
Floor below 0.3 ppm
All four series bend down: NO flow delivery, not photophysics.
70 calibration points, 116 ppm NO/N₂ standard diluted into 10 slm (7 slm for argon).
BACKUP · LIF CALIBRATION

## Slide 28: Flow model behind those numbers
Closed reactor at 1.4–1.6 bar
The 1 mm nozzle carries the whole pressure drop; falsifiable with a manometer.
Dilution below 1.4× at the probe
Round-jet entrainment anchored to the measured centreline decay constant.
Verified three ways
Exact mass balance, analytic annular profile, grid study within 10 %.
Quasi-1D balances plus an axisymmetric laminar solution written for this geometry; water droplets not included.
BACKUP · FLOW MODELLING

## Slide 29: Where the LIF stations sit in the flow
Recirculation behind the sheath
The annular jet separates at the sheath tip: a bubble ~10 mm long on the axis.
x₀ falls at the reattachment
Axial velocity there is still reversed, so no single residence time applies.
The two downstream points are 2–3 ms apart
130 → 200 ppm over that interval is a usable kinetic step.
Axisymmetric laminar solution, open tube, air at 10 slm; reattachment at 70 ± 1 mm from the grid study.
DIAGNOSTICS · LIF

## Slide 30: Voltammetry and Electrochemical Impedance Spectroscopy
DIAGNOSTICS · LIQUID PHASE
Impedance spectroscopy tracks the same trend quantitatively: AC conductivity rises by orders of magnitude, an independent fingerprint of accumulating ionic RONS.
H2O (baseline)
Cyclic voltammetry shows the condensed liquid turning electro-active with treatment time, as redox features grow from the flat H₂O baseline.