## Slide 1
TokaLab: an open-access and open-source FAIR framework for tokamak synthetic diagnostics and inverse problems benchmarking
Riccardo Rossi, Vasiliki Anagnostopoulou, Valentina D’Agostino, Pasqualino Gaudio, Michela Gelfusa, Simone Kaldas, Andrea Murari, Alessandro Puleio, Novella Rutigliano, Tayyaba Sajid, and Ivan Wyss
8th International Conference on Frontier in Diagnostic Technologies
Frascati, 19-21 October 2026

## Slide 2: The Problems
Steep entry barrier.
Nuclear fusion is a complex, multidisciplinary field, from plasma physics to engineering, diagnostics and data analysis. This discourages students from starting a career in it.
Closed source.
Most algorithms are closed-source and tailored to a specific machine. As a result, several groups work on the same problem in parallel, with little collaboration.
Missing Benchmarking.
Ad hoc algorithms are validated on machine-specific data, with no common datasets or metrics to benchmark their results.
Plasma physics
MHD
Turbulence & transport
Atomic physics
Nuclear physics
Neutronics
Electromagnetism
Diagnostics
Materials science
Superconducting magnets
Cryogenics
Vacuum technology
RF heating
Inverse problems
Neutral beam injection
Power electronics
Control engineering
Thermal hydraulics
Data analysis
Structural mechanics
Tritium & fuel cycle
Remote handling
Machine learning
Radiation protection
Optics & lasers
Spectroscopy
HPC & numerical methods
Same problem: equilibrium reconstruction
JET
EFIT
ASDEX Upgrade
CLISTE
TCV
LIUQE
✗ Different codes, no common benchmark
Reference equilibrium codes per machine, as compared in Coelho et al., EPS 2016–17

## Slide 3: Our Solution
TokaLab is a Virtual Tokamak Laboratory built on four pillars:
Open Source: Everyone can download, use and contribute to it.
Beginner-Friendly: Easy to use for non-experts (e.g. bachelor and master students).
Modular: Modules with different levels of physics fidelity are interchangeable without major modifications.
Multi-Machine: Users can design their own tokamak or apply the methods to existing ones.
Scan to get started on GitHub
Findable · Accessible · Interoperable · Reusable
TokaLab
open virtual tokamak
Students
Learn by doing, at multiple levels of complexity
Contributors
Share and extend modules openly on GitHub
Researchers
Benchmark algorithms on shared data and metrics
Same tools, same data, same benchmarks — for everyone

## Slide 4: TokaLab architecture
Tokamak
Geometry
Machine Specific
Machine Agnostic
Upload all machine-independent information
Create computational domain
SimPla
SimRad
SynDiag
TokaPlot
Equilibrium and profile simulations
Generate radiation profile and/or phantoms
Synthetic diagnostics – evaluate measurements
Advanced Plotting
% machine definition
Machine: “TokaLab”
% geometry
Major_radius: 6; %[m]
Minor_radius: 2; %[m]
% wall information
Wall = load(“TokaLabWall.mat”);
% other information
Other info…

## Slide 5: TokaLab architecture
Tokamak
Geometry
Machine Specific
Machine Agnostic
Upload all machine-independent information
Create computational domain
SimPla
SimRad
SynDiag
TokaPlot
Equilibrium and profile simulations
Generate radiation profile and/or phantoms
Synthetic diagnostics – evaluate measurements
Advanced Plotting

## Slide 6: TokaLab architecture
Tokamak
Geometry
Upload all machine-independent information
Create computational domain
SimPla
SimRad
SynDiag
TokaPlot
Equilibrium and profile simulations
Generate radiation profile and/or phantoms
Synthetic diagnostics – evaluate measurements
Advanced Plotting

## Slide 7: TokaLab architecture
Tokamak
Geometry
Upload all machine-independent information
Create computational domain
SimPla
SimRad
SynDiag
TokaPlot
Equilibrium and profile simulations
Generate radiation profile and/or phantoms
Synthetic diagnostics – evaluate measurements
Advanced Plotting
Physics models: high-fidelity physics, slow (e.g. Bremsstrahlung)
Analytical models (or phantoms): lower fidelity, fast (e.g. MARFE-like)

## Slide 8: TokaLab architecture
Tokamak
Geometry
Upload all machine-independent information
Create computational domain
SimPla
SimRad
SynDiag
TokaPlot
Equilibrium and profile simulations
Generate radiation profile and/or phantoms
Synthetic diagnostics – evaluate measurements
Advanced Plotting

## Slide 9: TokaLab architecture
Tokamak
Geometry
Upload all machine-independent information
Create computational domain
SimPla
SimRad
SynDiag
TokaPlot
Equilibrium and profile simulations
Generate radiation profile and/or phantoms
Synthetic diagnostics – evaluate measurements
Advanced Plotting

## Slide 10: TokaLab applications
Sharing
Open-Source repository to share methods, algorithms, solutions and problems
Education
Development of computational resources to support education
Research
Synthetic tokamak for methods verification
Integrable in workflow for diagnostic design
Open-Source repository for benchmarking
Data generation for machine/deep learning training and test, data augmentation.
In this conference:
AI session (Tuesday)
Ivan Wyss, Optimising the layout of tomographic diagnostics with Genetic Programming
In this conference:
AI session (Tuesday)
Novella Rutigliano, Integrating magnetic and kinetic measurements in the equilibrium reconstruction of tokamaks with Physics Based Neural Networks

## Slide 11: Diagnostic design
It can be used to develop methods for diagnostics design, data analysis, approximation validity, etc.
The example shows Type-I cold plasma approximation against full-Stokes hot plasma approach for plasma polarimetry variables: Faraday rotation and Cotton-Mouton phase shift.
Longer wavelengths increase the polarimetric signals, and so the SNR, but also leads to strong non-linearities, making measurements harder to interpret.

## Slide 12: Benchmarking
With TokaLab it is possible to generate different synthetic/numerical scenarios that are open to everyone.
A new repository, BenchLab has been developed for benchmarking.
The example reports the workflow for inverse problems:
Scenario simulation (Target)
Synthetic diagnostics simulation
Inverse problem (from diagnostics to field)
Comparison between target and prediction.
SimPla + SimRad
Generates scenarios
SynDiag
Evaluate measurements
Algorithms to be benchmarked
Evaluate measurements from fields
Measurements are used by data analysis algorithms
Data analysis algorithms outputs
Comparison with target

## Slide 13: Benchmarking
TIKO
At the moment BenchLab contains only tomographic algorithms (from line-integrated emissivity to local emissivity) and compares two algorithms:
Tikhonov
Maximum Likelihood (ML)
New algorithms can be easily integrated.

## Slide 14: Algorithms development and test
TokaLab capabilities are well suited for Artificial Intelligence applications:
Methods verification
AI and developer “Gym” where specific algorithms can be designed, developed, and tested before going on real scenario and real data
Data augmentation
In this conference:
Poster Session A (Monday)
Tayyaba Sajid, A Neural Network Approach for DTT Plasma Profile Reconstruction validated on data-driven TCV kinetic surrogates
Simone Kaldas, Journal of Fusion Energy, 2026
https://doi.org/10.1007/s10894-026-00568-w

## Slide 15: Beyond coding
We built not just lines of code, but a team.
Research
Used in more than five peer-reviewed scientific articles
Presented at several international conferences
Adopted in national and international collaborations and projects
Education
Integrated into several university courses
Development of an educational game (TokaCards)
Dissemination
Organisation of workshops and events at Tor Vergata University
Contribution
Everyone can contribute by joining the team or by just developing/implementing new methods

## Slide 16: Conclusions and Next Steps
TokaCards
Educational Card Game
TokaLab
VirtualLab
BenchLab
Conclusions
We built a virtual tokamak laboratory for sharing codes and methods.
Everything is based on multi-fidelity: from simple, easy-to-use tools to research-grade methods.
It has found applications in many research works (more than initially expected).
Next Steps
New modules: free-boundary equilibria, impurity transport, new benchmarks (e.g. equilibrium reconstruction).
New initiatives: more educational activities and wider collaborations.

## Slide 17
TokaLab: an open-access and open-source FAIR framework for tokamak synthetic diagnostics and inverse problems benchmarking
Riccardo Rossi, Vasiliki Anagnostopoulou, Valentina D’Agostino, Pasqualino Gaudio, Michela Gelfusa, Simone Kaldas, Andrea Murari, Alessandro Puleio, Novella Rutigliano, Tayyaba Sajid, and Ivan Wyss
8th International Conference on Frontier in Diagnostic Technologies
Frascati, 19-21 October 2026