## Slide 1
The Motion Magnification for large historical and modern structures
Enzo Fioriti¹, Eugenia Verrigni Petrei Castelli², Alessandro Colucci¹, Alessandro Picca¹ and Ivan Roselli¹
¹ENEA ²Università SAPIENZA
ENEA C.R. Casaccia, Laboratorio TERIN ICER ICS
Frascati, 19-21 October 2026

## Slide 2
ORIGINAL VIDEO MAGNIFIED VIDEO
shaking table
NO A.I. INSIDE !

## Slide 3
The camera position in ‘Piazza dei Miracoli’

## Slide 4
Large noise effects
Original video Magnified: bending ~1Hz vertical ~2.6Hz torsional ~6.3Hz
( The original video
is by C. Capotorti )

## Slide 5: Signal extraction
First frame of the magnified video of the Leaning Tower, the MM amplification here is 120 in the frequency range 0.1 – 12.5 Hz.
The final signal, to be elaborated in the frequency domain.
MM is a very convenient technique, but a large number of disturbances act on the video footage: the camera own vibrations, a sudden gust of wind, air turbolences, shadows, low frame rate, poor pixel resolution, short video recording duration, a large random movement in background, … any kind of noise you can imagine.

## Slide 6: MM frequency artifacts 1
Motion magnification works by extracting and amplifying the small movements of pixels in a video: if the camera itself vibrates, it causes a global motion of all pixels.
Our tripod was neither base-isolated from the ground nor shielded from the wind; consequently, its own structural resonant frequencies were directly coupled into the video and then magnified.
This means that also the frequency domain analysis is affected by the artifacts. In fact, since our commercial camera operates at frame rate around of 25 frames per second (fps), according to the Nyquist-Shannon Theorem, the maximum frequency that can be recovered in our case is:
fNyquist = Ffps / 2 = 12.5 Hz
while the calculated resonance frequencies of the tripod are: 2.1 , 5.4 , 18.2 Hz.
Now, if the tripod vibrates at frequencies higher than 12.5 Hz, these frequencies will fold back into the lower spectrum: the 18.2 Hz frequency will appear as a 25 - 18.2 = 6.8 Hz peak. This phenomenon is called aliasing; therefore, these frequencies can be surely discarded.

## Slide 7: MM frequency artifacts 2
To reduce the risk of eliminating a real frequency content filtering the vibration signal, we have chosen to use a Savitzky-Golay filter (SG).
It offers a balance between noise reduction and signal integrity, smoothing high-frequency noise while preserving the low-frequency range.
Unlike traditional moving averages that tend to flatten the data, the SG filter maintains the higher-order moments of the seismic waveform, ensuring that the spectral energy distribution remains physically representative.
However, improper parameter settings can lead to over-smoothing, erasing the subtle modal signatures of a structure or to fit the noise itself, generating spurious spectral peaks that lead to false diagnostic conclusions.
Moreover, the filter is quite ineffective against low-frequency environmental noise, especially in short signals, boundary effects also become a concern, as the lack of data points at the beginning and end of the record can bias the spectral estimate.

## Slide 8
Non-filtered PSD results
square: Fiorentino 2019 ; diamonds: Vignali 2025
The horizontal dotted line selects the candidate frequencies to be identified as the first four natural modes.
Note that between
0.96 Hz – 1.06 Hz
are indicated two modes.

## Slide 9: Filtered PSD results
circles : Motion Magnification; green bold points : Fiorentino19 ; diamonds : Vignali25 ; triangle : FEM
The X are the peaks that the filtering algorithm considers as significant, non-duplicate frequencies.
The red asterisk *
are the artifacts produced by the tripod.

## Slide 10: Details of filtered PSD 0 – 10 Hz
circles : Motion Magnification ; green bold points : Fiorentino19 ; diamonds : Vignali25 ; triangle : FEM
A real first mode, the soil response, or an SG filter artifact ?
The red star:
is the tripod aliasing (below)
The red asterisk:
*
is a resonance
of the tripod (below)

## Slide 11: Numerical results
=

## Slide 12
CASE STUDY– A VIADUCT
The viaduct is a twin-deck cable-stayed bridge with a curved horizontal alignment (475 m radius), 145 m long and 24 m wide. The deck consists of a multi-cell box girder hinged at one end to the base of the pylon and supported at the other by a crossbeam connected to the stay cable system. A cantilever extends from the crossbeam, serving as a support for the second, simply supported span.
MM target
Notes: Viadotto Ansa del Tevere situato sulla A91 Roma-Fiumicino nel quartiere Magliana.
Si tratta di un ponte strallato a doppia carreggiata ad andamento planimetrico curvilineo (475 m di raggio) lungo 145 m e largo 24 m.
L’impalcato si compone da una travata a cassone multicellulare incernierata ad una estremità, alla base della antenna, e dall’altra sorretta da un traverso sul quale insiste il sistema di stralli. Da qui si sviluppa un cantilever che funge da primo appoggio della seconda campata semplicemente appoggiata.

## Slide 13
MM vs OMA Frequency domain Analysis
Chart: Frequenza (Hz)
0,89 Hz
2,83 Hz
CASE STUDY– A VIADUCT
Here MM misses the peak ! (Probably because of the wind)
Hz
Ampl
Notes: Successivamente sono stati confrontati i dati di accelerazione relativi alla postazione MF3 ottenuti con l’OMA e con il Moto Magnificato.
Per la prima si riporta lo spettro medio in accelerazione normalizzato in direzione verticale di due sensori ubicati alle estremità del traversone. Mentre lo spettro in accelerazione normalizzato relativo alla tecnica del MM è stato elaborato eseguendo la trasformata di Fourier (FFT) della storia temporale delle accelerazioni, ricavata derivando due volte quella degli spostamenti rilevati. Si precisa che le accelerazioni utilizzate per il MM si riferiscono ad un pixel posizionato al centro del traversone. Dal grafico si evince che la tecnica del MM ha consentito di identificare le frequenze naturali della struttura, eccezione fatta per il modo corrispondente 1,9 Hz. Dall’analisi OMA a quest’ultima frequenza corrisponde il modo torsionale del traversone, che nella area prossima al suo baricentro produce ampiezze molto inferiori rispetto alle due estremità e quindi non apprezzabili dal MM, ma individuabili dagli accelerometri.
Analizzando l’OMA di riferimento, ci rendiamo conto che alla frequenza di 1.9Hz e 2.55 corrispondono i primi due modi torsionali dell’impalcato.
Avendo preso in esame nel MM un punto in mezzeria del traverso non riusciamo ad apprezzare le ampiezze relative a questa frequenza

## Slide 14
The Motion Magnification for large historical and modern structures
Enzo Fioriti, Eugenia Verrigni Petrei Castelli, Alessandro Colucci, Alessandro Picca and Ivan Roselli
THANK YOU !
CR Casaccia, Laboratorio TERIN - ICER - ICS

## Slide 15
original
magnified

## Slide 16: MM frequency artifacts II
Several strategies exist to overcome the camera vibrations:
modifying the tripod stiffness (lowering the tripod , for example)
removing large-scale camera motion before the magnification algorithm is applied, specialized algorithms for large motion,
event cameras that record only pixel changes,
frequency filtering (temporal filters that selectively amplify motion within a specific frequency band),
artificial intelligence and machine learning.
high-quality hardware to eliminate vibrations at the source or a machine-grade high-speed camera that can provide a stable recording platform, minimizing or even preventing camera shake from the start.
But these remedies lose effectiveness due to their proximity to the useful frequency content: the disturbances are pervasive and too contiguous with the real signal.
This prevents also the simple subtraction of doubtful frequencies from the spectrum of interest in order to fix completely the problem.
Similar drawbacks are encountered using low-pass or band-pass filters, which generally prove to deteriorate the signal.
Furthermore, in outdoor settings, changing lighting conditions can easily produce non-filterable broadband noise.