## Slide 1
Plasma density diagnostics
and machine-learning jitter analysis
for stable PWFA operation at SPARC_LAB
Romain Demitra
SPARC_LAB · INFN Laboratori Nazionali di Frascati
A. Biagioni, L. Crincoli, M. Ferrario, R. Pompili
On behalf of the SPARC_LAB collaboration
ICFDT8 · ENEA Frascati · 21 October 2026

## Slide 2
Driver and witness
Two electron bunches:
the driver excites the wake;
the witness gains energy.
Plasma source
3 cm × 2 mm · H₂
3D-printed capillary
9 kV · ≈400 A
Synchronous diagnostics
Incoming beam, laser and RF
Plasma-density profile
Outgoing energy spectrum
Measuring the plasma and the beam
Romain Demitra · SPARC_LAB / INFN-LNF · ICFDT8 · 21 October 2026
02

## Slide 3
The Hβ line width carries information on electron density
Electric microfields
Nearby charges perturb the hydrogen energy levels and broaden the emission line.
From width to density
Infer nₑ from the Stark contribution using the line-broadening model.
Instrumental and Doppler broadening must also be assessed.
Illustration: SPARC_LAB, Plasma Sources and Diagnostics
Why Stark broadening measures density
Romain Demitra · SPARC_LAB / INFN-LNF · ICFDT8 · 21 October 2026
03

## Slide 4
ACQUISITION
Time-gated ICCD images record hydrogen emission from each discharge.
PROCESSING
Extract and fit Hβ for each image; check residuals and instrumental broadening.
DENSITY
Convert the fitted Stark width to nₑ and repeat along the spatial coordinate.
Raw image, fitted line and residuals
Spatially resolved fits reconstruct the density profile for each shot
From Hβ spectra to electron density
Romain Demitra · SPARC_LAB / INFN-LNF · ICFDT8 · 21 October 2026
04

## Slide 5
Shot-resolved energy spectra
Plasma density at beam arrival
Laser OFF / ON · each row is one shot
6% → 0.4%
relative density fluctuations
Laser-assisted ignition reduces density fluctuations and shots without acceleration.
Measuring the effect of laser-assisted ignition
Romain Demitra · SPARC_LAB / INFN-LNF · ICFDT8 · 21 October 2026
05

## Slide 6
Six working points · 19 measured inputs
Band: shot-to-shot SD · hatching: electrodes
σ(nₑ)/⟨nₑ⟩: ≈1% in five runs;
10.8% in B3.
Input family
Input features
Beam (7)
Charge, timing, durations,
separation, x/y beam position
Radio-
frequency (4)
Gun / linac phase and power
Laser (4)
Phase, intensity, x/y laser position
Plasma (4)
PC scores a₁/a₂, peak z, length
Principal component analysis (PCA)
nₑ(z) ≈ mean profile + a₁ u₁(z) + a₂ u₂(z)
Mode amplitudes a₁ and a₂ are the ML inputs.
Predict witness energy and energy spread
Combining plasma and machine diagnostics
Romain Demitra · SPARC_LAB / INFN-LNF · ICFDT8 · 21 October 2026
06

## Slide 7
Six working points, evaluated with held-out shots
Witness energy
R² ≈ 0.48–0.71
in low-density-jitter runs
Witness energy spread
Weak prediction in stable runs
B3 is an exception
Fivefold validation within each run. Error bars: standard deviation across folds.
Predictability depends on both the operating regime and the target quantity.
What can the measured state predict?
Romain Demitra · SPARC_LAB / INFN-LNF · ICFDT8 · 21 October 2026
07

## Slide 8
B4 · Ridge regression
Representative of five low-density-jitter runs
B3 · Random forest
Larger density fluctuations
Permutation importance: loss of prediction quality when one input is shuffled.
Injected charge leads the prediction
The density profile leads in B3
Which measurements support the prediction?
Romain Demitra · SPARC_LAB / INFN-LNF · ICFDT8 · 21 October 2026
08

## Slide 9
Plasma diagnostics help interpret accelerator stability
Measure the plasma
Hβ spectra
density at each shot
Stark spectroscopy resolves density variations during acceleration.
Verify stabilization
6% to 0.4%
density fluctuations
Density and beam diagnostics quantify the improvement with laser-assisted ignition.
Interpret residual jitter
Charge / density
regime-dependent predictors
Charge leads in stable runs.
Density variations lead in B3.
Spread remains weakly predicted in stable runs.
The useful observables depend on the plasma regime and the beam quantity.
Conclusions
Romain Demitra · SPARC_LAB / INFN-LNF · ICFDT8 · 21 October 2026
09