## Slide 1
This original "Closing the loop: why fusion power demands a new diagnostic blueprint" was created by Alexandru Boboc and Andy Meigs, October 2026
Copyright © UK Industrial Fusion Solutions Ltd. 2025. All rights reserved.
No part of this publication may be reproduced, stored in a retrieval system of any nature, or transmitted, in any form or by any means including photocopying and recording, without the prior written permission of the copyright owner.
Licences issued by the Copyright Licensing Agency or any other reproduction rights organisation do not apply. If any unauthorised acts are carried out in relation to this copyright work, a civil claim for damages may be made and/or a criminal prosecution may result.
COPYRIGHT NOTICE

## Slide 2: Closing the loop: why fusion power demands a new diagnostic blueprint
Principal Diagnostics Engineers
(Members of STEP Diagnostics Leadership team)
Plasma Science and Operation Division, UKAEA National Lab
Culham Campus, Abingdon, OX14 3DB, UK
Alexandru Boboc, Andrew Meigs
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy

## Slide 3: Outline
What are plasma diagnostic
Dichotomy dilemma
Functional role and link with controls
Key requirements
Strategy points
Conclusion
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy

## Slide 4: What are plasma diagnostics
A device or something to measure a property of plasma (e.g. density)
Historically most of them are for post-mortem something to understand plasma physics with some for real-time control(e.g. plasma shape from magnetics sensors)
Evolved from getting one point measurement information to something more advanced like a 2-D profiles, 3D tomography or real-time for control
Advanced with help on computing to evaluate the present* and predict* where the plasma will be in the future
*FMIDA (Forward modelling and Integrated Data Analysis)
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy

## Slide 5: Diagnostics dichotomy
Today’s fusion experiments diagnostic systems strategy
Diagnostics organised around plasma control
Focus on reliability and resilience
Physics exploration become secondary
Key elements:
  Robust and protected methods
  Plasma-state reconstruction
  Fault detection and classification
  Redundancy in methods and channels
  Detailed measurements where predicted models cannot capture unforeseen events
Physics delivery for the most sophisticated diagnostics
Focus on diagnostic high-quality measurements
Advanced control from diagnostics is a secondary priority
at the start
https://euro-fusion.org/programme/demo/
https://stepfusion.com
The future burning plasmas reactor needs
(e.g.DEMO*,STEP**)
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy

## Slide 6
Burning plasma, reactor mode
Plasma Control Parameters and plant protection primarily define diagnostics
(with some room for still unknown Physics that could impact and drive control)
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy

## Slide 7: Defining the required plasma diagnostic set
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy
OFFICIAL - Programme Only
Initial Requirements
Diagnostics Options
Assumptions & feasibility
Diagnostics set chosen
Informed assumptions on achievable measurements
Quantities we need to measure
Range of Technology options to deliver
Candidate Sensor Set
Refined Requirements
Requirements for each diagnostic
R&D on short-list diagnostics set
Market Engagement
Plasma scenario input
Plasma Control System

## Slide 8: Definition of some Key Physics Parameters* to Control
*this list is not definitive yet
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy

## Slide 9: Functional role of the diagnostics set - part 1
Control and Protection
Real-time
Direct and indirect parameter information
Predictive models for control(FMIDA)
Markers,triggers and alarms
Supervision and State
Real-time to inter-pulse
Fast fits and reduced models
Consistency checks
Model-measurement residuals
For the same physical measurements, we have different products, latencies and assurance levels
Development and deep analysis
Inter-pulse to offline
Calibrated full spectra
Advanced FMIDA/posterior
Root cause and new metrics
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy

## Slide 10: Functional role of the diagnostics set –part 2
Logical connections between requirements and the sensor/diagnostics technologies are complex – this can be managed by capturing relevant information in a matrix* format achieved using System Engineering methodologies as in the example table below:
*T.Beernaert “Implementation of Dependency Structure Matrix-based systems engineering for STEP plant control systems” (Internal STEP document)
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy

## Slide 11: Functional role of a single diagnostic
Control:
Provide information about one or a set of plasma parameters
Act as backup for another systems
Act as a reference input for another systems
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy
Physics:
Provide high accuracy data for scenario development
Provide high accuracy data for post-mortem analysis

## Slide 12: Plasma Measurement System (PMS) / Plasma Diagnostics
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy
The new engineering era !

## Slide 13: R&D Innovation Development Program for Diagnostics
Legend:
CP: Control Parameter
PMS: Plasma Measurement System (plasma diagnostic)
PMSS: PMS Set
Simplify !!!
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy
Control Task
Control Model A
CP1
CP2
PMS1
PMS2
PMS3
PMS4
PMS5
Control Task
Control Model A
CP1
CP2
PMS6
PMS3
PMS4
PMS5
Enabling Technology
specific control task performed by control model A requiring parameters CP1 and CP2 to be determined from the PMSS {PMS1, …, PMS5}
Enabling Technology allows direct measurement of CP1 (or reduced) decoupling measurement of CP1 and CP2 ⇒ new PMSS {PMS3, …, PMS6} with new requirements
New idea

## Slide 14: How plasma control and diagnostics works together
Legend:
CP: Control Parameter
PMS: Plasma Measurement System (plasma diagnostic)
PMSS: PMS Set
R&D Innovation Development Program for Plasma Control
Simplify !!!
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy
Control Task
Control Model A
CP1
CP2
PMS6
PMS3
PMS4
PMS5
Control Model B
CP1
CP3
PMS6
PMS3
PMS7
PMS8
PMS9
CP2 ⇒ A no longer the best for the control task
The control CP2 can’t be determined to the required performance ⇒ Control Model A’s performance is inferior to Control Model B’s performance ⇒ new PMSS {PMS3, PMS6, …, PMS9} with new requirements.
Solution:
Different control model using valid alternative parameters
Issue:
Control parameter 2 is no longer valid

## Slide 15: Engineering challenge - System integration
All diagnostics must be integrated with the entire plant from day one of design
Diagnostic number is severely reduced in number as well as resolution (e.g. space limitation)
A novel smart Forward Modelling and Integrated Data Analysis (FMIDA) system
    Combine fewer weaker systems to provide the parameter for control
    Individual optimisation of diagnostic for parameters it infers,
    Grouped diagnostic optimisation to reduce both parameter error/accuracy and further reduce machine impact.
High radiation fluences requires new materials/approaches
A strong tech-gap programme and innovation is required
Lack of an industry chain for diagnostics builders has a direct impact on Delivery & Cost
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy

## Slide 16: Strategic Plan elements for diagnostic plants
Design and Cost Reduction: Minimalist, Modular, Control-First requirement
Reliability: Radiation tolerant
Remote Handling: Zero manual access, Self-Aligning Mechanical RH Interfaces
Operations: Predictive RAMI Analytics & Automated Failure Isolation, self-calibration
Maintenance: Off-Line "Hot Cell" Refurbishment & Swap Workflows
Decommissioning: Low-Activation Material Selection, designed for waste stream segregation
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy

## Slide 17: Forward Modelling and Integrated Data Analysis (FMIDA) logic
Forward models turn candidate hardware into quantified information — integration reveals what the whole set can really deliver.
UKAEA
1
DEFINE THE NEED
Control / protection parameters
Accuracy • latency • robustness
2
MODEL ONE DIAGNOSTIC
Plasma → signal
Physics + instrument + uncertainty
3
OPTIMISE IT
Views • channels • resolution
Maximise useful information
4
INTEGRATE A CLUSTER
Shared state + joint likelihood
Resolve degeneracy • cross-check
5
SELECT THE SET
Meet requirements with minimum
machine impact and uncertainty
candidate state x
→
synthetic signal d = F(x, design) + ε
→
posterior p(x | all data)
→
value of the diagnostic set
ITERATE
Add, remove or redesign diagnostics until
the required plasma parameters are identifiable at the required performance.
The output is not a measurement
it is a trusted plasma-state estimate with an uncertainty level
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy

## Slide 18: Forward Modelling and Integrated Data Analysis (FMIDA) strategy
Qualification of simplified models and software frameworks using data from existing machines suitable for real-time control
Frameworks/techniques that can handle large complex groups of diagnostic and produce surrogate models for control if necessary
Availability of groups of professional scientific programmers for these tasks and integration with new “standards” such as IMAS/SimDB for all input/output data
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy

## Slide 19: Use the past : staffing and lesson-learned issues from old experiments1
Human-resource capability is identified as rarely considered at early design phase, yet decisive for systems that must run for decades; succession planning is listed as a day-one design requirement.
Software development is judged to carry the same importance and cost as hardware, if not more — and is routinely unbudgeted.
Diagnosticians must be involved for full mechanical design of the plant, not consulted after it.
Routine tasks are team-sized, not person-sized: full system commissioning could require many people for weeks at a time;
Costing for the diagnostic lifetime never done
All five points paraphrased from the lessons-learned section of [1] — an open-access UKAEA-authored paper (UKAEA-CCFE-PR(24)263), i.e. our own recorded experience, not an external opinion.
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy

## Slide 20: Conclusion
Non-stop operation, full automation
Reliability and availability is essential
Industry chain and skill set ready for building to scale the first fleet of commercial reactors
A.Boboc and A.Meigs "Closing the loop: Why fusion power demands a new diagnostic blueprint"
ICFDT8 8th International Conference on Frontier in Diagnostic Technologies, 19th -21st October 2026 Frascati, Italy
Operation world for reactor diagnostics
So, for design any new diagnostic today for any machine use these directive above plus:
Innovation is key, go crazy, build start-ups
Transfer existing technologies from other fields
No perfection required => Design & Build, Fail Fast and Repeat but keep an eye on cost

## Slide 21: Many thanks ! For more please contact us at: Alexandru.Boboc@ukaea.uk Andrew.Meigs@ukaea.uk Acknowledgments I would like to thank o all the members Plasma Science and Fusion Operation Division and UKFE for the effort in developing STEP diagnostics. A particular thanks to Neil Conway and Hendrik Meyer for valuable comments to this presentation.
This work has been funded by STEP Fusion, a major technology and infrastructure programme led by UK Fusion Energy Ltd(UKFE), previous named as UK Industrial Fusion Solutions Ltd (UKIFS), which aims to deliver the UK’s prototype fusion powerplant and a path to the commercial viability of fusion.

## Slide 22
DELIVER A UK PROTOTYPE FUSION ENERGY PLANT,
TARGETING 2040, AND A PATH TO
COMMERCIAL VIABILITY OF FUSION.
STEP MISSION