## Slide 1
L. Manzoni (1),(2) *, F. Filippi (2), M. Scisciò (2), M. Alonzo (2), P.L. Andreoli (2), G. Cristofari (2),
E. Di Ferdinando (2), B. Grau (2)(3), V. Piergotti (2), C. Verona (3), M. Migliorati (1),
M. Traunfellner (4), M. Lunzer (4), M. Cipriani (2) and F. Consoli (2).
(1) Università di Roma La Sapienza, Rome, Italy
(2) ENEA, Nuclear Department, C.R. Frascati, Italy
(3) Università di Roma Tor Vergata, Rome, Italy
(4) UpNano GmbH, Vienna, Austria
* leonardo.manzoni@uniroma1.it
Soft X-rays Detection for Plasma Temperature Measurement at the ABC Laser Facility

## Slide 2
The ABC Laser Facility
The ABC laser facility at ENEA Research Centre (Frascati, Italy) is a high-power laser devoted to experiment of inertial confinement fusion and laser-plasma interaction.
Nd:phosphate glass laser.
Wavelength: 1054 nm.
2 x 100J beams.
3-7 ns pulse duration.
Intensity up to 1015 W/cm2.

## Slide 3
X-Ray Diodes at ABC
The interaction chamber is equipped with diodes to detect soft X-rays emitted by laser-generated plasma, used to determine the plasma electron temperature.
Active area: 25 mm2.
Sensitive thickness:100 µm.
Bias voltage: 50 V
They are a set of eight Ge(Li) semiconductor detectors, equipped with variable-thickness filters and interchangeable positions on both sides of the target, arranged in a radial array around the interaction point.

## Slide 4
X-rays from laser-driven plasma are emitted from 3 kinds of electron transition:
Free – free
Free – bound
Bound – bound
X-Ray Emission from Laser Induced Plasma
Calculated X-ray spectrum from Al target irradiated at intensities of 1014 W/cm2
hν1= 2304 eV
Emitted spectral power:
(Hp: Maxwellian electron velocity distribution)
For ν > ν1:
D. Duston et al., Phys. Rev. A 31, 3220 (1985).
Al plasma
Te = electron plasma temperature
Notes: Per Al, h\nu è 2304 eV

## Slide 5
X-Ray Detection
ν = photon frequency.
e = elementary charge.
ε = energy to generate an electron-hole pair.
kf = attenuation coefficient.
df = filter thickness.
Filter transmission
Sensitivity:
(generated current/incident photon energy).
R. W. Kuckuck, Semiconductor Detectors for Use in the Current Mode, Lawrence Radiation Lab (1971).
A photon generates a number of electron-hole pairs in the diode proportional to the deposited energy.

## Slide 6
Plasma Temperature Evaluation
Current from diode:
X-ray
Emitted spectral power
X-ray diode
Diode + filter sensitivity
Filter
?
Ratio of two current signals:
Temperature evaluation with two diodes.
With more than two diodes it is possible to estimate an error on the measurement.
Notes: Absolute measurements are needed to determine the multiplication constant. The most robust way to determine the temperature is by comparing two signals.

## Slide 7
Results from Foam Target
Energy: 30-40 J.
Pulse duration: 3 ns.
Focal spot size: 100 µm.
Intensity: 1x1014 W/cm2.
M. Cipriani et al., presented at 21st DDFIW, Frascati, Italy, 8–11 June 2026.
Laser parameters
X-ray diodes setup
Experimental campaign to study laser interaction with 3D-printed nanostructured plastic foams.
Target manufactured by:

## Slide 8
Results from Foam Target
SHOT | Te average [eV]
#7196 | 320 ± 46
#7221 | 334 ± 41

## Slide 9
Results Comparison with X-ray Grating
SHOT | Te average from diodes [eV] | Te from X-ray grating
#7196 | 320 ± 46 | 366 ± 18
#7221 | 334 ± 41 | 336 ± 15
#7196
#7221
M. Salvadori et al., 2019 JINST 14 C03007.
Validation of the results using an X-ray diffraction grating already installed in the chamber.

## Slide 10
Results from Metallic Target
Energy: 30-40 J.
Pulse duration: 3 ns.
Focal spot size: 50 µm.
Intensity: 5x1014 W/cm2.
Laser parameters
X-ray diodes setup
Experimental campaign conducted with thick aluminum targets.
(Diffraction grating unavailable because the target blocked the line of sight).

## Slide 11
Results from Metallic Target
SHOT | Te average [eV]
#7281 | 604 ± 142
#7285 | 734 ± 120

## Slide 12
Conclusions
X-Ray Diode Array: Implemented a filtered PIN diode diagnostic at the ABC laser facility for reliable electron temperature () reconstruction and uncertainty estimation.
Design: Optimized filter thickness and multi-detector configurations (up to 8 channels) to minimize errors and statistical signal fluctuations.
Cross Validation: Successfully tested on foam and aluminum targets, showing excellent agreement with independent transmission grating measurements.
Future Upgrades:
  Enhanced EMP shielding for improved signal-to-noise ratio in high-power regimes.
  Integration of a high-density transmission grating with a SLIX camera for time-resolved spectral characterization.

## Slide 13
Thank you
for your attention
Acknowledgements
Activities partially funded through the ReMade@ARI project by the European Union as part of the Horizon Europe call HORIZON-INFRA-2021-SERV-01 under grant agreement number 101058414 and co-funded by UK Research and Innovation (UKRI) under the UK government’s Horizon Europe funding guarantee (grant number 10039728) and by the Swiss State Secretariat for Education, Research and Innovation (SERI) under contract number 22.00187. Views and opinions expressed are however those of the author(s) only and do not necessarily reflect those of the European Union or the UK Science and Technology Facilities Council or the Swiss State Secretariat for Education, Research and Innovation (SERI). Neither the European Union nor the granting authorities can be held responsible for them.

## Slide 14
Backup Slides

## Slide 15
Filter Optimisation
Filter thickness in diode pairs can be optimized to minimize the effect of statistical signal fluctuations on temperature estimation error.
Parameter to minimise

## Slide 16
X-Ray Angular Emission
Angular emission
All the diodes must be positioned at the same angle from the normal to the target.
Cylindrical symmetry around the axis normal to the target [1].
D. Giulietti e L. A. Gizzi, Riv. Nuovo Cimento 21, 1 (1998).
Emitted spectral power:

## Slide 17
Temporal Resolution
µe,h = electron and hole mobilities
D = diode thickness
V = voltage
For our Ge(Li) diodes:
te = 0,5 ns
th = 1 ns
I. C. E. Turcu e G. J. Tallents, X-Rays from Laser-Plasmas: Generation and Applications, John Wiley & Sons (1999).
Charge collection time:

## Slide 18
X-Ray Diffraction Grating
d = grating period
m = diffraction order
Spectrum reconstruction:
Spectral resolution:
Diffraction limit:
Geometrical resolution: