## Slide 1
Research Progress of the Polarimeter/Interferometer on the EAST and BEST Tokamak
Shouxin Wang1, Haiqing Liu1, Yinxian Jie1, Yang Zhang1, Ling Zhang1 , Weiming Li1 , Yuan Yao1, Hui Lian1, Xuechao Wei1, Ting Lan1, Ximo Peng2, Yao Zhang1, Weixing Ding3
8th International Conference on Frontier in Diagnostic Technologies, Oct. 19-21, 2026, Frascati, Italy
1Institute of Plasma Physics, Hefei Institutes of Physical Science. Chinese Academy of Sciences, Hefei 230031, China
2University of Science and Technology of China, Hefei 230026, China
3University of California Los Angeles, Los Angeles, CA 90095, United States of America
OCT 21, 2026
Notes: 姓名；来自哪里；EAST POINT， BEST 前向模型

## Slide 2
02 Application of POINT on EAST tokamak
CONTENTS
03 Development of POINT Model for BEST tokamak
01 Introduction
04 Summary and Outlook

## Slide 3
EAST Far-Infrared System Layout
A
D
I
M
A
B
C
D
E
F
P
O
G
H
I
J
K
L
M
N
HCN interferometer
solid-state diode sources inteferometer
Polarimeter-interferometer
（POINT）
POlarimeter-INTerferometer (POINT@432 mm)
HCN interferometer (HCN@ 337 mm)
CO2 Dispersion Interferometer (DI@9.3 mm)
Core profiles,
Line-integrated
Line-integrated
Solid-state diode Sources Interferometer（SSI@461 mm）
Line-integrated
CO2 Dispersion Interferometer）

## Slide 4
POlarimeter and Interferometer (POINT) on EAST
The polarimeter-interferometer is one of the most critical diagnostics on EAST, serving three main roles : i. Device protection (disruption warning); ii. Operational control (feedback control of electron density, current density, etc.); iii. Physical understanding.
POINT
Real-time ne measurement
MHD
instabilities
Plasma displacement
Perturbation measurement
Core density fluctuation
Disruption
Real-time profile monitoring
Real-time feedback control
EAST
POINT

## Slide 5
POlarimeter and Interferometer (POINT) on EAST
The polarimeter-interferometer is one of the most critical diagnostics on EAST, serving three main roles : i. Device protection (disruption warning); ii. Operational control (feedback control of electron density, current density, etc.); iii. Physical understanding.
POINT
Real-time ne measurement
MHD
instabilities
Plasma displacement
Perturbation measurement
Core density fluctuation
Disruption
Real-time profile monitoring
Real-time feedback control
POINT Optical Layout
Three wave technique

## Slide 6
POINT System Measurement Results
Line-integrated density and Faraday rotation angle measurement
Density Feedback
ne and q profiles
Vertical displacement measurement
Disruption precursor
Density fluctuation

## Slide 7
Solid - State Source Lasers for POINT
VDI Solid - State Source Lasers
Domestic Solid - State Source Lasers
  Easy operation No preheating required
  Frequency stability Suitable for long - pulse operation
  Smaller size Easy to implement electromagnetic shielding
Operability, stability, and reliability have all been significantly improved!
BUT the out power is much lower than gas laser, especially for higher frequency.
Intermediate Frequency and Power Stability
1000s H - mode measurement
Long pulse faraday measurement

## Slide 8
Development of POINT Model for BEST

## Slide 9
03
POINT model based on ray tracing
Integrated into IMAS, validated EAST data;
Good agreement between POINT model and TIP model
Assumption： Collisionless, cold plasma
Measurement：integral density and faraday
Programming: Python
Validation: EAST data and POINT system configuration
  interferometer =point_model(equilibrium,core_profiles,geometry)

## Slide 10
Ip | 5.3MA
Te0 | 18keV
BT | 6T
ne | 7.2×1019m-3
Schematic illustration of the designed LOS for the POINT
BEST Q~1 scenario
118 μm offers a Faraday rotation signal two orders of magnitude stronger than 10.6 μm, making it the clear choice for robust polarimetric measurements, also exhibits larger beam deflection.
For BEST, the signal advantage decisively outweighs the refraction penalty.
Central horizontal chords cover plasma current center
*For Q>5, ne will be 2×1020m-3
Physical Design of BEST POINT diagnostic

## Slide 11
03
Cotton-Mutton effect
CM also has little effect on faraday rotation, except for the 5th chord which is poloidal chord passes the plasma center.
As wavelength increases, the CM effect becomes more pronounced, reaching a 15.7% contribution at 500 µm.
CM effect is calculated using Matrix Propagation Along the Ray Path
Cotton-mutton effect

## Slide 12
Summary and Outlook

## Slide 13
Summary:
POINT supports density and faraday rotation measurements and the long-pulse H-mode measurements demonstrate system operability and stability.
An IMAS-integrated ray-tracing model has been developed, with results compared against EAST data and the TIP model.
Initial LOS and wavelength studies indicate a strong Faraday signal at 118 μm; CM effects and beam deflection have also be assessed.
04 Summary and Outlook
Future Plans：
Extend validation and quantify CM for more BEST scenario.
And finite-temperature effects should be considered.

## Slide 14
Thank You!

## Slide 15
backup

## Slide 16
02
System Error
Cotton-mutton effect
The plasma birefringence effect leads to a change in polarization ellipticity
Finite temperature effect，Geometric phase error
Finite temperature effect: when the plasma temperature is high, the dielectric tensor needs to be corrected
Geometric phase error: considering the electromagnetic wave propagation path in the plasma
the maximum system geometric phase is on the order of 0.01°, negligible
Refraction effect
Mechanical vibration and intermediate frequency error
Collinearity error
May cause optical path deviation
Simple calculation shows a maximum POINT deviation of 14 mm for an 82 mm
window, with minor impact.
Substituting EAST parameters:
Electron density measurement error caused by mechanical vibration is less than 10¹⁶ /m²
Mechanical vibration error:
Intermediate frequency error:
System collinearity error is approximately 0.2°
J. Chen et al PPCF 60 (2018) 085001
T. Lan et al POP 23, 072109 (2016)
Jie Chen, PhD Thesis, HUST, 2013
electron temperature is below 10 keV, the measurement error is within 10%
Zhiyong Zou, PhD Thesis, ASIPP, CAS, 2018