## Slide 1: Control of Parametric Instabilities by means of Non-monochromatic RF Power Injection
PDR SOLUTIONS for EAST and FTU
By
FRANCESCO NAPOLI

## Slide 2: OUTLINE
PARAMETRIC DECAY STABILIZATION METHODS
LITERATURE BACKGROUD
PUMP SPECTRAL REPRESENTATION
FEATURES OF THE SPECTRAL BROADENING MODEL
NEW PARAMETRIC DISPERTION RELATION (PDR)
PDR VALIDATION
PDR SOLUTIONS FOR EAST AND FTU
BREAKTHROUGH: PDR SOLUTIONS FOR EAST AND FTU
CONCEPTUAL DESIGN OF A RF DRIVER FOR FTU
N// SPECTRUM CONTROL OF A MULTI-JUNCTION ANTENNA
CONCEPTUAL DESIGN OF A RF DRIVER FOR EAST
CONCLUSIONS

## Slide 3: PARAMETRIC DECAY STABILIZATION METHODS
INTRINSIC PARAMETERS:
DENSITY
TEMPERATURE
PLASMA COMPOSITION
EXTRINSIC PARAMETERS:
PUMP POWER DENSITY
PUMP FREQUENCY
PUMP SPECTRUM (MODULATED/MULTI PUMP)

## Slide 4: LITERATURE BACKGROUD
In laser-pellet fusion, the application of a finite bandwidth pump to stabilize PIs is well known (Brillouin and Raman scattering):
Theoretical studies: VALEO et al 1973; THOMSON et al 1974, 1975
Experimental studies: OBENSCHAIN et al 1976, 1977; MIZUNO et al. 1977
In magnetic confinement fusion, this method has attracted less attention:
Theoretical studies: STEFAN Phys. Fluids 26 1983
Experimental studies: MATSUMOTO et al Plasma Physics 12 25 1983; ARKHIPENKO et al Journal of Physics Conf. Series 257 2010

## Slide 5: PUMP SPECTRAL REPRESENTATION
Chart: 
| 0 | 0.5 | 1 | 1.5 | 1.75 | 2 | 2.5 | 3 | 3.5 | 4 | 5 | 6 | 10
Pc | 1 | 0.88889 | 0.66667 | 0.47059 | 0.39506 | 0.33333 | 0.24242 | 0.18182 | 0.14035 | 0.11111 | 0.074074 | 0.052632 | 0.019608
PL_tot | 0 | 0.11111 | 0.33333 | 0.52941 | 0.60494 | 0.66667 | 0.75758 | 0.81818 | 0.85965 | 0.88889 | 0.92593 | 0.94737 | 0.98039
PL1_PL2 | 0 | 0.055556 | 0.16667 | 0.26471 | 0.30247 | 0.33333 | 0.37879 | 0.40909 | 0.42982 | 0.44444 | 0.46296 | 0.47368 | 0.4902
fc
fc-fM
fc+fM
Pc
PL1
PL2
PL1=PL2=
Ptot=
E(t)++
=B/A
-
+
AMPLITUDE MODULATED DRIVER-PUMP:

## Slide 6: PUMP SPECTRAL REPRESENTATION
m=B/A > 1: overmodulation
m=1: PLtot = (1/3)Ptot, Pc=(2/3)Ptot
m=2: Pc=PL1=PL2=(1/3)Ptot (triple driver pump)
m=10: PLtot = (49/51)Ptot, Pc=(1/51)Ptot
m->Inf: PL1=PL2->(1/2)Ptot; Pc->0 (double driver pump)
In the overmodulation regime, nonlinearities must be taken into account (AM nonlinear distortions).
The multiple driver-pump scheme should be preferred due to destabilizing effects on PIs caused by a narrow bandwidth AM pump as observed by K. Matsumoto (Plasma Physics 12 25 1983) and in agreement with theoretical considerations by Aliev (Journal de Physique 7 40 1979).
Within the multiple driver-pump scheme, intermodulation products must be taken into account not only to avoid power losses in not useful spectral components but also to avoid amplitude modulations able to destabilize PIs.
An optimum backoff of the power amplifier and the equalization of multiple drivers can minimize the nonlinear distortions due to the non-ideal behaviour of the tube (klystron).
Note: in this power application, tube nonlinearities could be not as detrimental as in telecoms!
Notes: As AM modulator, a voltage controlled amplifier should not be used but instead a multiplier circuit (mixer) should be preferred to avoid most of nonlinear distortions. Also AM modulation in undermodulation regime with an amplitude equalization could be a solution to avoid the nonlinearities of the AM modulator…
Tube nonlinear distortions can be detrimental due to amplitude and phase changing.

## Slide 7: Features of the Spectral Broadening model
Standard theory | Spectral Broadening model
WKB approximation | full-wave analysis in radial direction
4 waves interaction | full-spectrum analysis
No pump depletion | Pump depletion
No collisions | Collisions
Poisson-Vlasov system | Maxwell-Boltzmann system
Simplified model of thermal noise | Analytical model of thermal noise
No RF antenna noise | RF antenna noise

## Slide 8: NEW PARAMETRIC DISPERSION RELATION
fc
f0-fM
f0+fM
Pc
PL1
PL2
f3
f1
f4
f2
f5
f6
,
,
,
AM:
Selection
Rules:
: PDR with a non-monochromatic pump
: PDR with a monochromatic pump as in standard theory
PDR:
Case
Studies:

## Slide 9: PDR VALIDATION
FTU (SOL)
ne (10^12 m^-3) | 2
Te (eV) | 10
nz0 | 2
f0 (GHz) | 8
B0 (T) | 4.5
Pden (kW/cm^2) | 3.06
(c/ω0)k// | theoretical gamma | max gamma | Δgamma %
5 | 0.0016876 | 0.001974526 | 17.00%
10 | 0.0027476 | 0.003077283 | 12.00%
15 | 0.0036335 | 0.003960563 | 9.00%

## Slide 10: Experimental Advanced Superconducting Tokamak
ne (10^12 cm^-3) | 1
Te (eV) | 12
nz0 | 2.1
f0 (GHz) | 2.45
B0 (T) | 1.8
Pden (kW/cm^2) | 1.45
EAST (SOL)

## Slide 11: MAX GAMMA vs MODULATION INDEX
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te
15 | 1.45*10^3 | gamma_0 /5*gamma_0 | 1*10^12 | 12
fM ≈ 10-60 MHz

## Slide 12: MAX GAMMA vs MODULATION INDEX
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te
5-7-10-15 | 1.45*10^3 | 2*gamma_0 | 1*10^12 | 12
fM ≈ 10-20 MHz

## Slide 13: FRASCATI TOKAMAK UPGRADE
FTU (SOL)
ne (10^12 m^-3) | 2
Te (eV) | 10
nz0 | 2
f0 (GHz) | 8
B0 (T) | 4.5
Pden (kW/cm^2) | 3.06

## Slide 14: MAX GAMMA vs MODULATION INDEX
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te
15 | 3.06*10^3 | 0.5*gamma_0/3*gamma_0 | 2*10^12 | 10
fM ≈ 15-95 MHz
Results consistent with K. Matsumoto et al. Plasma Phys. 25 (1983) and V.Stefan, Phys. Fluids, 26 (1983)

## Slide 15: MAX GAMMA vs MODULATION INDEX
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te
5-7-10-15 | 3.06*10^3 | 2*gamma_0 | 2*10^12 | 10
fM ≈ 30-65 MHz

## Slide 16: breakthrough
fc
f0-fM
f0+fM
Pc
PL1
PL2
nz0
nz0
nz0
Pc
PL1
PL2
nz0
nzL1
nzL2
Pc
PL1
PL2
nzL1,2= nz0 ± Δnz0
nzL1,2= nz0

## Slide 17: breakthrough
fM << γ0/2 π ≈ 5-15 MHz
fM = 100 kHz
|Δn//0|/n//0 ≈ 0%
|Δn//0|/n//0 ≈ 10%
67.86%
(c/ω0)k// = 10

## Slide 18: breakthrough
fM << γ0/2 π ≈ 5 MHz
fM = 100 kHz
(c/ω0)k// = 5

## Slide 19: breakthrough
fM = 100 kHz
|Δn//0|/n//0 ≈ 10%
fM << γ0/2 π ≈ 5 MHz

## Slide 20: EAST – MAX GAMMA vs DENSITY
Chart: 
| 1*10^12 | 2*10^12
 | 0.66923 | 0.67692
(c/ω0)k// | Pden (m=0) | ne | Te | nz0
10 | 1.45*10^3 | 1*10^12 – 2*10^12 | 12 | 2.1
caso 1 | fM = 10 kHz
10% | m = 2
cm-3

## Slide 21: EAST – MAX GAMMA vs POWER DENSITY
Chart: 
| 1.45*10^3 | 2*10^3 | 3*10^3
 | 0.66923 | 0.68939 | 0.70588
(c/ω0)k// | Pden (m=0) | ne | Te | nz0
10 | 1.45-2-3*10^3 | 1*10^12 | 12 | 2.1
caso 1 | fM = 10 kHz
10% | m = 2

## Slide 22: CONCEPTUAL DESIGN OF A RF DRIVER FOR FTU
In FTU a full phased waveguide antenna array is employed.
Unfortunately, the Brambilla code shows that an optimum waveguide phasing for a double peaked n// spectrum would imply impractical reflection levels.
Hence, it is only possible to use a multiple driver-pump scheme.
Necessary changes to the LHCD system to make a double driver-pump scheme:
Combine two power transmission lines in oversized circular waveguide (bringing power from two gyrotrons working at two different frequencies) just before the 12-way LH power splitter/mode converter.
Modify the terminal part of the power transmission line: after the 12-way LH power splitter/mode converter, on each of 12 WR 137 rectangular waveguides, the phase shifter should be replaced by a cascaded system based on waveguide directional filters (each made of two band-pass power filters and two hybrid junctions) which should allow to phasing selectively the two different spectral driver components.
Design and development of the new power microwave system is required.
Unfortunately, this system implementation is not ITER relevant because the LHCD system of ITER is foreseen with a passive active multi-junction (PAM) antenna.

## Slide 23: CONCEPTUAL DESIGN OF A RF DRIVER FOR FTU
FTU LHCD System | 
Nominal frequency | 8 GHz
RF Source | Gyrotron
Nominal RF power | 1 MW
Number of RF sources | 6
Maximum overall power | 6 MW
Maxiumum pulse length | 1 s
Maximum duty cycle | 1/600

## Slide 24: CONCEPTUAL DESIGN OF A RF DRIVER FOR FTU
Φ
a
b
a
b
Φ
Φ
f0+f1+f2
f0+f2
f1
f2
f0
f0
f0+f2
f2
f1
f0+f1+f2
Φ
a
a
Φ
f2
f2
f1
f1+f2
f1
f1+f2

## Slide 25: N// SPECTRUM CONTROL OF A MULTI-JUNCTION ANTENNA (FAM/PAM)
Phase difference between two adjacent modules
Number of active waveguides in a module
Intrinsic phase shift of the multijunction waveguide array
N// peak of a single module
(3 kW/cm2)

## Slide 26: CONCEPTUAL DESIGN OF A RF DRIVER FOR EAST
Digital phase shifter

## Slide 27: CONCEPTUAL DESIGN OF A RF DRIVER FOR EAST
Master oscillator f01
Power divider
20 identical RF drive chains
Master oscillator
f02
Power divider
20 identical RF drive chains
Phase
control
Phase
Ref.
ΔΦ01
ΔΦ02
Double driver-pump scheme:
x 20
NB1: the multiple driver-pump scheme can be ideally applied at the same frequency but this is not desirable in practice for two reasons: 1) the operating point of the tube should be kept in linear region to avoid nonlinear distortions and this is helped by the power splitting on different (but close) frequencies within the klystron bandwidth; 2) to phase out independently different drivers among antenna modules, it is necessary to have a spectral separation (not time coherence) among different drivers.
NB2: at the same time, to avoid nonlinear self-interactions among pump components, it’s important to keep the spectral separation as small as possible!

## Slide 28: CONCLUSIONS
WE DISCOVERED A NEW METHOD TO CONTROL PIs BY MEANS OF AN AMPLITUDE MODULATED PUMP/ MULTIPLE DRIVER-PUMP WITHIN THE KLYSTRON BANDWIDTH.
SIMULATIONS SUGGEST THIS RESULT CAN BE ACHIEVED WITH A DIFFERENT N// PEAKING OF THE AM SIDEBANDS/MULTIPLE DRIVER-PUMP.
UNFORTUNATELY, IT IS VERY DIFFICULT TO APPLY THIS METHOD ON THE LHCD SYSTEM OF FTU (NECESSARY CHANGES ON THE POWER TRASMISSION LINE).
INSTEAD IT IS STRAIGHTFORWARD TO APPLY THIS METHOD ON THE LHCD SYSTEM OF EAST (NECESSARY CHANGES ON THE RF TRASMISSION LINE).
WE HAVE SHOWN HOW THE RF DRIVER OF EAST SHOULD BE MODIFIED.
THIS METHOD CAN BE APPLIED ALSO ON THE FUTURE LHCD SYSTEM OF ITER.

## Slide 29
THANK YOU!

## Slide 30: growth rate estimation for pis suppression
We know from full-wave simulations that to have a significant pump depletion, LH sidebands should grow of 60 dB in power over a 3 cm radial length in the SOL of FTU: we have a spatial growth rate 4.6.
To have a negligible effect on the pump driver, the LH sideband power level should be at least one order of magnitude lower. This imply a spatial growth rate threshold3.84 corresponding to a growth rate reduction of 16.5%.
Thus, a growth rate reduction of about 20% (as in the double driver pump case) seems well sufficient to have a significant reduction of PIs.
In this work we also found a maximum growth rate reduction of about 30%, well below the previous threshold level, and this should correspond to a LH sideband power level about 2 order of magnitude lower in the SOL of FTU!

## Slide 31: PDR VALIDATION
(c/ω0)k// | omega_guess | gamma_guess | omega_0 | gamma_0 | delta_omega% | delta_gamma%
5 | 0.0005163 | 0.0016876 | 0.001239133 | 0.001974526 | 140.00% | 17.00%
10 | 0.0010326 | 0.0027476 | 0.001941309 | 0.003077283 | 88.00% | 12.00%
15 | 0.0015489 | 0.0036335 | 0.00260218 | 0.003960563 | 68.00% | 9.00%
FTU (SOL)
ne (10^12 m^-3) | 2
Te (eV) | 10
nz0 | 2
f0 (GHz) | 8
B0 (T) | 4.5
Pden (kW/cm^2) | 3.06
Chart: 
| 5 | 10 | 15
gamma_guess | 0.0016876 | 0.0027476 | 0.0036335
max_gamma | 0.0019745 | 0.0030773 | 0.0039606

## Slide 32: PDR VALIDATION
Chart: 
| 5 | 10 | 15
omega_guess | 0.00051631 | 0.0010326 | 0.0015489
omega | 0.0012391 | 0.0019413 | 0.0026022
FTU (SOL)
ne (10^12 cm^-3) | 2
Te (eV) | 10
nz0 | 2
f0 (GHz) | 8
B0 (T) | 4.5
Pden (kW/cm^2) | 3.06
(c/ω0)k//
(c/ω0)k// | omega_guess | gamma_guess | omega_0 | gamma_0 | delta_omega% | delta_gamma%
5 | 0.0005163 | 0.0016876 | 0.001239133 | 0.001974526 | 140.00% | 17.00%
10 | 0.0010326 | 0.0027476 | 0.001941309 | 0.003077283 | 88.00% | 12.00%
15 | 0.0015489 | 0.0036335 | 0.00260218 | 0.003960563 | 68.00% | 9.00%

## Slide 33: EAST
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te
5-6-7-8-9-10-15 | 1.45*10^3 | 2*gamma_0 | 1*10^12 | 12
fM ≈ 10-20 MHz
Chart: 
| 0 | 2 | 3 | 10
delta nz = 5 | 1 | 0.94853 | 0.93382 | 0.93382
delta nz = 6 | 1 | 0.90299 | 0.89552 | 0.89552
delta nz = 7 | 1 | 0.8797 | 0.8797 | 0.8797
delta nz = 8 | 1 | 0.86364 | 0.86364 | 0.87121
delta nz = 9 | 1 | 0.86154 | 0.86154 | 0.86923
delta nz = 10 | 1 | 0.84615 | 0.85385 | 0.86154
delta nz = 15 | 1 | 0.83465 | 0.84252 | 0.85827

## Slide 34: EAST
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te
15 | 1.45*10^3 | gamma_0 /5*gamma_0 | 1*10^12 | 12
fM ≈ 10-60 MHz
Chart: 
| 0 | 2 | 3 | 10
1*gamma_0 | 1 | 0.92126 | 0.91339 | 0.91339
2*gamma_0 | 1 | 0.83465 | 0.84252 | 0.85827
3*gamma_0 | 1 | 0.7874 | 0.80315 | 0.82677
4*gamma_0 | 1 | 0.75591 | 0.7874 | 0.81102
5*gamma_0 | 1 | 0.74016 | 0.77165 | 0.80315
Results consistent with K. Matsumoto et al. Plasma Phys. 25 (1983) and V.Stefan, Phys. Fluids, 26 (1983)

## Slide 35: EAST
(c/ω0)k// | Pden (m=0) | ne | Te
6 | 1.45*10^3 | 1*10^12 | 12
Chart: 
| 0 | 0.5 | 0.7
Li_Zi=1 | 1 | 0.85821 | 0.79104
Li_Zi=2 | 1 | 0.92537 | 0.89552
Trizio | 1 | 0.9403 | 0.91791
Te | 1 | 0.9892 | 0.97381

## Slide 36: EAST
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te
6 | 1.45*10^3 | 2*gamma_0 | 1*10^12 | 12
fM ≈ 15 MHz
Chart: 
| 0 | 2 | 3 | 10
Tex2_D_100% | 0.97381 | 0.97381 | 0.97381 | 0.97381
Li_50%_Zi=2 | 0.92537 | 0.92537 | 0.92537 | 0.92537
Li_50%_Zi=1 | 0.85821 | 0.85821 | 0.85821 | 0.85821
Li_70%_Zi=1 | 0.79104 | 0.79104 | 0.79104 | 0.79104
Li_70%_Zi=2 | 0.89552 | 0.89552 | 0.89552 | 0.89552
AM_Li_70% | 1 | 0.72388 | 0.69403 | 0.69403 | 0.69403
AM_D_100% | 1 | 0.90299 | 0.89552 | 0.89552

## Slide 37: FTU
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te
5-10-15 | 3.06*10^3 | 2*gamma_0 | 2*10^12 | 10
fM ≈ 30-65 MHz
Chart: 
| 0 | 1 | 2 | 3 | 10
delta nz = 5 | 1 | 0.96581 | 0.94017 | 0.93162 | 0.92308
delta nz = 7 | 1 | 0.90435 | 0.86087 | 0.86957 | 0.86957
delta nz = 10 | 1 | 0.875 | 0.83036 | 0.83929 | 0.84821
delta nz = 15 | 1 | 0.87156 | 0.81651 | 0.83486 | 0.84404

## Slide 38: FTU
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te
15 | 3.06*10^3 | 0.5*gamma_0/3*gamma_0 | 2*10^12 | 10
fM ≈ 15-95 MHz
Chart: 
| 0 | 1 | 2 | 3 | 10
0.5*gamma_0 | 1 | 0.98165 | 0.97248 | 0.9633 | 0.9633
1*gamma_0 | 1 | 0.94495 | 0.90826 | 0.90826 | 0.89908
2*gamma_0 | 1 | 0.87156 | 0.81651 | 0.83486 | 0.84404
3*gamma_0 | 1 | 0.86239 | 0.77064 | 0.78899 | 0.81651

## Slide 39: FTU
(c/ω0)k// | Pden (m=0) | ne | Te
5 | 3.06E+03 | 2*10^12 | 10
Chart: 
| 0 | 0.5 | 0.7
Li_Zi=1 | 1 | 0.86325 | 0.79487
Li_Zi=2 | 1 | 0.93162 | 0.89744
Trizio | 1 | 0.94017 | 0.91453
Te | 1 | 0.97934 | 0.9633
Li_Zi=1_50MHz | 1 | 0.64957 | 0.5812

## Slide 40: FTU
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te
5 | 3.06E+03 | 2*gamma_0 | 2*10^12 | 10
fM ≈ 30 MHz
Chart: 
| 0 | 1 | 2 | 3 | 10
AM_D_100% | 1 | 0.96581 | 0.94017 | 0.93162 | 0.92308
Li_50%_Zi=1 | 0.86325 | 0.86325
Li_50%_Zi=2 | 0.93162 | 0.93162
Li_70%_Zi=1 | 0.79487 | 0.79487
Li_70%_Zi=2 | 0.89744 | 0.89744
Tex2_D_100% | 0.9633 | 0.9633

## Slide 41: FTU – max gamma vs collision frequency
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te
5 | 3.06E+03 | 2*gamma_0 | 2*10^12 | 10
fM ≈ 30 MHz
Chart: 
| 0.1 | 1 | 10 | 20 | 30 | 50 | 100 | 200 | 300 | 400 | 500 | 600
max_gamma_D_100% | 1 | 1 | 0.95726 | 0.91453 | 0.87179 | 0.78632 | 0.59829 | 0.33333 | 0.19658 | 0.11966 | 0.08547 | 0.059829
max_gamma_nu_i=0 | 0.94017
max_gamma_nu_e=0 | 0.86325
max_gamma_Li_50% | 0.64957
max_gamma_Li_70% | 0.5812
f_col (MHz)

## Slide 42: EAST - breakthrough
(c/ω0)k// | delta_fo (MHz) | delta_nzo | kperp
10 | 0 | 0% | 10.64117869
10 | -0.1 | -10% | 11.40537123
10 | 0.1 | 10% | 9.876998323
10 | 0.1 | -10% | 11.40519236
10 | -0.1 | 10% | 9.877152846
10 | -1 | -10% | 11.40617567
10 | 1 | 10% | 9.876302559
10 | -1 | 0% | 10.64201173
10 | 1 | 0% | 10.64034476
10 | -10 | 0% | 10.64946863
10 | 10 | 0% | 10.63279888
10 | -20 | 0% | 10.65766891
10 | 20 | 0% | 10.62432897
10 | -30 | 0% | 10.66577972
10 | 30 | 0% | 10.61576876
10 | -100 | 0% | 11.67376017
10 | 100 | 0% | 10.55330004
(c/ω0)k// | delta_fo (MHz) | delta_nzo | kperp
5 | 0 | 0% | 1.474070014
5 | -0.1 | -10% | 2.236307631
5 | 0.1 | 10% | 0.711844599
5 | -0.1 | 10% | 0.711855285
5 | 0.1 | -10% | 2.236272537
5 | -1 | -10% | 2.23646546
5 | 1 | 10% | 0.711796484
5 | -10 | 0% | 1.475208349
5 | 10 | 0% | 1.472919346
5 | -20 | 0% | 1.47633438
5 | 20 | 0% | 1.471756316
5 | -30 | 0% | 1.477448134
5 | 30 | 0% | 1.470580896
(c/ω0)k// | Pden (m=0) | ne | Te | nz0
5-10 | 1.45*10^3 | 1*10^12 | 12 | 2.1
Case 1 | 
Case 2 | 

## Slide 43: EAST – Δnz = 5 (Δnz0 = 0%)
Chart: 
| 1 | 1.01 | 1.02 | 1.03 | 1.04 | 1.05 | 1.06 | 1.07 | 1.08 | 1.0900000000000001 | 1.1000000000000001 | 1.1100000000000001 | 1.1200000000000001 | 1.1300000000000001 | 1.1400000000000001 | 1.1500000000000001 | 1.1600000000000001 | 1.1700000000000002 | 1.1800000000000002 | 1.1900000000000002 | 1.2000000000000002 | 1.2100000000000002 | 1.2200000000000002 | 1.2300000000000002 | 1.2400000000000002 | 1.2500000000000002 | 1.2600000000000002 | 1.2700000000000002 | 1.2800000000000002 | 1.2900000000000003 | 1.3000000000000003 | 1.3100000000000003 | 1.3200000000000003 | 1.3300000000000003 | 1.3400000000000003 | 1.3500000000000003 | 1.3600000000000003 | 1.3700000000000003 | 1.3800000000000003 | 1.3900000000000003 | 1.4000000000000004 | 1.4100000000000004 | 1.4200000000000004 | 1.4300000000000004 | 1.4400000000000004 | 1.4500000000000004 | 1.4600000000000004 | 1.4700000000000004 | 1.4800000000000004 | 1.4900000000000004 | 1.5000000000000004
m=0 | 0.0001092 | 0.0001274 | 0.0001274 | 0.0001456 | 0.0001638 | 0.0001638 | 0.000182 | 0.0002002 | 0.0002002 | 0.00021839 | 0.00023659 | 0.00025479 | 0.00025479 | 0.00027299 | 0.00029119 | 0.00030939 | 0.00032759 | 0.00034579 | 0.00036399 | 0.00038219 | 0.00040039 | 0.00043679 | 0.00045499 | 0.00047319 | 0.00049139 | 0.00052779 | 0.00056419 | 0.00058239 | 0.00061878 | 0.00065518 | 0.00069158 | 0.00072798 | 0.00078258 | 0.00083718 | 0.00089178 | 0.00096458 | 0.0010374 | 0.0011102 | 0.0012194 | 0.0013286 | 0.0014742 | 0.0016562 | 0.0018928 | 0.0021293 | 0.0023659 | 0.0024751 | 0.0023659 | 0.0019656 | 0.00085538 | 0 | 0
m=1 | 0.0001092 | 0.0001274 | 0.0001274 | 0.0001456 | 0.0001638 | 0.0001638 | 0.000182 | 0.0002002 | 0.0002002 | 0.00021839 | 0.00023659 | 0.00025479 | 0.00025479 | 0.00027299 | 0.00029119 | 0.00030939 | 0.00032759 | 0.00034579 | 0.00036399 | 0.00038219 | 0.00040039 | 0.00043679 | 0.00045499 | 0.00047319 | 0.00049139 | 0.00052779 | 0.00056419 | 0.00058239 | 0.00061878 | 0.00065518 | 0.00069158 | 0.00072798 | 0.00078258 | 0.00083718 | 0.00089178 | 0.00096458 | 0.0010374 | 0.0011102 | 0.0012194 | 0.0013286 | 0.0014742 | 0.0016562 | 0.0018928 | 0.0021293 | 0.0023659 | 0.0024751 | 0.0023659 | 0.0019656 | 0.00085538 | 0 | 0
m=2 | 0.0001092 | 0.0001274 | 0.0001274 | 0.0001456 | 0.0001638 | 0.0001638 | 0.000182 | 0.0002002 | 0.0002002 | 0.00021839 | 0.00023659 | 0.00025479 | 0.00025479 | 0.00027299 | 0.00029119 | 0.00030939 | 0.00032759 | 0.00034579 | 0.00036399 | 0.00038219 | 0.00040039 | 0.00043679 | 0.00045499 | 0.00047319 | 0.00049139 | 0.00052779 | 0.00056419 | 0.00058239 | 0.00061878 | 0.00065518 | 0.00069158 | 0.00072798 | 0.00078258 | 0.00083718 | 0.00089178 | 0.00096458 | 0.0010374 | 0.0011102 | 0.0012194 | 0.0013286 | 0.0014742 | 0.0016562 | 0.0018928 | 0.0021293 | 0.0023659 | 0.0024751 | 0.0023659 | 0.0019656 | 0.00085538 | 0 | 0
m=3 | 0.0001092 | 0.0001274 | 0.0001274 | 0.0001456 | 0.0001638 | 0.0001638 | 0.000182 | 0.0002002 | 0.0002002 | 0.00021839 | 0.00023659 | 0.00025479 | 0.00025479 | 0.00027299 | 0.00029119 | 0.00030939 | 0.00032759 | 0.00034579 | 0.00036399 | 0.00038219 | 0.00040039 | 0.00043679 | 0.00045499 | 0.00047319 | 0.00049139 | 0.00052779 | 0.00056419 | 0.00058239 | 0.00061878 | 0.00065518 | 0.00069158 | 0.00072798 | 0.00078258 | 0.00083718 | 0.00089178 | 0.00096458 | 0.0010374 | 0.0011102 | 0.0012194 | 0.0013286 | 0.0014742 | 0.0016562 | 0.0018928 | 0.0021293 | 0.0023659 | 0.0024751 | 0.0023659 | 0.0019656 | 0.00085538 | 0 | 0
m=10 | 0.0001092 | 0.0001274 | 0.0001274 | 0.0001456 | 0.0001638 | 0.0001638 | 0.000182 | 0.0002002 | 0.0002002 | 0.00021839 | 0.00023659 | 0.00025479 | 0.00025479 | 0.00027299 | 0.00029119 | 0.00030939 | 0.00032759 | 0.00034579 | 0.00036399 | 0.00038219 | 0.00040039 | 0.00043679 | 0.00045499 | 0.00047319 | 0.00049139 | 0.00052779 | 0.00056419 | 0.00058239 | 0.00061878 | 0.00065518 | 0.00069158 | 0.00072798 | 0.00078258 | 0.00083718 | 0.00089178 | 0.00096458 | 0.0010374 | 0.0011102 | 0.0012194 | 0.0013286 | 0.0014742 | 0.0016562 | 0.0018928 | 0.0021293 | 0.0023659 | 0.0024751 | 0.0023659 | 0.0019656 | 0.00085538 | 0 | 0
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te | nz0
5 | 1.45*10^3 | 2*pi*10^6 | 1*10^12 | 12 | 2.1
fM = 1 MHz
Results consistent with K. Matsumoto et al. Plasma Phys. 25 (1983) and V.Stefan, Phys. Fluids, 26 (1983)

## Slide 44: EAST – CASE1 Δnz = 5 (Δnz0 = 5%)
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te | nz0
5 | 1.45*10^3 | 2*pi*10^6 | 1*10^12 | 12 | 2.1
Chart: 
fM = 1 MHz
k_perp

## Slide 45: EAST – CASE1 Δnz = 5 (Δnz0 = 10%)
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te | nz0
5 | 1.45*10^3 | 2*pi*10^6 | 1*10^12 | 12 | 2.1
Chart: 
fM = 1 MHz

## Slide 46: EAST – CASE1 Δnz = 10 (Δnz0 = 10%)
Chart: 
| 9 | 9.0500000000000007 | 9.1000000000000014 | 9.1500000000000021 | 9.2000000000000028 | 9.2500000000000036 | 9.3000000000000043 | 9.350000000000005 | 9.4000000000000057 | 9.4500000000000064 | 9.5000000000000071 | 9.5500000000000078 | 9.6000000000000085 | 9.6500000000000092 | 9.7000000000000099 | 9.7500000000000107 | 9.8000000000000114 | 9.8500000000000121 | 9.9000000000000128 | 9.9500000000000135 | 10 | 10.050000000000001 | 10.1 | 10.15 | 10.1999999999999 | 10.25 | 10.3 | 10.35 | 10.4 | 10.4499999999999 | 10.5 | 10.55 | 10.6 | 10.65 | 10.6999999999999 | 10.75 | 10.8 | 10.85 | 10.9 | 10.9499999999999 | 11 | 11.05 | 11.1 | 11.15 | 11.1999999999999 | 11.25 | 11.3 | 11.35 | 11.4 | 11.4499999999999 | 11.5
0 | 0 | 2.9605e-05 | 5.9209e-05 | 0.00011842 | 0.00014802 | 0.00017763 | 0.00020723 | 0.00026644 | 0.00029605 | 0.00035526 | 0.00038486 | 0.00044407 | 0.00050328 | 0.00053289 | 0.00059209 | 0.00068091 | 0.00074012 | 0.00079933 | 0.00088814 | 0.00097696 | 0.0010658 | 0.0011842 | 0.0013322 | 0.0014506 | 0.0016283 | 0.0018355 | 0.0021019 | 0.0024276 | 0.0028421 | 0.0033453 | 0.0037302 | 0.0038486 | 0.0034638 | 0.0021611 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 8.8814e-05 | 0.00014802 | 0.00017763 | 0.00023684 | 0.00029605 | 0.00032565 | 0.00038486 | 0.00047368 | 0.00053289 | 0.0006217 | 0.00071051 | 0.00085854 | 0.0010066 | 0.001273 | 0.0016283 | 0.0020723 | 0.0019243 | 0 | 0 | 0 | 5.9209e-05 | 0.00035526 | 0.00059209 | 0.00079933 | 0.0010066 | 0.0012434 | 0.0015098 | 0.0018355 | 0.0022204 | 0.0027236 | 0.0031973 | 0.0033157 | 0.0028717 | 0.0010362 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.0010066 | 0.0017467 | 0.0016875 | 0 | 0 | 0
2 | 0.00017763 | 0.00023684 | 0.00029605 | 0.00035526 | 0.00041447 | 0.00047368 | 0.00056249 | 0.0006217 | 0.00074012 | 0.00085854 | 0.00097696 | 0.0011546 | 0.0013914 | 0.0017171 | 0.0021908 | 0.0026052 | 0.002546 | 0.001273 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00023684 | 0.00056249 | 0.00091775 | 0.0013026 | 0.0018059 | 0.0023684 | 0.0025756 | 0.0020131 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00026644 | 0.00079933 | 0.0013618 | 0.0020131 | 0.0024572 | 0.0023388 | 0.00085854 | 0 | 0
3 | 0.00023684 | 0.00026644 | 0.00032565 | 0.00038486 | 0.00047368 | 0.00053289 | 0.0006217 | 0.00071051 | 0.00079933 | 0.00094735 | 0.0010954 | 0.001273 | 0.0015394 | 0.0018947 | 0.0023684 | 0.0027828 | 0.0027236 | 0.0016579 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00014802 | 0.00059209 | 0.001125 | 0.0017467 | 0.0020427 | 0.0013026 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5.9209e-05 | 0.00041447 | 0.00079933 | 0.0012138 | 0.0017171 | 0.0023092 | 0.002694 | 0.002546 | 0.001273 | 0 | 0
4 | 0.00023684 | 0.00029605 | 0.00035526 | 0.00041447 | 0.00047368 | 0.00056249 | 0.0006513 | 0.00074012 | 0.00085854 | 0.00097696 | 0.001125 | 0.0013322 | 0.0015987 | 0.0019835 | 0.0024572 | 0.0028717 | 0.0028124 | 0.0018059 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00059209 | 0.0013026 | 0.0016579 | 0.00071051 | 0 | 0 | 0 | 0 | 0 | 0 | 2.9605e-05 | 0.00035526 | 0.0006513 | 0.00097696 | 0.0013914 | 0.0018651 | 0.0024276 | 0.0028124 | 0.0026348 | 0.0014506 | 0 | 0
5 | 0.00026644 | 0.00029605 | 0.00035526 | 0.00041447 | 0.00050328 | 0.00056249 | 0.0006513 | 0.00074012 | 0.00085854 | 0.0010066 | 0.0011546 | 0.0013618 | 0.0016283 | 0.0020131 | 0.0025164 | 0.0029013 | 0.0028717 | 0.0018651 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00017763 | 0.00094735 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00020723 | 0.00047368 | 0.00076972 | 0.0010658 | 0.0014506 | 0.0019539 | 0.0024868 | 0.0028717 | 0.002694 | 0.0015098 | 0 | 0
10 | 0.00026644 | 0.00032565 | 0.00038486 | 0.00044407 | 0.00050328 | 0.00059209 | 0.00068091 | 0.00076972 | 0.00088814 | 0.0010362 | 0.0011842 | 0.001421 | 0.0016875 | 0.0020723 | 0.002546 | 0.0029605 | 0.0029309 | 0.0019539 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00074012 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00017763 | 0.00041447 | 0.0006513 | 0.00088814 | 0.0011842 | 0.0015691 | 0.0020427 | 0.0025756 | 0.0029309 | 0.0027532 | 0.0016283 | 0 | 0
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te | nz0
10 | 1.45*10^3 | 2*pi*10^6 | 1*10^12 | 12 | 2.1
fM = 1 MHz
k_perp

## Slide 47: EAST – CASE1 Δnz = 5 (Δnz0 = 0% – 5% – 10%)
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 10
caso 1 - 10% nz = 5 | 1 | 0.86765 | 0.68382 | 0.73529 | 0.75 | 0.76471 | 0.77941
caso 1 - 5% nz = 5 | 1 | 0.86765 | 0.68382 | 0.73529 | 0.77941
caso 1 - 0% nz = 5 | 1 | 1 | 1 | 1 | 1
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te | nz0
5 | 1.45*10^3 | 2*pi*10^6 | 1*10^12 | 12 | 2.1
fM = 1 MHz

## Slide 48: EAST – CASE1 (Δnz0 = 10%) Δnz = 5 vs Δnz =10
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 10
caso 1 - 10% nz = 5 | 1 | 0.86765 | 0.68382 | 0.73529 | 0.75 | 0.76471 | 0.77941
caso 1 - 10% nz = 10 | 1 | 0.86154 | 0.67692 | 0.72308 | 0.74615 | 0.75385 | 0.76923
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te | nz0
5 | 1.45*10^3 | 2*pi*10^6 | 1*10^12 | 12 | 2.1
10 | 1.45*10^3 | 2*pi*10^6 | 1*10^12 | 12 | 2.1
fM = 1 MHz
Now the growth rate reduction
seems almost insensitive to N//
variation!

## Slide 49: EAST – CASE1 vs CASE2 Δnz = 10 (Δnz0 = 10%)
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te | nz0
10 | 1.45*10^3 | 2*pi*10^6 | 1*10^12 | 12 | 2.1
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 10
Caso 1 | 1 | 0.86154 | 0.67692 | 0.72308 | 0.74615 | 0.75385 | 0.76923
Caso 2 | 1 | 0.86154 | 0.67692 | 0.72308 | 0.73846 | 0.75385 | 0.76923
fM = 1 MHz

## Slide 50: EAST – CASE1 (Δnz0 = 5% - 10%) m=2 vs modulation frequency
Chart: 
| 1000000 | 100000 | 1000
caso1_10%_m=2 | 1 | 1 | 0.98864
caso1_5%_m=2 | 1 | 1 | 1 | 1
(c/ω0)k// | Pden (m=0) | deltaf_M | ne | Te | nz0
10 | 1.45*10^3 | 10^3 – 10^6 | 1*10^12 | 12 | 2.1
fM = 1 kHz – 1 MHz
fM

## Slide 51: FTU - breakthrough
(c/ω0)k// | Pden (m=0) | ne | Te | nz0
10 | 3.06E+03 | 2*10^12 | 10 | 2
(c/ω0)k// | delta_fo (MHz) | delta_nzo | kperp
10 | 0 | 0% | 12.627472
10 | -1 | 0% | 12.635479
10 | 1 | 0% | 12.619451
10 | -1 | -10% | 13.468361
10 | 1 | 10% | 11.78765
10 | -1 | 10% | 11.802597
10 | 1 | -10% | 13.451252
Case 1 | 
Case 2 | 

## Slide 52: FTU – CASE1 Δnz = 10 (Δnz0 = 10%)
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te | nz0
10 | 3.06E+03 | 2*pi*10^6 | 2*10^12 | 10 | 2
fM = 1 MHz
Chart: 
| 11.4 | 11.450000000000001 | 11.500000000000002 | 11.550000000000002 | 11.600000000000003 | 11.650000000000004 | 11.700000000000005 | 11.750000000000005 | 11.800000000000006 | 11.850000000000007 | 11.900000000000007 | 11.950000000000008 | 12.000000000000009 | 12.05000000000001 | 12.10000000000001 | 12.150000000000011 | 12.200000000000012 | 12.250000000000012 | 12.300000000000013 | 12.350000000000014 | 12.400000000000015 | 12.450000000000015 | 12.500000000000016 | 12.550000000000017 | 12.600000000000017 | 12.650000000000018 | 12.700000000000019 | 12.75000000000002 | 12.80000000000002 | 12.850000000000021 | 12.900000000000022 | 12.950000000000022 | 13.000000000000023 | 13.050000000000024 | 13.100000000000025 | 13.150000000000025 | 13.200000000000026 | 13.250000000000027 | 13.300000000000027 | 13.350000000000028 | 13.400000000000029 | 13.450000000000029 | 13.50000000000003 | 13.550000000000031 | 13.600000000000032 | 13.650000000000032 | 13.700000000000033 | 13.750000000000034 | 13.800000000000034 | 13.850000000000035 | 13.900000000000036
m=0 | 0.00043961 | 0.00046709 | 0.00052204 | 0.00057699 | 0.00063194 | 0.00068689 | 0.00074184 | 0.00082427 | 0.00087922 | 0.00096165 | 0.0010716 | 0.001154 | 0.0012639 | 0.0014013 | 0.0015386 | 0.001731 | 0.0019233 | 0.0021706 | 0.0024453 | 0.0027201 | 0.0029674 | 0.0030773 | 0.0030223 | 0.0027201 | 0.0020882 | 2.7476e-05 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
m=1 | 0.00082427 | 0.00098913 | 0.0011815 | 0.0014287 | 0.001676 | 0.0016485 | 0.001154 | 0 | 0 | 0 | 0.00021981 | 0.00043961 | 0.00063194 | 0.0007968 | 0.00098913 | 0.0011815 | 0.0014013 | 0.0016485 | 0.0019233 | 0.0022255 | 0.0025003 | 0.0026377 | 0.0025827 | 0.0022805 | 0.0014562 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00041214 | 0.0010716 | 0.0014013 | 0.0013188 | 0.00054951 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
m=2 | 0.0011265 | 0.0013188 | 0.0015936 | 0.0018684 | 0.0020882 | 0.0020882 | 0.0017859 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00027476 | 0.00054951 | 0.00082427 | 0.0011265 | 0.0014837 | 0.0018134 | 0.0020332 | 0.0019783 | 0.0015661 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00013738 | 0.00057699 | 0.00098913 | 0.0014287 | 0.0017859 | 0.0019508 | 0.0018409 | 0.0012914 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
m=3 | 0.0012364 | 0.0014562 | 0.001731 | 0.0020057 | 0.0022255 | 0.002253 | 0.0019508 | 0.0010716 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00013738 | 0.00049456 | 0.00087922 | 0.0012914 | 0.0015661 | 0.0015386 | 0.00096165 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2.7476e-05 | 0.00035718 | 0.00065942 | 0.00096165 | 0.0013188 | 0.0017035 | 0.0020057 | 0.0021431 | 0.0020332 | 0.0015112 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
m=4 | 0.0012914 | 0.0015112 | 0.0017859 | 0.0020882 | 0.0022805 | 0.002308 | 0.0020332 | 0.0012089 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00043961 | 0.0009067 | 0.0012639 | 0.0012364 | 0.00046709 | 0 | 0 | 0 | 0 | 0 | 0 | 2.7476e-05 | 0.00030223 | 0.00054951 | 0.00082427 | 0.0011265 | 0.0014562 | 0.0018134 | 0.0021156 | 0.0022255 | 0.0021156 | 0.0016211 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
m=5 | 0.0013188 | 0.0015386 | 0.0018134 | 0.0021156 | 0.0023354 | 0.0023354 | 0.0020607 | 0.0012639 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5.4951e-05 | 0.00060447 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00019233 | 0.00041214 | 0.00065942 | 0.0009067 | 0.0012089 | 0.0015386 | 0.0018684 | 0.0021431 | 0.0022805 | 0.0021431 | 0.0016485 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
m=10 | 0.0013463 | 0.0015936 | 0.0018684 | 0.0021431 | 0.0023629 | 0.0023904 | 0.0021156 | 0.0013463 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00043961 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00019233 | 0.00038466 | 0.00057699 | 0.0007968 | 0.0010166 | 0.0012914 | 0.0016211 | 0.0019508 | 0.0022255 | 0.0023354 | 0.0021981 | 0.0017035 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
k_perp

## Slide 53: FTU – CASE2 Δnz = 10 (Δnz0 = 10%)
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te | nz0
10 | 3.06E+03 | 2*pi*10^6 | 2*10^12 | 10 | 2
fM = 1 MHz
k_perp
Chart: 
| 11.4 | 11.450000000000001 | 11.500000000000002 | 11.550000000000002 | 11.600000000000003 | 11.650000000000004 | 11.700000000000005 | 11.750000000000005 | 11.800000000000006 | 11.850000000000007 | 11.900000000000007 | 11.950000000000008 | 12.000000000000009 | 12.05000000000001 | 12.10000000000001 | 12.150000000000011 | 12.200000000000012 | 12.250000000000012 | 12.300000000000013 | 12.350000000000014 | 12.400000000000015 | 12.450000000000015 | 12.500000000000016 | 12.550000000000017 | 12.600000000000017 | 12.650000000000018 | 12.700000000000019 | 12.75000000000002 | 12.80000000000002 | 12.850000000000021 | 12.900000000000022 | 12.950000000000022 | 13.000000000000023 | 13.050000000000024 | 13.100000000000025 | 13.150000000000025 | 13.200000000000026 | 13.250000000000027 | 13.300000000000027 | 13.350000000000028 | 13.400000000000029 | 13.450000000000029 | 13.50000000000003 | 13.550000000000031 | 13.600000000000032 | 13.650000000000032 | 13.700000000000033 | 13.750000000000034 | 13.800000000000034 | 13.850000000000035 | 13.900000000000036
m=0 | 0.00043961 | 0.00046709 | 0.00052204 | 0.00057699 | 0.00063194 | 0.00068689 | 0.00074184 | 0.00082427 | 0.00087922 | 0.00096165 | 0.0010716 | 0.001154 | 0.0012639 | 0.0014013 | 0.0015386 | 0.001731 | 0.0019233 | 0.0021706 | 0.0024453 | 0.0027201 | 0.0029674 | 0.0030773 | 0.0030223 | 0.0027201 | 0.0020882 | 2.7476e-05 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
m=1 | 0.00082427 | 0.00098913 | 0.0011815 | 0.0014287 | 0.001676 | 0.0016485 | 0.001154 | 0 | 0 | 0 | 0.00021981 | 0.00043961 | 0.00063194 | 0.0007968 | 0.00098913 | 0.0011815 | 0.0014013 | 0.0016485 | 0.0019233 | 0.0022255 | 0.0025003 | 0.0026377 | 0.0025827 | 0.0022805 | 0.0014562 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00041214 | 0.0010716 | 0.0014013 | 0.0013188 | 0.00054951 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
m=2 | 0.0011265 | 0.0013188 | 0.0015936 | 0.0018684 | 0.0020882 | 0.0020882 | 0.0017859 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00027476 | 0.00054951 | 0.00082427 | 0.0011265 | 0.0014837 | 0.0018134 | 0.0020332 | 0.0019783 | 0.0015661 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00013738 | 0.00057699 | 0.00098913 | 0.0014287 | 0.0017859 | 0.0019508 | 0.0018409 | 0.0012914 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
m=3 | 0.0012364 | 0.0014562 | 0.001731 | 0.0020057 | 0.0022255 | 0.002253 | 0.0019508 | 0.0010716 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00013738 | 0.00049456 | 0.00087922 | 0.0012914 | 0.0015661 | 0.0015386 | 0.00096165 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2.7476e-05 | 0.00035718 | 0.00065942 | 0.00096165 | 0.0013188 | 0.0017035 | 0.0020057 | 0.0021431 | 0.0020332 | 0.0015112 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
m=4 | 0.0012914 | 0.0015112 | 0.0017859 | 0.0020882 | 0.0022805 | 0.002308 | 0.0020332 | 0.0012089 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00043961 | 0.0009067 | 0.0012639 | 0.0012364 | 0.00046709 | 0 | 0 | 0 | 0 | 0 | 0 | 2.7476e-05 | 0.00030223 | 0.00054951 | 0.00082427 | 0.0011265 | 0.0014562 | 0.0018134 | 0.0021156 | 0.0022255 | 0.0021156 | 0.0016211 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
m=5 | 0.0013188 | 0.0015386 | 0.0018134 | 0.0021156 | 0.0023354 | 0.0023354 | 0.0020607 | 0.0012639 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 5.4951e-05 | 0.00060447 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00019233 | 0.00041214 | 0.00065942 | 0.0009067 | 0.0012089 | 0.0015386 | 0.0018684 | 0.0021431 | 0.0022805 | 0.0021431 | 0.0016485 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
m=10 | 0.0013463 | 0.0015936 | 0.0018684 | 0.0021431 | 0.0023629 | 0.0023904 | 0.0021156 | 0.0013463 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00043961 | 0 | 0 | 0 | 0 | 0 | 0 | 0.00019233 | 0.00038466 | 0.00057699 | 0.0007968 | 0.0010166 | 0.0012914 | 0.0016211 | 0.0019508 | 0.0022255 | 0.0023354 | 0.0021981 | 0.0017035 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 54: FTU – CASE1 vs CASE2 Δnz = 10 (Δnz0 = 10%)
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 10
caso1_10% | 1 | 0.85714 | 0.67857 | 0.73214 | 0.75 | 0.75893 | 0.77679
caso2_10% | 1 | 0.85714 | 0.67857 | 0.73214 | 0.75 | 0.75893 | 0.77679
(c/ω0)k// | Pden (m=0) | omega_M | ne | Te | nz0
10 | 3.06E+03 | 2*pi*10^6 | 2*10^12 | 10 | 2
fM = 1 MHz