## Slide 1: Maximum peaking by impurity injection
FTU experimental campaign 2019 - program F04 Impurity Injection
Scientific Coordinators: C.Mazzotta, G.Pucella
Scientific team: G.Aruzzese, F.Bombarda, L.Boncagni, L.Carraro, O.D’Arcangelo, D.Frigione, L.Gabellieri, E.Giovannozzi, M.Marinucci, M.E.Puiatti, A.Romano, O.Tudisco, et al.
C.Mazzotta
WIP 1th Apr 2019

## Slide 2: Impact of peaking on fusion power Angioni EPS 2009
Pressure profile peaking increases with increasing density peaking (decreasing collisionality ) [Angioni PPCF 09]
Impact of peaked density profile on impurity transport, MHD and fast particle instabilities under assessment
In a reactor, operation above density limit possible, thanks to density peaking
Projection from JET profiles, at predicted density peaking, increase of fusion power by ~30% with respect to flat density [Weisen PPCF 06]
[ Weisen PPCF 06 ]
Fixed b and
Greenwald fraction
No (inverse) correlation observed between density peaking and temperature peaking [AUG Angioni PoP 03, JET Weisen PPCF 06, JT-60U Takenaga NF 08]
2

## Slide 3: Outline
Historical excursus by K.A. Razumova at EPS 2017 self-organized plasma
  Dependence of stored energy with electron density - Helium and Neon puffing
Alcator summary by A. Hubbard EPS 2017 I and H-mode plasmas at high BT and P Implications for future fusion devices. Extrapolations, open issues, and needed research
Impurity Injection in T-10 N. Kirneva EPS 2017 Helium and Neon doped plasmas
FTU behavior in terms of density limit, peaking, ITB and collisionality Pucella 2015, Mazzotta NF 2015 e EPS 2017, in the past Frigione and more…
  Impurity Injection in T-10 N. Kirneva EPS 2017 Helium and Neon doped plasmas
  Density peaking with Neon Mazzotta FTU 2014-2018, Frigione JET 2018
  JET hybrid plasmas Neon scan Frigione NF 2019
Conclusions and FTU experimental proposal for the next campaign
ALFVEN PRIZE

## Slide 4: Not only FTU… W(ne) or ne(W)? Razumova EPS 2017 and Plasma Physics Report 2017
With He injection, plasma density may increase without changes in confinement.
There is no dependence of confinement on plasma density. We have confused the reason and the consequence. The plasma density depends on confinement.

## Slide 5: Not only FTU… Alcator summary Hubbard EPS 2017

## Slide 6: Not only FTU… Alcator summary Hubbard EPS 2017

## Slide 7: Not only FTU… Effect of the Impurity Injection on plasma confinement in T-10 tokamak Kirneva EPS 2017

## Slide 8
He & Ne combined doping Kirneva EPS 2017

## Slide 9
Helium doping Kirneva EPS 2017

## Slide 10
Neon doping Kirneva EPS 2017

## Slide 11
He & Ne combined doping Kirneva EPS 2017

## Slide 12: FTU Density limit and peaking Pucella, Tudisco, Mazzotta et al.
At the first order, the shape of the density profile on FTU depends on the central line-averaged density and, for a given central line-averaged density, it depends on the plasma current, and it does not depend on the toroidal magnetic field. Finally the peaking factor at the disruption linearly depends on the edge safety factor q.
The experiments on FTU highlights the edge nature of the density limit, as a holds for the maximum achievable line-averaged density along a peripheral chord, whilst Greenwald-like scaling is not valid for the central chord, where the maximum achievable line-averaged density essentially depends on the toroidal magnetic field only. This behavior is explained in terms of density profile effects. [Pucella NF 13]
12

## Slide 13: FTU peaking with Neon injection Mazzotta, Pucella, Tudisco et al
Major Radius (m)
ne (1020 m-3)
0.5s
ρ
Te (keV)
1.2s
0.5s
#37342
#37344
time (s)
ne (1019 m-3)
#37342 Neon injection at 0.6 s
#37344 D puffing only
ne 0/< ne >vol
1.2 s
#37342 has 50 ms Neon puff at 0.6 s (the D fuelling is off) provokes a spontaneous increase of the density and peaking [Mazzotta NF 15]
Spectroscopic evaluation: a small fraction of electrons stripped from Neon can contribute to the density rise. [Mazzotta EPS 13]
From JETTO: the Neon impurity induces a decrease of the ion thermal diffusivity coefficient due to the suppression of the turbulent component of the ion transport, but leaves the electron energy transport unchanged. [Mazzotta NF 15]

## Slide 14: Density peaking observed to increase with decreasing collisionality in H-mode plasmas Angioni EPS 2009
Statistical analyses identify collisionality as the most relevant parameter
Consistent observations in
AUG [ Angioni PRL 03 ]
JET [ Weisen NF 05 ]
C-Mod [ Greenwald NF 07 ]
and JT-60U [ Takenaga NF 08 ]
14
[Angioni PPCF 09]

## Slide 15: FTU collisionality Mazzotta EPS 2017, Tudisco FED 2010, M.Romanelli PPCF 2007
Statistical analyses identify collisionality as the most relevant parameter
Consistent observations in
AUG [ Angioni PRL 03 ]
JET [ Weisen NF 05 ]
C-Mod [ Greenwald NF 07 ]
and JT-60U [ Takenaga NF 08 ]
FTU
15
FTU [ Mazzotta EPS 17,
Tudisco FED 10
M.Romanelli PPCF 2007 ]

## Slide 16: FTU collisionality Mazzotta EPS 2017
FTU
37342 Neon doped
37344 Undoped
FTU [ Mazzotta EPS 17, NF 2015 ]
16

## Slide 17: JET Frigione NF 2019
A Neon scan was performed in JET Hybrid plasmas to study impurity seeding technique for power exhaust mitigation (reducing the divertor tile temperature without affecting the global confinement).
The fusion performance represented by the total neutron yield was reduced.
The core electron density profiles featured a peaking effect increasing with Ne injected.
The peaking is reproduced if a particle pinch to ZEFF and grad Ti is introduced as (ITG) theory.
Further experimental activity is planned to extend this study in the baseline scenario
17
#90287
un-seeded
#90280 seeded
t2=6.5s
t1=4.9s
t2=6.6s
t1=4.9s
1.4 MA, 1.9 T
#90280 seeded
#90287 un-seeded

## Slide 18: FTU experiments: possible goals for combined doping Ne + He
We can confirm the T-10 results
We can reach higher peaking (and improved density limit ?)
We can delay the MHD activity and disruption
We can understand better the MARFE dynamic
We can obtain pressure record
We can confirm (or not) the saturation of τE
We can better understand the collisionality role
We can confirm neutron rate and energy behaviour
We can study the particle transport in the ITB to assess the role of the ETG and the absence of TEM
Or are the ITG?
More… what happen if I heat in the gradient region?

## Slide 19
ne (1020 m-3)
dBθ/dt (T/s)
time (s)
#37340 V-on 90mV
#37341 V-on 85mV
#37342 V-on 82mV
Conclusions: what we know about Neon injection
more impurity is injected more disruptive MHD activity is observed
strong increase of the electron density for the Neon seeded discharges, also the density peaking factors were found to be in excess of three
at higher starting density, the same injected impurity amount induces an abrupt density rise and the discharge rapidly ends in a disruption (right fig.)
Our neutron rate increase, as well as τE
The combinations He before Ne and Ne before He must be explored at leaste once. The confinement could be different.
More: we can consider the possibility to have the He/D fuel mixture. In this case we have to assess the reference scenario
Proposal for: before Helium and after Neon combined injection
Experimental proposal for combined doping Ne + He

## Slide 20
As current increases the induced density rise is less steep and the peaking effect is milder
At 700 kA, no disruption. It’s interesting to get a long pulse…
Proposal for: Helium and Neon combined injection
Experimental proposal Ne + He (or one doping alnone): Current Scan
Also in this case, the combinations He before Ne, and Ne before He must be explored at least once.
What happen if I heat in the gradient region?

## Slide 21
THE END ?

## Slide 22
W(ne) or ne(W)? Razumova EPS 2017
W(ne) or ne(W)? W(ne) or ne(W)? W(ne) or ne(W)?
With Ne injection, strong changes in the stored energy Wd lead to low changes in the plasma density ne