## Slide 1: Tungsten spectral identification and transport in FTU plasmas: W LBO injection
G.Apruzzese, F.Bombarda, L.Carraro, F. Cordella, L.Gabellieri, M O’Mullane, G. Pucella, M.E. Puiatti, A.Romano, M.Valisa, B.Zaniol

## Slide 2
Tungsten is to be used as plasma facing material on future
machines and is presently being tested on existing experiments
Spectral identification of W line emission ( ADAS atomic database)
To assess if W accumulates, comparison with lighter element Ni ( W transport code not available)
THE MOTIVATION IS TWOFOLD

## Slide 3
Background
PLT, ASDEX-U, LHD, JET, RFX-mod, as well as FTU, recorded quasi continuum bands of W in the spectral regions of 20-40 and 45-65 Angstrom.
W transport properties can be qualified from time history and space distribution of its emission ( lines, Prad, SXR)
LHD

## Slide 4
W emission Features have been identified in FTU C1-A April 2019 campaign
42614
perturbations of Te make very difficult the W transport analysis : Te decrease dominates SXR (t)

## Slide 5
Goals and experimental strategy
The W emission bands result from overlapping of the emission from several ionizations states, therefore a well resolved identification of W spectrum in those spectral regions would be of great interest in order to increase the confidence on the atomic physics models ( M.O’Mullane ADAS) => use of SOXMOS spectrometer on loan from Padova ( 2 gratings: 600g/mm and higher resolution 1200 g/mm)
SXR tomography would contribute to the radial localization of the W emission.
The W penetration into the core plasma and its accumulation can be determined by analyzing the time evolution and radial profiles of SXR, Prad and by tilting the SPRED LoS.
Injection of Ni in comparable discharges would add the possibility of comparing transport properties of impurities with different mass and charge, ( 1-dim transport code for Ni available , NOT AVAILABLE FOR W)

## Slide 6
EXPERIMENTAL STRATEGY and REQUIREMENTS
‘Short ‘ discharges ( 1.s) : inject W with LBO at 0.4/0.5 s
At High Te ( ECRH in the core) (stationary conditions, to be discussed with Ec group )
-Collect spectra with SOXMOS 600 g/mm grating
-Repeat with 1200g/mm to better resolve lines in the emission feature.
-Tilt the SPRED to compare core and edge emission behaviors vs time.
-Repeat (partially ) with Ni injection
ne (1020 particles m-3) 0.5 (to be checked with EC group)
B (T) 5.3
I (kA) 500
Special requirements
change of SOXMOS spectral range and grating (access to the torus hall)
ECRH for maximum Te
Essential diagnostics
SOXMOS, SPRED
ne, Te profiles,
SXR Tomography profiles
Visible Bremsstrahlung, Visible spectroscopy

## Slide 7
Pulse Plan ( total 10 shots)
Ip 500 kA Bt=5.3 T ,ECRH ne=0.5 10 20m-3
W quasi continuum 40-70 Å shot
600g/mm y=155 (36-65 A) 1 check of W quantity
Repeate with different LBO diaphragm 1 SCAN THE SPRED POSITION
Y=160
W quasi continuum 20-40 Å
600 g/mm y=120 (15-40) with different LBO diaphragm 1 check of W quantity
Repeat Y=115, or 125 , check the feature ends 1
W quasi continuum 40-70 Å
1200 g/mm Y=210 (37-57), 230 (45-67) 2 SCAN THE SPRED POSITION
W quasi continuum 20-40 Å
1200 g/mm y=160 (20-36) , y=170 (23-40) 2
Repeat ( partially) with LBO Ni 2 SCAN THE SPRED POSITION
  SOXMOS wavelength scan (600g/mm)
  y=230(87-131) Ni XXI 96, XXII 103, XXIII 111, XXIV 104, XXV 118
  Y=360(229-296), Ni XV 249, NI XVIII 292)