## Slide 1: FTU 2019 F08 - Elongated Plasmas
Motivations, strategy and pulse plan
Giuseppe Ramogida / FSN-FUSTEC-TES
G. Calabrò, F. Bombarda, L. Boncagni, D. Carnevale, M. Iafrati, R. Lombroni
WIP 17/06/ 2019 - ENEA Frascati

## Slide 2: Motivations and previous results
z [m]
r [m]
Investigation on possible LH transitions, aiming to study the impact of ELMs on the LM limiter
IAEA 2014:
Elongated plasmas (5.5 T, 200kA, k1.2, tpulse  1.5s) with ECW additional heating (500 kW)
Vary local magnetic shear (flux surfaces opening) at the CLL
IAEA 2016:
Ohmic elongated configurations (k1.2) obtained for 3.5s
Since 2012 experiments were carried out, obtaining ohmic elongated configurations (k > 1.2), but it was not possible to investigate H‑mode access due to the lack of enough EC heating

## Slide 3: Reference #37869

## Slide 4: Investigating LH transitions with outer X-point

## Slide 5: Experimental strategy - 2019
Experimental aims
Assess low current, max elongation k>1.2 discharges with LM limiter achievable without loss of vertical control with improved PID
Attempt to observe LH transitions (2.7 T, two gyrotrons required) in k > 1.2 discharges
Compare with circular, standard elongation, discharge, same EC power
LM limiter position scan, same EC power
Density (0.3-0.6 x1020 m-3) scan, same EC power
EC deposition scan
Experimental setup
2.7 T, 250-300 kA, 0.4 x 1020m-3

## Slide 6: Pulse plan
Zero at 2.7 T
2.7 T / 250-300 kA / 0.3-0.4·1020 m-3 with elongation steps
Repeat, if vertical control is lost, tuning parameters
2.7 T / 250-300 kA / 0.3-0.4·1020 m-3 at maximum elongation
2.7 T / 250-300 kA / 0.3-0.4·1020 m-3 / max k with 700 kW EC
2.7 T / 250-300 kA / 0.3-0.4·1020 m-3 / standard k with 700 kW EC
2.7 T / 250-300 kA / 0.3-0.4·1020 m-3 / max k with 700 kW EC, reducing distance from LM limiter
2.7 T / 250-300 kA / 0.3-0.4·1020 m-3 / max k with 700 kW EC, reducing or increasing density

## Slide 7: Technical requests and diagnostics
Technical requirements:
  At least two gyrotrons
  Poloidal limiter inserted
  Liquid Metal limiter as target
  Vertical control parameters should be tuned
  F current limit close to the max value (i.e. 11.5kA)
  Low recycling conditions
Essential diagnostics:
  Magnetics
  H at high voltage when operating at low density
  Interferometer, Michelson, Thomson Scattering
  Edge probes
  Liquid Metal limiter diagnostics