## Slide 1
MAG-2.1-T026-D003: CEA TF WP design
WPMAG Final Meeting, 12th Feb. 2020, Frascati
L. ZANI & CEA team

## Slide 2: Introduction
TF system
  Refine radial plates (RP) TF WP#4 design on 2018 DEMO baseline through working on inputs and upgrading MADMACS-TF tool RP option features (e.g. RP radial thickness, mechanical approach including small FEA mechanical studies…).
  Pre-CDR preparation: for DN, Snowflake and Super-X, establish cross-section of TF coils at the poloidal locations of the VV ports, alternatively: statement that TF coil is infeasible including justification.
  Run MADMACS-TF to carry out optimization loops on DEMO 2018 configuration with impact on TF design of refined input calculations loops (EM map, TH calculation, cryoplant operation optimization…). Provide recommendations on the most valuable flow to proceed with
Task content
not conducted  inputs to be provided

## Slide 3: Methodologic considerations
Recall: WP#4 RP concept remains within the ITER-like approach
No side pancakes
Similar CICC embedding in RPs as ITER approach

## Slide 4: Methodologic considerations
cable
mechanical
FL(r)
etc…
r
Insulation layers
● ground + ins. gap
● inter-plates
● inter-turn
 1 mm
 2 mm
 8 + 10 mm
a
a
a/2
geometry
etc…
EM
BMAX
BMIN
dS
FL(r)
Jacket + RP merged
Ic(Beff) adapted
Objectives: after 2018 DPRM recommendations tentative improvements were considered
increase
decouple r-q
& optimize
Check with FEA
Refined gradient
a/2
a/2

## Slide 5: Methodologic considerations
The design changes were still carried out with CEA tool  MADMACS-TF
The workflow was adapted to allow decorrelating the radial and toroidal RP thicknesses
Image extracted from ITER DDD
Critical zones appear to be in the radial part of the RPs thickness
Toroidal parts of RP thickness seem to be safe
 The FEA will give an answer to this interrogation
This difference might come from the addition of the vault effect and compression
 At pre-design stage a similar approach will be applied for DEMO WP#4
First attempt was to decrease the radial thickness to gain radial built…but…as per ITER DDD…

## Slide 6: Methodologic considerations
The design approach considers a graded radial thickness that can accomodate the possible contrains on the inner parts of the WP#4, with the rules as:
- highest value possible on last turn
- high value on the two previous turns
- low value on other turns, min. ½ max
Tor. thck.
Rad. thck.
The reference design is carried out with overall constrains consistent with the the DEMO 2018 reference baseline for WP#3
- maximum width of WP housing = 1240 mm
(mechanical rationale > outerleg under OOP loads)
- maximum total TF thickness = 1.25 m
(EM rationale > same room for CS > constant flux)
- same maximum field (11.99 T)
The radial thickness pattern was considered in confrontation with ITER one
7
8.5
9
9
DP insulation
RP insulation
lT
lR
lR
Rad. thck.

## Slide 7: WP#4 updated design
As result the WP#4 (upgraded approach) features are below
DEMO 2018 Reference |  | 
TF features | WP#4 | WP#3
Conductor current (kA) | 93242 | 92091
# of SC strands | 831 | 848
# of Cu strands | 996 | 965
Cable dimensions (mm) | 52.9 | 51.6 x 44.9
# of pancakes | 16 | 18
# of turns (regular pancakes) | 10 | 9
Jacket thickness (mm) | 1.5 | 9.3
RP toroidal thickness lT (mm) | 17.2 | -
RP radial thickness lR (mm) | Turns 1~7  6 mm Turns 7~8  11 mm Turn 9  12 mm | -
Casing Tresca stress (MPa) | 623.3 | 629.6
Jacket+RP Tresca stress (MPa) | 616.9 | 620
SC strand amount (t) | 840 | 873
The leftover space for insultation allowed the below features
  Conductor insulation = 0.5 mm
  RP insulation = 1 mm
The SC amount is slightly smaller (~ - 4%) than WP#3
  Similar BEFF effect as for DEMO 2015 comparison
small figures  possible optimization of insulation
 refinement of BEFF calculation

## Slide 8: Updated WP#4 optimization
Conductor insulation
ITER reference
 1.25 mm
DEMO
 1.5 mm
RP insulation
ITER reference
 3 mm
DEMO
 5 mm
All WP#4 features are unchanged, except:
 housing toroidal dimensions
 increase from 1240 to 1310 mm (+ 70 mm)
 outer leg side thickness decrease ( -35 mm over 150 mm)
► consequences on OOP load absorption?
 housing radial dimensions
 increase from 680 to 700 mm (+ 20 mm)
 sCAS increase 623 to 643 MPa (+20 MPa)
 no TF inner boundary change (CS unchanged)
► no strong consequences
the mecanical FEA is expected to give guidelines to identify the upgrades boundaries
FEA carried out on the reference design
Insulation dimension improvement
           see MAG-3.1 presentation

## Slide 9: Updated WP#4 optimization
Electromagnetical representation improvement
 calculate more accurately B gradient with WP#4
With MADMACS-TF model
> linear approach with direct correlation between radial excursion (from machine axis to plasma side) and B variation (from BMAX to zero) DB = 0.88 T BEFF= 11.54 T
DEMO 2018 Reference |  | 
TF features | WP#4 ref | WP#4 + self fied
# of SC strands | 831 | 774
# of Cu strands | 996 | 138
Cable dimensions (mm) | 52.9 | 52.7
SC strand amount (t) | 840 | 783
An improved field determination can save SC amount (~ 7% in simple approach)
An overall precise B map calculation is foreseen with an adapation of CEA tool (TRAPS) to round geometry
With improved approach
> self-field is considered as acting on the most loaded conductor (infinite round cable) exclusively (no grading from other conductors)
DB = 1.43 T BEFF= 11.31 T

## Slide 10: Thermo-hydraulic considerations
First Termo-Hydraulic approach with WP#4 upgraded design
In a first attempt a « first degree check » was conducted to see the difference with WP#3
Simplified calculation hypotheses are as below:
BEFF map is deduced from the WP#3 one (calculated with TRAPS)
THEA only is used
  No interpancake heat flux considerations
  No heat load from casing
  WP heat load calculated with “equivalent squares”
- Optimistic approach
- Comparative trend with WP#3 targeted
DTMARG = 1.74 K
- DTMARG 0.06 K lower than WP#3 in simplified conditions
- WP#3 DTMARG evaluated at 1.62 K in relevant conditions (TACTICS)
- WP#4 DTMARG expected in suitable range with TACTICS
WP#4 TACTICS model to be run
           see MAG-2.2 presentation

## Slide 11: Conclusions - perspectives
Conclusions
  TF WP#4 upgraded design was proposed according to the recommendations of DPRM 2018 panel, with a graded RP concept, within unchanged WP housing.
  Optimisation was attempted, regarding insulation and BEFF calculation. Further investigations on dimensional impact should be evaluated by detailed studies
  First TH analysis is provided, to be followed by another one
Perspectives TS 2020
  Adjustment of WP#4 design according to mechanical FEA
  EM calculation update > transfer to TH
NB: this proposal should be adjusted according to the volume of work (when identified) which is needed for addressing Gate Review documentation

## Slide 12: Thank you for your attention Questions ?