## Slide 1
MAG-2.1-T026-D001: CEA CS WP design
WPMAG Final Meeting, 12th Feb. 2020, Frascati
L. ZANI & CEA team

## Slide 2: Introduction
CS system (~ 0.2 ppy)
  Target flux convergence tentative on the CS 2018 configuration with discussion on the features impacted (Rext, DTMARG, SC material …). If appropriate compare method & outputs from PROCESS with MADMACS-CS ones.
  Propose a reference CEA 2018 CS design out of the previous convergence study.
  Consider inter-modules vertical forces for improving method for CS refined design & limits evaluation (dimensioning of tie plates…)
  Interact with PMI on the flexibility margin of CS height optimization
Task content
CS + PF forces approach merged in the MAG-2.1 PF deliverable

## Slide 3: Methodologic considerations
CS design method
With the previous CS CEA design attempt (TS 2018) the target flux was extracted from PROCESS (611 Wb) with flux evaluated at CS outer edge
specifications were impossible to reach (max Y ~ 600 Wb)
Some room for improvement were identified
The flux is calculated at the edge of the CS, supposing a flat variation of flux outside the CS (~ infinite solenoid)
  It therefore overestimates the flux CS production
The target flux extracted is the total flux consumption (PF + CS) avec the whole scenario, ensuring a conservative assumption
  It therfore overestimates the total flux requirement over the scenario (inductive flux + vertical field flux)
The alternative approach consists in considering as flux target the one necessary to produce at the plasma center

## Slide 4: Methodologic considerations
One can see below the flux variation along radial dimension is not negligible
CS inner
CS outer
Plasma center
Example on features ranged in DEMO ones
285 Wb
171 Wb

## Slide 5: Methodologic considerations
We start from the reference CS geometry (from CREATE analysis) with reference current patterns for scenario
 | geometry |  |  |  | NI (A.T) |  | 
 | R [m] | Z [m] | DR [m] | DZ [m] | PREMAG | SOF | EOF
CS3U | 2.49 | 7.066 | 0.65 | 2.986 | 2.91E+07 | 1.36E+07 | -5.94E+06
CS2U | 2.49 | 4.08 | 0.65 | 2.986 | 2.91E+07 | -1.42E+06 | -2.91E+07
CS1 | 2.49 | -0.399 | 0.65 | 5.972 | 5.82E+07 | -9.60E+06 | -5.82E+07
CS2L | 2.49 | -4.878 | 0.65 | 2.986 | 2.91E+07 | -7.17E+06 | -2.91E+07
CS3L | 2.49 | -7.864 | 0.65 | 2.986 | 2.81E+07 | 2.51E+07 | -1.24E+07
PF1 | 5.4 | 9.66 | 1.15 | 1.15 | 1.65E+07 | 1.42E+07 | 2.32E+06
PF2 | 14 | 7.9 | 0.85 | 0.85 | 3.86E+06 | -5.22E+06 | -5.89E+06
PF3 | 17.97 | 2.5 | 1.1 | 1.1 | -8.47E+06 | -5.12E+06 | -6.08E+06
PF4 | 17.97 | -2.5 | 1.1 | 1.1 | 1.20E+07 | -3.98E+06 | -3.64E+06
PF5 | 14 | -7.9 | 1.2 | 1.2 | -9.91E+06 | -7.76E+06 | -8.98E+06
PF6 | 7 | -10.6 | 1.4 | 1.4 | 2.40E+07 | 1.55E+07 | 1.03E+07
Plasma | 9.54 | -0.01 | 0.1 | 0.1 | 0.00E+00 | 1.79E+07 | 1.79E+07
Calculation with CEA tool (BOBOZ) considering all coils (5 CS modules + PF)
DY (PREMAG – EOF) = 305 Wb
  new target Y
Flux is considered as provided only by the central module and the two adjacent modules (2/3 of CS) therfore giving a conservative approach to the method regarding flux.
In this hypothesis flux can be eavluated only at Premag (symmetry reasons)

## Slide 6: CS Design
At first loop we try to get the maximum flux
CEA tool used: MADMACS-CS (MAgnet Design MACroscopic Simulator for CS) + BOBOZ
DTMARG=1.5 K
TOP= 4.7 K
sHOOP=667 MPa
VMAX=10 kV
hCS = 18.2 m
strand = DEMO 2015
Insul = DEMO 2015
No PF currents
DEMO 2018 CS (MAX FLUX) | 
Conductor current (kA) | 98
# of SC strands | 2215
# of Cu strands | 0
THOTSPOT (K) | 233.5
Jacket thickness (mm) | 17.60
cable size (mm) | 43.68
# of turns | 11
# of pancakes (total in CS) | 214
# pck small / central module | 34 / 78
BMAX on conductor (T) | 15.67
Central module L (H) | 1.56
TDELAY / TDISCHARGE (s) | 3 / 7.7
YCS PLASMA (Wb) | 356.6
SC amount (t) | 386.4
Over-performance in YPLASMA
High SC amount
(high BMAX, low IC)
Slight copper excess

## Slide 7: CS Design
DTMARG=1.5 K
TOP= 4.7 K
sHOOP=667 MPa
VMAX=10 kV
hCS = 18.2 m
YPLASMA = 305 Wb
strand = DEMO 2015
Insul = DEMO 2015
No PF currents
DEMO 2018 CS (TARGET FLUX) | 
Conductor current (kA) | 98
# of SC strands | 520
# of Cu strands | 965
THOTSPOT (K) | 250.3
Jacket thickness (mm) | 15.52
cable size (mm) | 36.18
# of turns | 7
# of pancakes (total in CS) | 248
# pck small / central module | 40 / 88
BMAX on conductor (T) | 11.63
Central module L (H) | 1.18
TDELAY / TDISCHARGE (s) | 5.8
YCS PLASMA (Wb) | 303.9
SC amount (t) | 72.3
Slight under-performance in YPLASMA
Drastic SC amount decrease
  about 80 % drop in Nb3Sn amount
  Wb marginal cost is quite high
  about 6 tons Nb3Sn per Wb
  elements to check pros & cons aspects on economical ground
At second loop we try to get the target flux
 only by playing on the number of turns

## Slide 8: CS Design
At third loop we try to get the exact target flux
 playing on current
DTMARG=1.5 K
TOP= 4.7 K
sHOOP=667 MPa
VMAX=10 kV
hCS = 18.2 m
YPLASMA = 305 Wb
strand = DEMO 2015
Insul = DEMO 2015
No PF currents
DEMO 2018 CS (TARGET FLUX) | 
Conductor current (kA) | 100
# of SC strands | 542
# of Cu strands | 971
THOTSPOT (K) | 249.5
Jacket thickness (mm) | 15.80
cable size (mm) | 36.50
# of turns | 7
# of pancakes (total in CS) | 246
# pck small / central module | 40 / 86
BMAX on conductor (T) | 11.64
Central module L (H) | 1.13
TDELAY / TDISCHARGE (s) | 5.7
YCS PLASMA (Wb) | 305.8
SC amount (t) | 74.6
Current up to 100 kA
current increase rate (2%) and SC amount one (3%) higher than YPLASMA one (1%)
The design is somehow also optimistic as PF currents are ignored.

## Slide 9: CS Design
CS Design refinement for maximum flux
 PF currents are integrated (Premag = most critical time)
DEMO 2018 CS (MAX FLUX) | 
Conductor current (kA) | 98
# of SC strands | 2564
# of Cu strands | 0
THOTSPOT (K) | 157.1
Jacket thickness (mm) | 17.00
cable size (mm) | 46.84
# of turns | 11
# of pancakes (total in CS) | 208
# pck small / central module | 34 / 72 (- 4)
BMAX on conductor (T) | 15.94 (+ 0.2 T)
Central module L (H) | 1.63
TDELAY / TDISCHARGE (s) | 3 / 8.0
YCS PLASMA (Wb) | 338.8 (- 5%)
SC amount (t) | 433.7 (+12%)
SC increase by ~10% (as BMAX increase too)
Flux at plasma decreased but still higher than requirement
PF currents are kept unchanged from scenario but the CS currents are different.
  Item to be checked under plasma equilibrium point of view
DTMARG=1.5 K
TOP= 4.7 K
sHOOP=667 MPa
VMAX=10 kV
hCS = 18.2 m
strand = DEMO 2015
Insul = DEMO 2015
PF currents PREMAG

## Slide 10: CS Design
CS Design refinement for target flux
 PF currents are integrated (Premag = most critical time)
DEMO 2018 CS (TARGET FLUX) | 
Conductor current (kA) | 105
# of SC strands | 681
# of Cu strands | 935
THOTSPOT (K) | 249.1
Jacket thickness (mm) | 16.30
cable size (mm) | 37.64
# of turns | 7
# of pancakes (total in CS) | 236
# pck small / central module | 38 / 84
BMAX on conductor (T) | 12.29 (+0.7 T)
Central module L (H) | 1.05
TDELAY / TDISCHARGE (s) | 3 / 5.5
YCS PLASMA (Wb) | 305.4
SC amount (t) | 89.7 (+ 20%)
With Premag PF currents the SC amount increases by ~10 %.
  BMAX increased by 0.7 T
DTMARG=1.5 K
TOP= 4.7 K
sHOOP=667 MPa
VMAX=10 kV
hCS = 18.2 m
YCS = 305 Wb
strand = DEMO 2015
Insul = DEMO 2015
PF currents PREMAG

## Slide 11: Fatigue approach
Fatigue considerations: fatigue approach is the more realistic one > here attempted
The equivalent hoop stress representing fatigue should be taken at ~ 300 MPa (as for PF coils)
A minimum compliant stress value is searched
DEMO 2018 CS (fatigue) | 
Conductor current (kA) | 105
# of SC strands | 1665
# of Cu strands | 290
THOTSPOT (K) | 250.6
Jacket thickness (mm) | 22.00
cable size (mm) | 41.17
# of turns | 10
# of pancakes (total in CS) | 192
# pck small / central module | 32 / 64
BMAX on conductor (T) | 14.45
Central module L (H) | 1.11
TDELAY / TDISCHARGE (s) | 3 / 5.8
YCS PLASMA (Wb) | 305.0
SC amount (t) | 237.3
sJACKET (MPa) | 484.8
DTMARG=1.5 K
TOP= 4.7 K
VMAX=10 kV
hCS = 18.2 m
YCS = 305 Wb
strand = DEMO 2015
Insul = DEMO 2015
PF currents PREMAG
With 10 turns a minimum sJACKET is found at 484 MPa
  Fatigue model effective hoop is not reached
  Corresponding number of cycles to be checked

## Slide 12: Fatigue approach
Fatigue considerations (2):
Another try is attempted to see if decrease of stress is possible with 11 turns
DEMO 2018 CS (fatigue) | 
Conductor current (kA) | 104.5
# of SC strands | 2360
# of Cu strands | 0
THOTSPOT (K) | 186.6
Jacket thickness (mm) | 23.00
cable size (mm) | 45.02
# of turns | 11
# of pancakes (total in CS) | 184
# pck small / central module | 64
BMAX on conductor (T) | 15.10
Central module L (H) | 1.21
TDELAY / TDISCHARGE (s) | 6.3
YCS PLASMA (Wb) | 304.9
SC amount (t) | 344.9 (+ 45%)
sJACKET (MPa) | 457.4 (- 6%)
DTMARG=1.5 K
TOP= 4.7 K
VMAX=10 kV
hCS = 18.2 m
YCS = 305 Wb
strand = DEMO 2015
Insul = DEMO 2015
PF currents PREMAG
With 11 turns a minimum sJACKET is found at 457 MPa
  optimization on sJACKET can likely be further investigated
  NbTi amount increases drastically
  The marginal price per gained cycle (scaling stress/cycles to be evaluated) could be important
  It is very likely impossible to find a compliant design with stress close to 300 Mpa
  investigation on trade-off (e.g. cycles versus burn duration) to be conducted

## Slide 13: Breakdown study
Plasma Breakdown (BD) study
Simlarly as for DEMO 2015 the BD assessment was paramerically explored with Bint approach
DTMARG=TCS(Bint)-TOP(P,TBD)
Impact on TCS dynamic
~ 250 [nt,TBD] points were evaluated with THEA
BD features: 10% of the CS current variation between PREMAG & SOF is linearly dumped in TBD time
Equation analytically solved  Bint (t)
TIN=4.5 K
DI (CS)=11 kA
nt (ms)
TBD (s)
DTMARG (K)

## Slide 14: Breakdown study
Plasma Breakdown (BD) study
The parametric study was converted into iso-DTMARG levels curve
The BD safety domain is identified and the TBD dependance of nt is issued
A design adaptation can be envisaged according to the DTMARG expected during BD
Comparison can be done with other DEMO 2018 designs
  Target flux design
  Fatigue-optimized design

## Slide 15: Conclusions - perspectives
Conclusions
  CS design options were proposed with different hypotheses, along maximum or target flux approaches.
  Fatigue approach showed that 300 MPa was impossible to reach. Minimum values with compliant designs were found at ~ 450 MPa.
  Breakdown study showed a [TBD, nt ] domain where some parts could reach quench. More investigations should be led to understand the driving parameters.
Perspectives TS 2020
  Introduce a fatigue model to directly include cycling effects. Benchmarks with SPC would be led.
  Conduct updated breakdown study on other CS designs
NB: this proposal should be adjusted according to the volume of work (when identified) which is needed for addressing Gate Review documentation

## Slide 16: Thank you for your attention Questions ?