## Slide 1
MAG-2.1-T026-D002: CEA PF WP design
WPMAG Final Meeting, 12th Feb. 2020, Frascati
L. ZANI & CEA team

## Slide 2: Introduction
PF system
  Apply on DEMO 2015 configuration a PF design method consistent with the existing alternative design, for industrial study purpose
  Carry out parametric optimization study on PF coils aspect ratio.
  Converge on a general design method for PFs and provide material for common memo
  Apply the methodology to 2018 PF system design
Task content
out-of-date 2015 PF design  this scope was not applied on DEMO 2015 but on DEMO 2018
  Optimization study on aspect ratio
  Parametric study on jacket stress criterion

## Slide 3: Methodologic considerations
PF design method
No ITER analogies were considered (as for DEMO 2015) therefore the plasma scenario pattern was directly implemented
Design workflow
------- Design features ------
DTMARG = 1.5 K
TOP = 4.7 K
VMAX = 5.5 kV
sHOOP = 667 MPa
 static approach
Current lines positions unchanged
Convergence = both PF sizes vary < 1% across iteration
Double pancakes winding
max unit length < 1.5 km
Reference geometry + scenario
spiral volumic ratio constant
strand diameter = 0.73 mm
JC law = PFCI one
Beff considered

## Slide 4: PF design (static option)
First loop we try to keep aspect ratio as close as possible to reference ( = 1)
 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6
Maximum field (T) | 6.536 | 4.679 | 5.050 | 4.980 | 5.010 | 6.556
Operating current (kA) | 51.02 | 52.59 | 50.42 | 50.13 | 51.61 | 50.48
N SC strands | 4966 | 316 | 401 | 377 | 398 | 5344
N Cu strands | 0 | 665 | 960 | 1340 | 970 | 0
Spiral outer diameter (mm) | 12 | 11.5 | 13.6 | 15.43 | 13.7 | 15.8
Jacket thickness (mm) | 3.56 | 6.79 | 3.28 | 2.83 | 6.09 | 3.18
T hotspot (K) | 38 | 248 | 247 | 249 | 250 | 48
Number of pancakes | 18 | 14 | 28 | 40 | 24 | 28
Number of turns | 18 | 8 | 6 | 6 | 8 | 17
WP vertical dimension (m) | 1.223 | 0.624 | 1.186 | 1.815 | 1.154 | 1.958
WP radial dimension (m) | 1.189 | 0.343 | 0.244 | 0.262 | 0.371 | 1.157
Discharge time (s) | 15.9 | 9.0 | 24.1 | 44.5 | 23.2 | 44.0
L (H) | 1.710 | 0.940 | 2.624 | 4.885 | 2.475 | 4.789
Pancake hydraulic length (m) | 612.9 | 691.0 | 661.3 | 661.7 | 682.9 | 739.0
Total SC amount (t) | 192.0 | 10.7 | 26.0 | 35.0 | 22.9 | 387.5
  PF1 & PF6 with SC excess (high BMAX) and copper excess (low Thotspot)
  PF2 ~ 5 aspect ratio drastical change (constrain on unit length = 2 x hydraulic length)

## Slide 5: PF design (static option)
At constant PF1 area & current
  aspect ratio R/Z is decreased
 | PF1 | PF1 OPTIM | PF6 | PF6 OPTIM
Maximum field (T) | 6.536 | 6.362 | 6.556 | 6.117
Operating current (kA) | 51.02 | 51.66 | 50.48 | 50.06
N SC strands | 4966 | 2747 | 5344 | 1496
N Cu strands | 0 |  | 0 | 490
Spiral outer diameter (mm) | 12 |  | 15.8 | 
Jacket thickness (mm) | 3.56 | 4.62 | 3.18 | 4.50
T hotspot (K) | 38 | 62 | 48 | 250
Number of pancakes | 18 | 32 | 28 | 60
Number of turns | 18 | 10 | 17 | 8
WP vertical dimension (m) | 1.223 | 1.798 | 1.958 | 3.067
WP radial dimension (m) | 1.189 | 0.544 | 1.157 | 0.395
Discharge time (s) | 15.9 | 15.7 | 44.0 | 42.3
L (H) | 1.710 | 1.674 | 4.789 | 4.648
Pancake hydraulic length (m) | 612.9 | 339.1 | 739.0 | 350.6
Total SC amount (t) | 192.0 | 104.5 | 387.5 | 110.3
  SC amount decreased by a factor of ~2 and ~4 respectively for PF1 and PF6
  Aspect ratio R/Z is close to 0.3
At second loop we try to optimize the SC amount by changing the aspect ratio

## Slide 6: PF design (static option)
Integration compliance was checked
PF reference
PF design
PF optimized
TF external contour
PF1 Low space for clamps
PF6 clash with TF
PF4 Possible clash with port
  Issues to be discussed to establish a PF reference design for studies (mechanical / feasibility)
  Discussions with plasma equlibrium experts sugdested
- PF1 & PF6 (+PF4) should be moved
 consequence on plasma equilibrium ?
- PF1 & and PF6 further optimization can be considered (switch to Nb3Sn / subcool)
 cost impact ?
- Positive point: PF2~5 can be moved closer to plasma
 enhanced plasma control ?

## Slide 7: PF design (fatigue option)
Fatigue approach: from SPC studies > fatigue is a limiting factor, therefore an exploration was conducted in this direction.
 | PF1 | PF2 | PF3 | PF4 | PF5 | PF6
Maximum field (T) | 6.137 | 3.720 | 4.600 | 4.463 | 3.793 | 5.388
Operating current (kA) | 51.66 | 52.59 | 50.42 | 50.13 | 51.61 | 50.06
N SC strands | 1657 | 188 | 296 | 270 | 191 | 561
N Cu strands | 0 | 730 | 1015 | 1385 | 1070 | 1140
Spiral outer diameter (mm) | 12 | 11.5 | 13.6 | 15.43 | 10 | 15.8
Jacket thickness (mm) | 11.10 | 14.10 | 5.70 | 6.30 | 13.60 | 9.20
T hotspot (K) | 166 | 247 | 250 | 250 | 252 | 248
Number of pancakes | 32 | 14 | 28 | 40 | 24 | 60
Number of turns | 10 | 8 | 6 | 6 | 8 | 8
WP vertical dimension (m) | 1.930 | 0.819 | 1.307 | 2.070 | 1.461 | 3.486
WP radial dimension (m) | 0.585 | 0.454 | 0.270 | 0.301 | 0.473 | 0.451
Discharge time (s) | 15.3 | 8.4 | 23.5 | 43.0 | 21.7 | 40.0
L (H) | 1.630 | 0.880 | 2.560 | 4.722 | 2.308 | 4.398
Pancake hydraulic length (m) | 340.4 | 693.8 | 661.8 | 662.4 | 685.4 | 352.0
Total SC amount (t) | 63.3 | 6.4 | 19.2 | 25.1 | 11.0 | 41.5
The change in the design method was the stress criterion that was chosen to a value close to the hoop stress found in the SPC report (EFDA_D_2MVZQV)  a 300 MPa upper limit value was chosen for sjacket
  decrease in BMAX
  (from WP size increase)
  decrease in NbTi amount
  (from BMAX decrease)
  increase in SS jacket amount
  (from s criterion decrease)
  increase in PF height
  worsen clash issues

## Slide 8: Comparative considerations
Comparisons: the impact of stress criterion change was quantified
 | NbTi amount (t) |  |  | 
Coil | Static design | Fatigue design | diff (%) | diff (t)
PF1 | 104.47 | 63.26 | -39.4% | -41.21
PF2 | 10.71 | 6.4 | -40.2% | -4.31
PF3 | 26.02 | 19.22 | -26.1% | -6.8
PF4 | 34.97 | 25.07 | -28.3% | -9.9
PF5 | 22.86 | 11.01 | -51.8% | -11.85
PF6 | 110.28 | 41.52 | -62.4% | -68.76
TOTAL | 309.31 | 166.48 | -46.2% | -142.83
  About 143 tons of NbTi less needed - at NbTi market price decrease is worth ~ 20 M€
 | Steel amount (t) |  |  | 
Coil | Static design | Fatigue design | diff (%) | diff (t)
PF1 | 75.5 | 172.8 | 129% | 97.3
PF2 | 70.0 | 174.6 | 149% | 104.6
PF3 | 67.2 | 123.3 | 84% | 56.1
PF4 | 91.1 | 218.7 | 140% | 127.5
PF5 | 119.7 | 305.9 | 156% | 186.2
PF6 | 128.1 | 275.8 | 115% | 147.6
TOTAL | 551.6 | 1271.1 | 130% | + 719.4
  About 720 tons of extra jacket steel needed
  Market price not evaluated / should be investigated to check overall impact
  The fatigue approach considerably impacts material inventory, among other items (cable dimensions…)
  A more detailed cost study could give indications on the resulting cost impact…possibly positive…

## Slide 9: Considerations on PF positions
PF repositioning
It was supposed that in reference configuration distances PF-TF were assessed (CAD checks)
PF were relocated to make their position allow compliance.
A factor of merit was checked: the distance to plasma center (supposingly relevant to plasma control capacities: the closer the better)
PF1
PF2
PF3
PF4
PF5
PF6
Plasma center
Reference geometry
PF initial
PF re-positioned
Distance to TF
Distance to plasma

## Slide 10: Spatial positions considerations
 | distance to TF (m) |  | 
Coil | PF CEA | Reference | difference
PF1 | 0.052 | 0.334 | -0.282
PF2 | 0.600 | 0.472 | 0.128
PF3 | 0.632 | 0.250 | 0.382
PF4 | 0.538 | 0.254 | 0.284
PF5 | 0.449 | 0.336 | 0.113
PF6 | -0.673 | 0.281 | -0.953
Metrology: - The differences between PFs locations is numbered and the shift needed to position their closest corner similarly as in reference geometry was evaluated
- The only PF « fatigue approach » configuration was carried out
  PF1 & PF6 are short of ~ 0.3 m & ~1 m to be correctly attached to TF
 | distance to plasma center (m) |  | 
Coil | PF CEA | reference | difference
PF1 | 10.772 | 10.510 | + 0.262
PF2 | 8.962 | 9.072 | -0.110
PF3 | 8.427 | 8.793 | -0.366
PF4 | 8.563 | 8.793 | -0.230
PF5 | 9.016 | 9.072 | -0.056
PF6 | 11.837 | 10.900 | 0.937
  PF1 & PF6 would be shifted away from plasma of ~0.3 m and ~1 m (~3% and ~10% increase)
  PF2 to PF5 would get closer to plasma of between ~0.1 m and ~0.4 m (between 1% and 4% decrease)
  Non negligible shifts required to recover PF correct postitionning (~0.1 m to ~1 m)
  Exchanges with plasma experts would give an idea of the possible impacts on the plasma control capacity

## Slide 11: Conclusions - perspectives
Conclusions
  The direct processing of reference scenario data was applied to addres the DEMO 2018 PF design definition.
  Aspect ratio were optimized to gain NbTi amount especially on PF1 and PF6.
  Fatigue consideration were included with lower stress limit and, beyong stell increase resulted in NbTi amount reduction
  At constant current lines, clashes with TF were identified with PF1 & PF6 and possibly PF3 & PF4 with ports. The shift to recover proper positions was evaluated to increase distance to plasma for PF1 & PF6 and reduce it for other PFs.
Perspectives TS 2020
  Introduce a fatigue model to directly include cycling effects. Benchmarks with SPC would be led.
  Adjust design with this updated model
  Compare the macroscopic model with FEA outcomes if available
NB: this proposal should be adjusted according to the volume of work (when identified) which is needed for addressing Gate Review documentation

## Slide 12: Thank you for your attention Questions ?