## Slide 1: 3D mechanical analysis of TF WP#2 ENEA-UNITUS
F. Giorgetti, G. Calabrò, P. Fanelli,
G. Tomassetti, V. Corato, L. Muzzi
WPMAG Final Meeting 11-13 February 2020

## Slide 2: Outline
Geometry
Homogenization
3D EM analsyis
3D Mechanical analysis
Conclusions
2020 TS

## Slide 3: Geometry
The WP#2 layer-wound configuration is composed of 6 graded Double Layers (DL) [1].
Baseline vs WP#2 configurations:
  Reduced radial space (from 820 mm to 607 mm), maintaining the same 12 T maximum field.
  Same inner TF coil (plasma facing) radius (i.e. 4323 mm).
  Same 520 mm casing nose thickness.
[1] L. Muzzi et al., ENEA TF Winding Pack Design and Analysis (2NGZ2G_v1_1)

## Slide 4: Geometry
The geometry domains of the TF coils and the WP as well were properly divided in sub-regions in order to obtain a mapped mesh in almost all TF parts.
Gravity support and Outer Inter Coil Structures not included in the simulations
ENEA CONFIGURATION
BASELINE
CONFIGURATION

## Slide 5: Homogenization
DLs equivalent orthotropic properties obtained with the procedure exposed in [2].
[2] M.E. Biancolini et al., Mechanical analysis of PF4 and TF systems (2MZKNX_v1_0)
DL6
DL1
Steel Jacket thickness = 10.4 mm
Aspect Ratio 1.35
Layers 17+15
Steel Jacket thickness 4.6 mm
Aspect Ratio 1.76
Layers 17+17
DL6
DL1

## Slide 6: Homogenization
Homogenization results.
  Young and shear moduli increase from DL1 to DL6 (increasing amount of steel passing from DL1 to DL6).
  Higher values obtained at 4.2K, due to stiffer behviour of steel at lower temperatures.

## Slide 7: 3D EM Analysis
The EM analysis is based on reference scenario of 8th of July [3].
Total current flowing in the 202 TF conductors is 14.8MAt
  Coils treated as a homogeneous media
EM analysis performed with ANSYS Maxwell
[3] Reference Equilibrium for 2018 WPMAG DEMO Single Null (8th July 2019)

## Slide 8: 3D EM Analysis
EM calculation results
  @Energization
  @EoF
|B| = 12 T
|B| = 12 T
B field contour @Equatorial plane
Energization
EoF

## Slide 9: 3D EM Analysis
EM forces vs. TF curvilinear abscissa
  @Energization (no out of plane forces)
  @EoF
TF - EM force densities @Equatorial plane

## Slide 10: 3D Mechanical Analysis
Analysis performed inside ANSYS Workbench environment.
The EM loads are interpolated inside ANSYS Maxwell on the structural mesh nodes (68904 points).
Material properties are extracted from [4]
[4] F. Nunio et al., Reference basis for mechanical & thermal analysis of TFC (EFDA_D_2MC8T4)

## Slide 11: 3D Mechanical Analysis
Mesh stats
  Number of elements: 356k
  Number of nodes: 393k
Boundary conditions
  Cyclic symmetry (16 sectors) applied through CEs
  Friction (μ=0.2) between casing and WP
  Casing-wedge insulation (left -12.5°): friction (μ=0.2)
  Casing-wedge insulation (right +12.5°): bonded [1]
  Vertical support
  Load steps:
    Cooling Down
    EM loads (@Energization)
    EM loads (@EoF)
[1] L. Muzzi et al., ENEA TF Winding Pack Design and Analysis (2NGZ2G_v1_1)

## Slide 12: 3D Mechanical Analysis
Casing results: deformation
  Maximum Casing deformation is 0.223 m @EoF instat of scenario (almost double with respet to @Energization)
 | CD+EM loads @Energization | CD+EM Loads @EoF
Total Deformation [m] | 0.115 | 0.223
CD+EM loads @Energization
CD+EM loads @EoF
0.05 m
0.21 m

## Slide 13: 3D Mechanical Analysis
Casing results: Stress (SINT)
  The critical locations are in the upper and lower curved portion of the casing above and below the inner straight leg.
  Another critical location is in the outer leg near the equatorial plane.
  The presence of OIS could be helpful to mitigate the stresses and to reduce the structure deformation.

## Slide 14: 3D Mechanical Analysis
Smeared WP results: deformations and Stresses
  Maximum WP deformation is 0.21 m @EoF instant of scenario (almost double with respet to @Energization)
  In the inner leg straight portion an almost constant compression of 103 MPa is observed
  Another critical location can be found in the lower part, but is influenced by roughly representation of the GS
  In the vertical direction a critical location could be found in the upper portion of straight leg
 | CD+EM loads @Energization | CD+EM Loads @EoF
Total Deformation [m] | 0.108 | 0.211

## Slide 15: Conlusions and future work
The TFC WP#2 configuration of 2018 DEMO has been analyzed.
Homogenization procedure allowed to extrapolate for each DL the equivalent elastic properties.
Both EM and structural analyses have been performed within ANSYS Workbech.
EM loads evaluated @Energization and @EoF instants of scenario.
Critical location were highlighted on steel casing and on smeared WP.
The availability of geometrical entities (i.e. gravity support, OIS) could be helpful to mitigate the stress state and to reduce the total deformations.

## Slide 16: 2020 TS
3D Mechanical and electro-magnetic analysis of the optimized solution proposed by Giordano Tomassetti [5].
The analysis presented will be repeated considering the optimized WP#2 layout. The effects of the increased EM field peak (from 12T to 12.5T) will be evaluated highlighting the differences with the baseline solution.
Work to be addressed:
  Geometry, considering the increased WP radial dimension
  Homogenization, because of the variation of the steel jacket thicknesses
  EM analysis, to reach the required 12.5T peak field
  Structural analysis, with the same BCs but the updated EM forces
GS and OIS will be considered (if available) to make a more reliable comparison.
[5] G. Tomassetti et al., 2D optimization to maximize the magnetic field (2P8X5E)

## Slide 17: 3D mechanical analysis of TF WP#2 ENEA-UNITUS
F. Giorgetti, G. Calabrò, P. Fanelli,
G. Tomassetti, V. Corato, L. Muzzi
WPMAG Final Meeting 11-13 February 2020